## Slide 1: An Overview of SPICE
October 2007

## Slide 2: Space Science Data: Two Kinds
SPICE deals with these data to support the planning for and analysis of these data
Science
Instrument
Data
Ancillary
Data
Notes: 2

## Slide 3
What are “Ancillary Data?”
Spacecraft
Planet
Earth
Sun
Solar System Barycenter
Time Conversion
Calculations
Logs of Commands
and Events
Other
Instrument
reference frame
Antenna
reference
frame
EME 2000
reference frame
(J2000)
Reference frames
and size/shape
of planet
and size/shape
of Earth
Sizes/shapes
Orientation
of spacecraft
Orientations
Orientation
Orientation
Relative positions
of spacecraft and
solar system bodies
Positions
Pointing of
Instrument
field-of-view
Pointing

## Slide 4: What are “Ancillary Data”?
“Ancillary data” are those that help scientists and engineers determine:
  where the spacecraft was located
  how the spacecraft and its instruments were oriented (pointed)
  what was the location, size, shape and orientation of the target being observed
  what events were occurring on the spacecraft or ground that might affect interpretation of science observations
In the above we’ve used past tense, but doing the same functions for future times is equally applicable
Notes: 3

## Slide 5: From Where do Ancillary Data Come?
Some come from the spacecraft
Some come from the mission control center
Some come from the spacecraft and instrument builders
Some come from scientists
SPICE is used to organize and package these data in useful, stable packages–what we call “kernels.”
The kernels are made available to scientists and engineers, along with NAIF Toolkit software, to help in the planning and analysis of science observations.

## Slide 6: Why SPICE?
Knowing observation geometry and events is an important element:
  in the design of space missions,
  in the selection of observations,
  and in analysis of the science data returned from the instruments.
Having proven, extensive and reusable means for producing and using ancillary data reduces cost and risk, and can help scientists and engineers achieve more substantive, accurate and timely results.

## Slide 7: SPICE System Components
The principal SPICE system components are:
  Data files, often called “kernels” or “kernel files”
  Software, known as the SPICE Toolkit, consisting of:
    a subroutine library
    a number of programs (executables)
      Some are “meaty” applications
      Some are “simple” utilities focused on kernel management
    a few “cookbook” programs
      Simple examples of using SPICE toolkit subroutines
  Documentation
      User Guides for programs
      Substantial source code documentation for all subroutines
        Provided explicitly for those who will use Toolkit subroutines to make their own application programs
      Technical reference documents for major families of subroutines
      A permuted index
  Tutorials
  Programming lessons built around SPICE
    Include tips, data, and NAIF’s solution code and numeric results
Notes: 5

## Slide 8: Genesis of the SPICE Acronym*
S
P
I
C
E
Spacecraft
Planet
Instrument
C-matrix
Events
* Coined by Dr. Hugh Kieffer, USGS Astrogeology Branch, Flagstaff AZ
Notes: 6

## Slide 9: Logical versus Physical View
Logical View
Physical View
Spacecraft
Planet
Instrument
Camera-matrix
Events
S
P
I
C
E
Software
SPICE Toolkit
SPK
PcK
IK
CK
EK
ESP ESQ
S
FK
LSK
SCLK
Space vehicle or target
body trajectory (ephemeris)
Target body size,
shape and orientation
Instrument field-of-view size,
shape and orientation
Orientation of space vehicle or
any articulating structure on it
Events information:
- Science Plan (ESP)
- Sequence of events (ESQ)
- Experimenter’s Notebook (ENB)
Reference frame specifications
Leapseconds tabulation
Spacecraft clock coefficients
API libraries, some application and utility programs, software documentation
Others
Content
Notes: 7

## Slide 10: SPICE System Contents - 1
SPK
PcK
IK
Space vehicle ephemeris (trajectory)
Planet, satellite, comet and asteroid ephemerides
More generally, position of something relative to something else
Planet, satellite, comet and asteroid orientations, sizes, shapes
Possibly other similar “constants” such as parameters for gravitational model, atmospheric model or rings model
Instrument information such as:
  Field-of-view size, shape, orientation
  Internal timing
Notes: 8

## Slide 11: SPICE System Contents - 2
CK
EK
Instrument platform (e.g. spacecraft) attitude
More generally, orientation of something relative to a specified reference frame
“Events,” broken into three components:
  ESP: Science observation plans
  ESQ: Spacecraft & instrument commands
  ENB: Experiment “notebooks” and ground data system logs
3 components
The Events kernel idea has not taken hold. After Cassini it will probably disappear.
Notes: 9

## Slide 12: SPICE System Contents - 3
Frames
  Definitions of and specification of relationships between reference frames (coordinate systems)
    Both “fixed” and “dynamic” frames are available
Other
Kernels
FK
LSK
SCLK
Leapseconds Tabulation
- Used for UTC <--> ET time conversions
Spacecraft Clock Coefficients
  - Used for SCLK <--> ET time conversions
Shape models (DEM and tessellated plates) (DSK) *
Star (sky) catalog (??K) *
UTC = Universal Time Coordinated ET = Ephemeris Time SCLK = Spacecraft Clock Time
* under development
Notes: 10

## Slide 13: SPICE System Contents - 4
SPICE
Toolkit
Library of modules used to:
  write binary SPICE kernel files
  read all (binary and text) SPICE kernel files
  compute quantities derived from SPICE kernel data
Example (“cookbook”) programs
Utility programs
  Kernel summarization or characterization
  Kernel porting
Application programs (a few)
  e.g. “chronos” time conversion application
Kernel production programs (a few)
  e.g. “mkspk” SPK production program
FORTRAN
C
IDL
MATLAB
Notes: 11

## Slide 14: Using SPICE in Science Planning
SPK
PcK
IK
CK
FK
SCLK
LSK
EK
User’s Own Modules
User’s Planning Program
“Tour” evaluation
or
Instrument pointing plan
  or
Observation geometry visualization
  or
Analysis of expected communications link performance
Select kernel types and specific kernels as needed
Selected
SPICE Toolkit
Library
Modules
Other
needed
data

## Slide 15: Using SPICE in Science Data Analysis
SPK
PcK
IK
CK
FK
SCLK
LSK
EK
User’s Own Modules
Derived
Observation
Geometry
Instrument
Calibration
Data
Instrument
Data
User’s
Science
Data
Analysis
Program
Spectacular
Science
Results
User’s Geometry Program
Selected
SPICE Toolkit
Library
Modules
Select kernel types and specific kernels as needed

## Slide 16: SPICE System Characteristics - 1
Portable SPICE kernel files
Portable NAIF Toolkit software
Focus is on the customer
Code is well tested before being released to users
Once released, code functionality is never changed or removed
  Except NAIF does reserve the right to fix bugs
Extensive user-oriented documentation is provided
  Includes highly documented source code
An extensive set of SPICE tutorials is available
“Open book” programming lessons are offered as a part of each NAIF-provided training class
Notes: 17

## Slide 17: SPICE System Characteristics - 2
All numeric computations use double precision
System includes built-in exception handling
  Catches most invalid inputs
  Offers a traceback and configurable action upon detection of a problem
Gives you access to most of JPL’s integrated ephemerides for spacecraft and natural bodies (planets, satellites, comets, asteroids)
Kernel files are separable
  Use only those you need for a particular application
Kernel files are extensible
  New data “types” can be added within a family
  New kinds of kernels can be developed
Notes: 18

## Slide 18: SPICE System Characteristics - 3
Broad applicability, means good value
  Multimission and multidiscipline
    Use it over and over again, no matter which NASA mission you’re working on
  The growing use of SPICE outside of the U.S. is helping extend the multimission applicability
Notes: 18

## Slide 19: SPICE System Characteristics - 4
The SPICE Toolkit is free to individual users
  Core SPICE system development is funded by NASA's Solar System Exploration Office
  NASA flight projects fund NAIF and/or others to adapt and deploy SPICE in support of NASA’s planetary missions and some cooperative missions
Distribution of SPICE software is not restricted under U.S. Government regulations
    SPICE is classified TSPA (“Technology and Software Publicly Available”)
    No ITAR restrictions on data, training or consulting
Commercial use of SPICE software is encouraged
  No license fees or other restrictions

## Slide 20: Supported Platforms
The SPICE Toolkit has been ported to a wide variety of popular “environments”
  Each environment is characterized by
    Hardware type (platform)
    Operating System
    Compiler
    Sometimes even selected compilation options
NAIF provides separate, ready-built SPICE Toolkit packages for each supported environment
  If you need to port the Toolkit to a new environment yourself, consult with NAIF staff

## Slide 21: For What Jobs is SPICE Used ?
Mission planning, modeling and visualization
Pre-flight mission evaluation from a science perspective
Detailed science observation planning
Mission operations engineering functions
Science data analysis, including correlation of results between instruments, and with data obtained from other missions
Data archiving, for future use by others
Education and Public outreach
Increasing
mission
maturity
(time)
The original focus
of SPICE
Notes: 13

## Slide 22: Examples - 1 What Can You Do With SPICE ?
Mission Design
  Compute interesting orbit properties; compare these with those of another design, or with another mission
  Evaluate possibilities for relay link times and duration
Mission Operations
  Predict or evaluate telecommunications link performance
  Analyze spacecraft orientation history
  Determine elevation and rise/set times of sun and tracking stations
  Compute location and lighting conditions for a rover

## Slide 23: Examples - 2 What Can You Do With SPICE ?
Science
  Design specific observations to be acquired
  Compute observation geometry needed for science data product labels, to later be used in searching a catalog for science data of interest
  Compute observation geometry needed to analyze some data or to correlate multiple data sets
    Examples of “observation geometry”:
      Lighting angles (phase, incidence, emission)
      Location (LAT/LON) of instrument footprint
      Range and local time
      Local season
Visualization, Education and Public Outreach
  Provide geometry used to drive web pages giving interesting parameters such as ranges, velocities, time of day on Mars
  Provide geometry for animations showing orbiter location and orientation, instrument footprint projected on the surface, and locations of surface assets or natural features of interest

## Slide 24: What “Vehicle” Types Can Be Supported ?
Cruise/Flyby
  Remote sensing
  In-situ measurement
  Instrument calibration
Orbiters
  Remote sensing
  In-situ measurement
  Communications relay
Balloons*
  Remote sensing
  In-situ measurements
Landers
  Remote sensing
  In-situ measurements
  Rover or balloon relay
Rovers
  Remote sensing
  In-situ sensing
  Local terrain characterization
Terrestrial applications
  Ephemerides for observers
* Not yet demonstrated

## Slide 25: Global SPICE Geometry
UTC to ET mapping
(“generic” LSK file)
ET to orbiter on-board clock mapping
(”orbiter” SCLK file)
Orbiter position relative to the center of Mars
(“orbiter” SPK file)
Orbiter frame orientation relative to J2000 frame
(“orbiter” CK file)
Earth position relative to Solar System barycenter (“planet ephemeris” SPK file)
Rover frame orientation relative to local level frame
(“rover” CK file)
Rover position relative to the landing site (lander)
(“rover” SPK file)
Local level frame orientation relative to planet body-fixed frame
(“mission” FK file)
Landing site (lander) position relative to the Mars center (“landing site” SPK file)
Mars position relative to the Solar System barycenter (“planet ephemeris” SPK file)
Planet body-fixed frame orientation relative to J2000 frame
(“generic” PCK file)
Ephemeris
Time (ET)
Universal Time
Coordinated (UTC)
Orbiter on-board
clock (SCLK)
XM
YM
ZM
XL
YL
ZL
XR
YR
ZR
XJ2000
YJ2000
ZJ2000
XO
YO
ZO
XE
YE
ZE
Position Vectors
Frame Orientations
Time conversions
Time conversions

## Slide 26: Orbiter Geometry
Solar array gimbal position relative to spacecraft center
(“structures” SPK file)
Camera frame orientation relative to spacecraft frame
(“mission” FK file)
Spacecraft frame orientation relative to inertial frame
(“spacecraft” CK file)
Spacecraft position relative to planet center
(“spacecraft” SPK file)
High gain antenna gimbal position relative to spacecraft
(“structures” SPK file)
Solar array gimbal frame orientation relative to spacecraft frame
(“solar array” CK file)
Magnetometer position relative to solar array gimbal
(“structures” SPK file)
Magnetometer frame orientation relative to solar array gimbal frame
(“mission” FK file)
High gain antenna gimbal frame orientation relative to spacecraft frame
(“antenna” CK file)
High gain antenna phase center location relative to high gain antenna gimbal
(“structures” SPK file)
High gain antenna frame orientation relative to high gain antenna gimbal frame
(“mission” FK file)
XM
YM
ZM
ZC
XC
YC
ZA
XA
YA
ZAG
XAG
YAG
ZSG
YSG
XSG
ZSC
YSC
XSC
Position Vectors
Frame Orientations

## Slide 27: Lander Geometry
Robotic arm gimbal frames orientations relative to each other (“arm” CK file)
Robotic arm camera frame orientation relative to last gimbal frame
(“mission” FK file)
Robotic arm gimbal and camera relative positions
(“structures” SPK file)
Lander frame orientation relative to local level frame (“lander” CK file)
Descent camera frame orientation relative to lander frame
(“mission” FK file)
Descent camera position relative to lander
(“structures” SPK file)
Mast camera head frame orientation relative to lander frame
(“mast camera” CK file)
Left and right mast camera frame orientations relative to camera head frame
(“mission” FK file)
Left and right mast camera positions relative to camera head
(“structures” SPK file)
Meteo sensor positions relative to lander (“structures” SPK file)
Lander position relative to landing site
(“lander” SPK file)
Local level frame orientation relative to planet body-fixed frame
(“mission” FK file)
Mast camera head position relative to lander
(“structures” SPK file)
Landing site position relative to planet center
(“landing site” SPK file)
XLL
YLL
ZLL
XDC
YDC
ZDC
XL
YL
ZL
ZRC
YRC
XRC
ZRC
XLC
ZCH
YLC
XCH
YCH
YRC
Position Vectors
Frame Orientations

## Slide 28: Rover Geometry
YL
ZL(GRAVITY)
XL(NORTH)
XR
YR
ZR
ZT
XT
YT
ZE
YE
XE
YRC
ZRC
XRC
YLC
XLC
ZLC
ZS
XS
YS
Frame Orientations
Position Vectors
Left and right mast camera center positions relative to end of mast
(“structures” SPK file)
End of mast position relative to elbow gimbal
(“structures” SPK file)
Mast elbow gimbal position relative to shoulder gimbal
(“structures” SPK file)
Mast shoulder gimbal position relative to torso gimbal
(“structures” SPK file)
Mast torso gimbal position relative to rover
(“structures” SPK file)
Rover position relative to landing site (“rover” SPK file)
Landing site position relative to planet center
(“landing site” SPK file)
Left and right mast camera frames orientation relative to mast elbow frame
(“mission” FK file)
Mast elbow frame orientation relative to mast shoulder frame (“mast” CK file)
Mast shoulder frame orientation relative to mast torso frame
(“mast” CK file)
Mast torso frame orientation relative to rover frame (“mast” CK file)
Rover frame orientation relative to local level frame (“rover” CK file)
Local level frame orientation relative to planet body-fixed rotating frame
(“mission” FK file)

## Slide 29: Major SPICE Users
[P] = partial use of SPICE [S] = special tools or services provided by NAIF
Notes: 19

## Slide 30: Building Blocks for Your Applications
NAIF offers the “SPICE” ancillary information system as a set of blocks for building tools that can help execute a multimission, international space exploration program
SPICE: the ancillary information system that NAIF builds and often operates.
NAIF: the JPL entity responsible for development and deployment of SPICE.
NAIF Node of the PDS: one responsibility of the NAIF Group--archiving and providing long-term access to SPICE data for the worldwide science community.