## Slide 1: Introduction to Kernels
October 2007

## Slide 2: What is a SPICE “Kernel”
Kernel = File
Kernel = File containing ancillary data
Kernel = a file containing low level ancillary data that may be used, along with other data and SPICE software, to determine higher level geometry parameters of use to scientists and engineers in planning and carrying out space missions.

## Slide 3: SPICE Kernels Family
SPK
  Spacecraft and Planet Ephemeris
PcK
  Planetary Constants, for natural bodies
    Orientation
    Size and shape
IK
  Instrument
CK
  Pointing (“C-matrix”)
EK
  Events, up to three distinct components
    ESP: science plan
    ESQ: sequence
    ENB: experimenter’s notebook
FK
  Reference frame specifications
SCLK
  Spacecraft clock correlation data
LSK
  Leapseconds
Meta-Kernel (a.k.a. “FURNSH kernel”)
  Mechanism for aggregating and easily loading a collection of kernel files
DSK (under development)
  Digital shape kernel
    Tesselated plate model
    Digital elevation model

## Slide 4
Text and Binary Kernels
SPICE text kernels are:
  text PCK (the most common type of PCK)
  IK
  FK
  LSK
  SCLK
  MK (“Furnsh” meta-kernel)
SPICE binary kernels are:
  SPK
  binary PCK (exists only for Earth and moon)
  CK
  ESQ (part of the E-kernel)
  DBK (database kernel)
  DSK (digital shape kernel)*
* New kind of kernel under development

## Slide 5: SPICE Kernel Forms
Binary form: SPK, binary PCK, CK, EK/ESQ1, DSK
  Binary kernels are not human-readable and require the use of Toolkit software to examine the data contents.
Text form: text PcK, IK, FK, LSK, SCLK, FURNSH (MK)
  Text kernels contain only printing characters (ASCII values 32-126), i.e. human-readable text.
    The TAB character (ASCII value 9) is not allowed.
“Transfer” form of a binary kernel
  This is an ASCII representation of a binary kernel
  Was used for porting the file between computers with incompatible binary representations (e.g. PC and UNIX)
  Use of the transfer kernel is no longer needed for porting
    But is one way to convert a non-native binary kernel into native format, needed for modifying the kernel or improving read efficiency
[1] The ESP and ENB components of the EK might be binary, text, or html, depending on specific implementation.

## Slide 6: Example Text Kernel
This is a sample SPICE text kernel. The \begindata and \begintext markers on lines by themselves set off the start of data and text blocks respectively.
KPL/<kernel type>
\begindata
  NAME = 'Sample text value'
  NaMe = 'Keywords are case sensitive'
  NUMBERS = ( 10.123, +151.241, -1D14 )
  NUMBERS += ( 1.0, 1, -10 )
  NUMBERS += ( 1.542E-12, 1.123125412 )
  NAIF_BODY_NAME += ( ‘SPEEDO’, ‘NEETO’ )
  NAIF_BODY_CODE += ( -678, -679 )
  TIME = @1972-JAN-1
  \begintext
  < some comments about the data >
  \begindata
  < more data, given again in keyword = value syntax >
  \begintext
  < etc., etc. >
  The above assignments demonstrate that text kernels can contain characters, times, and numeric values. For more detailed information see Kernel Required Reading.

## Slide 7: Text Kernel Operators
The “+=“ operator adds additional values to an existing variable. It creates a new variable if the referenced variable doesn’t already exist.
The “@” symbol preceding a calendar date identifies a date string. The string must not contain embedded blanks. The string will be parsed and converted to an internal double precision representation of that epoch. The date is interpreted as ephemeris time (ET).
  This conversion does not need a leapseconds kernel.

## Slide 8: Example Binary Kernel
A binary kernel contains lots of non-printing (unintelligible) data, usually interspersed with occasional occurrences of ASCII characters.
Other than moving binary kernels around on your computer, or between computers, the only way to use a binary kernel is to read it or add to it using a SPICE subroutine or program.

## Slide 9: Metadata In SPICE Kernels
All SPICE kernels can and should contain metadata–descriptive information about the basic kernel data.
Metadata might convey:
  when, where, how and by whom the file was made
  for what purpose the file was made
  what source data were used to make the file
  key characteristics of the file, such as:
    start and stop times
    information about data gaps
    notes on expected data accuracy
  cautions on use of the file
  whatever else the file creator thinks could be useful to consumers of the data product

## Slide 10: Examples of Metadata
MISSION_NAME = "MARS GLOBAL SURVEYOR"
SPACECRAFT_NAME = "MARS GLOBAL SURVEYOR"
DATA_SET_ID = "MGS-M-SPICE-6-V1.0"
KERNEL_TYPE_ID = SPK
PRODUCT_ID = "MGS_MAP1.BSP"
PRODUCT_CREATION_TIME = 2000-01-14T08:26:18
PRODUCER_ID = "MSOPNAV/JPL"
MISSION_PHASE_NAME = MAPPING
PRODUCT_VERSION_TYPE = ACTUAL
PLATFORM_OR_MOUNTING_NAME = "N/A"
START_TIME = 1999-03-09T00:58:56
STOP_TIME = 1999-06-02T00:58:56
etc.
Metadata* in
“comment area”
Data
SPICE Binary Kernel
Example of metadata as a PDS label
Metadata and
comments at
top of file
SPICE Text Kernel
\begindata
first data area
\begintext
more comments
\begindata
more data
etc.
etc.
Example of metadata as free-form text
Mars Global Surveyor Mapping SPK file, MGSNAV Solution
======================================================
Created by Boris Semenov, NAIF/JPL, June 14, 1999
Objects in the Ephemeris
--------------------------------------------------------
This file contains ephemeris data for the Mars Global Surveyor (MGS)
spacecraft. NAIF ID code for MGS is -94.
Approximate Time Coverage
--------------------------------------------------------
This file covers first three 28-day mapping cycles of the Mapping phase of the mission (mapping orbits 1 through 1040):
COVERAGE BEGIN TIME (TDB): 1999 MAR 09 01:00:00.000
COVERAGE END TIME (TDB): 1999 JUN 02 01:00:00.000
etc.
*Metadata in the comment area
of a binary kernel can be accessed
only using SPICE software.

## Slide 11: Loading Kernels - 1
To make kernels available to SPICE programs you “load” them.
When you load a text kernel:
  the file is opened
  the kernel contents are read into memory
    variable names and associated values are stored in a data structure called the “kernel pool”
  the file is closed
When you load a binary kernel:
  the file is opened
  for SPK, CK, and binary PCK files, no data are read until a read request is made by Toolkit software
  for ESQ files, the schema description is read, checked, and stored in memory at load time, but no data are read until a query/fetch is made
  for all practical purposes the binary file remains open unless specifically unloaded by you

## Slide 12: Loading Kernels - 2
Use the FURNSH routine to load all kernels–text and binary.
  Sample FORTRAN, C, IDL and MATLAB calls:
    CALL FURNSH ( ‘name.ext’ )
    furnsh_c ( “name.ext” );
    cspice_furnsh, ‘name.ext’
    cspice_furnsh ( ‘name.ext’ )
Best practices: don’t hard code filenames–list these in a “meta-kernel” and load the meta-kernel using FURNSH. (See next page.)
  CALL FURNSH (‘meta-kernel_name’)
Caution: ”Transfer format" versions of binary kernels can not be loaded; they must first be converted to binary with the Toolkit utility program tobin or spacit.

## Slide 13: What is a “Meta-Kernel”
The terms “meta-kernel” and “FURNSH kernel” are used synonymously
Using a meta-kernel makes it easy to manage which SPICE files are loaded into your program
A meta-kernel is a file that lists names (and locations) of a collection of SPICE kernels that are to be used together in some SPICE-based application
  You can then simply load the meta-kernel, causing all of the kernels listed in it to be loaded
A meta-kernel is implemented using the SPICE text kernel standards

## Slide 14: Sample Meta-Kernel Contents (1)
This is a sample meta-kernel that the Toolkit routine FURNSH could use to load a collection of kernels.
KPL/MK
\begindata
  KERNELS_TO_LOAD = (
  '/home/mydir/kernels/lowest_priority.bsp',
  '/home/mydir/kernels/next_priority.bsp',
  '/home/mydir/kernels/highest_priority.bsp',
  '/home/mydir/kernels/leapseconds.tls',
  '/home/mydir/kernels/sclk.tsc',
  '/home/mydir/kernels/c-kernel.bc',
  '/home/mydir/kernels+’,
  '/custom/kernel_data/p_constants.tpc’,
  )
The last file listed in this example (p_constants.tpc) demonstrates how to use the continuation character ‘+’ to work around the 80 character limitation imposed on string sizes by the text kernel standards.
(Use the module STPOOL to retrieve a continued string.)

## Slide 15: Sample Meta-Kernel Contents (2)
This sample meta-kernel uses PATH_VALUES/PATH_SYMBOLS keywords to specify directory where the kernels are located.
KPL/MK
\begindata
PATH_VALUES = ( '/home/mydir/kernels’ )
PATH_SYMBOLS = ( 'KERNELS' )
KERNELS_TO_LOAD = (
  '$KERNELS/lowest_priority.bsp',
  '$KERNELS/next_priority.bsp',
  '$KERNELS/highest_priority.bsp',
  '$KERNELS/leapseconds.tls',
  '$KERNELS/sclk.tsc',
  '$KERNELS/c-kernel.bc',
  '$KERNELS/custom/kernel_data/p_constants.tpc’,
  )
Although the OS environment variable notation $NAME is used to refer to the symbols set by the PATH_VALUES/PATH_SYMBOLS keywords, these symbols are NOT OS environment variables and are set and used for substitution by SPICE only in the context of this particular meta-kernel.

## Slide 16: Limits on Loaded Kernels
The number of binary kernels that may be loaded at any time is large, but limited.
  For SPK, CK, and binary PCK files:
    Loaded SPKs + Loaded CKs + Loaded binary PCKs <= 1000
  For ESQ files:
    Loaded ESQs <= 20
  For all kernels:
    Loaded kernels <= 1300
      Assumes each has been loaded only once, and not unloaded.
There are also limits on the number of keywords and values for all loaded text kernels:
  Maximum number of keywords is 5003.
  Maximum number of numeric data items is 40,000.
  Maximum number of character data items is 4000.

## Slide 17: Kernel Precedence Rule
The order in which SPICE kernels are loaded at run-time determines their priority when requests for data are made
  For binary kernels, data from a higher priority file will be used in the case when two or more files contain data overlapping in time for a given object.
    For SPKs, CKs and binary PCKs the file loaded last takes precedence (has higher priority).
    Priority doesn’t apply to ESQ files – all data from all loaded files are available.
  If two (or more) text kernels assign value(s) using the “=” operator to identical keywords, the data value(s) associated with the last loaded occurrence of the keyword are used–all earlier values have been replaced with the last loaded value(s).
  Orientation data from a binary PCK always supersedes orientation data (for the same object) obtained from a text PCK, no matter the order in which the kernels are loaded.

## Slide 18: Unloading Kernels
The unloading of a kernel is infrequently needed for FORTRAN or CSPICE applications but is essential for ICY scripts
  Because of the way IDL and MATLAB interact with external shared object libraries any kernels loaded during an IDL or MATLAB session will stay loaded until the end of the session unless they are specifically unloaded
The routines KCLEAR and UNLOAD may be used to unload kernels containing data you wish to be no longer available to your program.
  KCLEAR unloads all kernels and clears the kernel pool
  UNLOAD unloads specified kernels
  KCLEAR and UNLOAD are only capable of unloading kernels that have been loaded with the routine FURNSH. They will not unload any files that have been loaded with older load routines such as SPKLEF (those used prior to availability of FURNSH).
Caution: unloading text kernels with UNLOAD will also remove any kernel pool data provided through the kernel pool API (P*POOL)

## Slide 19: Backup
How kernels are made and used
Why and how kernels are modified
SPICE data structures hierarchy

## Slide 20: How Kernels are Made and Used at JPL
SPK
PcK
IK
CK
FK
ESP
ESQ
ENB
LSK
SCLK
Meta-kernel
(FURNSH)
NAV and NAIF
NAIF
NAIF or other
SBP*
SBP*
SBP*
SBP*
SBP*
SBP*
Text editor
for text versions
SBP*
for binary versions
Text editor
Text editor
SBP*
SBP*
SBP*
Text editor
Text editor
WWW or
e-mail
Text editor or
existing file, input
via ESQ or ENB
Web browser
or SBP*, depending
on implementation
SBP*
SBP*
SBP*
SBP*
SBP*
How Made?
How Made?
How Used?
How Used?
Who usually makes the kernels at JPL?
This represents current practice for
most JPL missions, but is by no means a
requirement. Anyone can make SPICE files.
*SBP = SPICE-based program that uses modules from the SPICE Toolkit. In some cases the Toolkit contains such a program already built. In some cases NAIF may have such a ready-built program that is not in the SPICE Toolkit.
The EK family
1
2
2
2
2
2
2
1
2
3
3
3
3
3
DSK
SBP*
SBP*
2

## Slide 21: Why & How Kernels are “Modified” - 1
SPK
PcK
Text version
IK
CK
FK
File Type
Why Modified
How Modified
To add metadata (comments) - COMMNT, SPACIT or SPICELIB module
-To merge files or subset a file - SPKMERGE
-To correct/revise an object ID - BSPIDMOD
To revise data values - Text editor
To add additional data items and values - Text editor
To revise data values - Text editor
To add additional data items and values - Text editor
To add metadata (comments) - COMMNT, SPACIT, or SPICELIB module
To merge files - DAFCAT, CKSMRG
To revise the interpolation interval - CKSPANIT, CKSMRG
To subset a file - CKSLICER
To revise data values - Text editor
To add additional data items and values - Text editor
DSK
To add metadata (comments) - COMMNT, SPACIT or SPICELIB module
-To merge files or subset a file - DSKMERGE

## Slide 22: Why & How Kernels are “Modified” - 2
ESP
ESQ
ENB
LSK
SCLK
Meta-kernel
(FURNSH)
Why Modified
How Modified
The EK family
File Type
To add, revise or delete “data” - (Depends on implementation)
To add metadata (comments) - (Depends on implementation)
To add additional data - Toolkit modules
To revise data - Toolkit modules
To delete data - Toolkit modules
To add metadata (comments) - COMMNT, SPACIT or SPICELIB module
To merge files - (under development)
To change entry status (public <--> private) - WWW
To delete an entry - WWW
- To add a new leapsecond - Text editor
- To add metadata - Text editor
- To revise contents in any way - Text editor

## Slide 23: SPICE Data Structures Hierarchy
OR
AND
SPK
CK
OR
PcK
IK
FK
LSK
SCLK
ENB
ESP
ESQ
DBK
MIME
including
plain text
DAS
TEXT
DAF
EK Family
Binary
Binary
Text
DAF = Double Precision Array File DAS = Direct Access, Segregated
DBK = Data Base Kernel DLA = DAS Linked Array (under development)
Excepting MIME, each of these data structures is built entirely of SPICE components.
PcK files are usually text-based, but binary versions exist for the earth and moon. The ESP has been
implemented using both the ENB and ESQ mechanisms. The DBK is a SQL-like, homebrew database.
Low
Level
Mid
Level
High
Level
Meta-kernel
(FURNSH)
DSK
DLA