## Slide 1: “Metadata” In SPICE Kernels Also known as “comments”
October 2007
Notes: 1

## Slide 2: What are Metadata?
Metadata are information that describe the context of kernel data, i.e. “data about data”
  “If you don’t write it down, it didn’t happen”
Examples of metadata:
  Data descriptions
    “This file contains representations of the trajectories for bodies X, Y and Z over the interval from launch to landing”
  Data accuracy
  Data pedigree
    How and by whom was the kernel created
      The program(s) and/or steps used in creation
      Contact information for user’s questions
        email address
        phone numbers
    Data sources used as inputs when creating the kernel
  Intended kernel usage
  Companion files
In SPICE, we normally refer to metadata as “kernel comments”
Notes: 2

## Slide 3: Where are SPICE Metadata Stored?
Binary Kernels contain a “comment” area
  A comment is text data
  Comments may be placed in binary kernels or read or extracted from binary kernels using the SPICE utility program commnt
Text Kernels have comments interleaved with the data
  Comments in text kernels can be read using any editor, or UNIX’s cat or more processors
Notes: 3

## Slide 4: Using COMMNT on Binary Kernels
Terminal Window
prompt> commnt
Welcome to COMMNT Version: 6.0.0
(SPICE Toolkit N0050)
COMMNT Options
( Q ) Quit.
( A ) Add comments to a binary file.
( R ) Read the comments in a binary file.
( E ) Extract the comments from a binary file.
( D ) Delete the comments in a binary file.
Option: R
Enter the name of the binary file.
Filename? /home/mydirectory/myproject/kernels/spk/de403s.bsp
Filename must include any required path and be less than 257 characters
This example shows reading the comments

## Slide 5: Viewing Text Kernel Comments
Terminal Window
prompt> more leapseconds.ker
\begintext
LEAPSECONDS KERNEL FILE
===============================================================
Modifications:
--------------
1998, Jun 17 WLT Modified file to account for the leapsecond
that will occur on December 31, 1998.
1997, Feb 22 WLT Modified file to account for the leapsecond
that will occur on June 30, 1997.
1995, Dec 14 KSZ Corrected date of last leapsecond from 1-1-95
to 1-1-96
etc…..
--More--(19%)
-More--(19%)

## Slide 6: How to Add Comments
Binary Kernels
  Include comment information at the time of kernel creation, using SPICE modules (subroutines)
    This capability not yet available in Icy or Mice
  Use the commnt utility program
    Adds comments provided in an external text file
Text Kernels
  Use a text editor
    Begin comment sections with the “\begintext” marker alone on a line
Restrictions
  For both binary and text kernels
    Comment line length limit is 255 characters. However, NAIF recommends using no more than 80 characters per line as this makes your comments far more readable!
    Use only printing characters (ASCII 32 - 126)
    Manipulating binary kernel comments requires the kernel be in the native binary format for the machine being used
  For text kernels
    Refer to “Kernel Required Reading” (kernel.req) for details
Notes: 7