## Slide 1: Leapseconds and Spacecraft Clock Kernels LSK and SCLK
October 2007

## Slide 2: SPICE Time Conversion Kernels
LSK - The leapseconds kernel is used in conversions between ephemeris time (ET/TDB) and Coordinated Universal Time (UTC).
SCLK - The spacecraft clock kernel is used in conversions between spacecraft clock time (SCLK) and ephemeris time (ET/TDB).
  (It’s possible there could be two or more clocks associated with a given spacecraft.)
In most cases one or two kernel files are needed to perform conversions between supported time systems.

## Slide 3: The Leapseconds Kernel (LSK)
Used in ET UTC and in ET SCLK conversions.
  Utility programs: spkmerge, chronos, spacit, etc.
  Subroutines: STR2ET, ET2UTC, TIMOUT, etc.
As with all SPICE kernels, load it using FURNSH.
NAIF updates the LSK when a new leapsecond is announced by the International Earth Rotation Service (IERS).
  The latest LSK file is always available from the NAIF server.
    The latest is always the best one to use.
  Announcement of each new LSK is made using the “spice_announce” system.
    http://naif.jpl.nasa.gov/mailman/listinfo/spice_announce
The leapseconds kernel contains a tabulation of all the leapseconds that have occurred, plus additional terms.

## Slide 4: Out of Date LSKs
An out-of-date leapseconds kernel can be used successfully for conversions that occur at epochs prior to the epoch of the first missing leapsecond.
  But any conversions of epochs occurring after the epoch of a missing leapsecond will introduce inaccuracies in multiples of one second per missed leapsecond.
Using the latest leapseconds kernel to perform conversions at epochs more than six months ahead of the last leapsecond listed may result in an error if, later on, a new leapsecond is declared for a time prior to the epochs you processed.

## Slide 5: The Spacecraft Clock Kernel (SCLK)
The spacecraft clock kernel contains data to perform conversions from SCLK to other time systems.
It is required by Toolkit utilities and routines that utilize SCLK time.
  For example, the SPICE CK subsystem makes heavy use of spacecraft clock time.
As with all SPICE kernels, use FURNSH to load it.
Ensure you have the correct version of the SCLK file for your spacecraft since this kernel may be updated rather frequently.
  SCLK files are usually maintained on a flight project’s database.
    For JPL operated missions they can usually be found on the NAIF server as well.
  When using a CK, “correct SCLK” means compatible with that CK.
    For reconstructed CKs, this is most likely the latest version of the SCLK.
    For “predict” CKs, this is probably the SCLK kernel used when the CK was produced.

## Slide 6: SCLK File Example
\begindata
SCLK_KERNEL_ID = ( @1999-08-02/10:53:19.72 )
SCLK_DATA_TYPE_82 = ( 1 )
SCLK01_TIME_SYSTEM_82 = ( 2 )
SCLK01_N_FIELDS_82 = ( 2 )
SCLK01_MODULI_82 = ( 4294967296 256 )
SCLK01_OFFSETS_82 = ( 0 0 )
SCLK01_OUTPUT_DELIM_82 = ( 1 )
SCLK_PARTITION_START_82 = ( 1.7772134886400E+11 )
SCLK_PARTITION_END_82 = ( 1.0995116277750E+12 )
SCLK01_COEFFICIENTS_82 = (
0.0000000000000E+00 -6.3119514881600E+08 1.0001400000000E+00
1.2098765056000E+10 -5.8393434781600E+08 1.0000900000000E+00
2.0171981312000E+10 -5.5239834681600E+08 1.0001200000000E+00
2.8245197568000E+10 -5.2086234581600E+08 1.0001100000000E+00
4.4413748224000E+10 -4.5770394481600E+08 1.0000800000000E+00
. . .
. . .
. . .
)
\begintext
SCLK value
TDT or TDB value
corresponding to SCLK value
Clock Rate
(seconds per most significant component)
Time system ID:
1 --> TDB, Barycentric Dynamical Time
2 --> TDT, Terrestrial Dynamic Time
Clock Type
Encoded clock readings at partition start and stop.

## Slide 7: Forms of SCLK Time Within SPICE
SCLK time in SPICE is represented in two different ways:
  a character string
  a double precision (DP) number called “ticks”
A SCLK character string is composed of one or more cascading integer numbers – similar to a digital clock.
  This form is what is generally found in downlinked telemetry, whether for science or engineering/husekeeping data.
A SCLK value encoded as a double precision (DP) number (called “ticks”) is used internal to SPICE because it’s easy to convert this to other time systems, such as ephemeris time (ET).

## Slide 8: Sample SCLK String - 1
The Cassini orbiter SCLK time string consists of three fields separated by delimiters.
1/4132564.034
Partition: Accounts for clock resets or counter roll-over.
Most Significant Clock Field:
Ranges from 0 to 4294967295 (232-1). Nominally 1 second increment.
Least Significant Clock Field:
Ranges from 0 to 255. Nominally 1/256th of a second increment.
Clock Field Delimiter* (not a decimal point)
Partition
Delimiter
* Several SCLK delimiter characters are available in SPICE. See “SCLK Required Reading” for details.

## Slide 9: What is a Partition?
A partition is a NAIF-created construct to handle spacecraft clock rollovers or resets.
When referring to epochs in the first partition, the leading ‘1/’ may be omitted.
Modern spacecraft rarely use a partition other than 1/.
1/4132564.034
The portion of the SCLK string circled above indicates the partition to which the remaining portion of the string is related.

## Slide 10: Sample SCLK String - 2
The Galileo spacecraft SCLK time string consists of five fields separated by delimiters.
1/16777214:90:9:7
Partition: Accounts for clock resets or counter roll-over.
Most Significant Clock Field:
Ranges from 0 to 16777214. Nominally 60 2/3rd second increment.
Least Significant Clock Field:
Ranges from 0 to 7. Nominally 1/120th of a second.
Clock Field Delimiters
Partition
Delimiter
Intermediate Clock Field:
Ranges from 0 to 9. Nominally 1/15th of a second.
Intermediate Clock Field:
Ranges from 0 to 90. Nominally 2/3rd of a second.

## Slide 11: Sample SCLK Strings - 3
Cassini
  1/1334314108.134
DS1
  1/67532406.010
Galileo
  1/16777214:90:9:7
Genesis
  1/666230496.204
MGS
  1/655931592.103
The following are examples of SCLK strings* from missions using SPICE.
MPF
  1/559627908.058
Mariner 9
  1/11542909
Mars Odyssey
  1/687231994.091
NEAR
  1/40409721942
Stardust
  1/697451990.042
Viking 1&2
  1/32233616
Voyager 1&2
  1/05812:00:001
Mars Express
  1/0090979196.29713
Venus Express
  1/0033264000.50826
Rosetta
  1/0101519975.65186
* When clock strings are used as arguments in modules they must be contained in quotes:
  - Single quotes for Fortran
  - Double quotes for C
  - Single quotes for IDL and MATLAB

## Slide 12: Encoded SCLK (Ticks)
Encoded spacecraft clock values represent “ticks since spacecraft clock start.”
  The time corresponding to tick “0” is mission dependent and does not necessarily relate to launch time. In fact it is often an arbitrary epoch occurring before launch.
A tick is the smallest increment of time that a spacecraft clock measures. For example, in the case of the Cassini orbiter this is nominally 1/256th of a second.
Encoded SCLK increases continuously independent of leapseconds, clock resets, and counter rollovers.
The representation of SCLK time in the SPICE system is a double precision encoding of a SCLK string.

## Slide 13: SCLK Interface Routines
SCS2E (SC, SCLKCH, ET) (SCLK String ET)
SCE2S (SC, ET, SCLKCH) (ET SCLK String)
SCT2E (SC, SCLKDP, ET) (Encoded SCLK ET)
SCE2C1 (SC, ET, SCLKDP) (ET Continuous Encoded SCLK)
SCE2T (SC, ET, SCLKDP) (ET Discrete Encoded SCLK)
SCENCD(SC, SCLKCH, SCLKDP) (Encode SCLK)
SCDECD(SC, SCLKDP, SCLKCH) (Decode SCLK)
Convert SCLK times using the following routines
1 Use SCE2C (not SCE2T) for C-kernel data access.