## Slide 1: Planetary Constants Kernel PCK
October 2007

## Slide 2: Topics
Overview
Using PCKs
Text PCKs
IAU Models
Binary PCKs
Interface Routines
PCK Reference Frames

## Slide 3: Overview
The P_constants kernel (PCK or PcK) is logically a part of the “planet kernel.”
SPICE PCK data consist of:
  Orientation (also known as “rotation”) models for extended, natural solar system bodies: sun, planets, natural satellites, a few asteroids
    Location of the pole and prime meridian
    Axis directions of a body-fixed, body-centered reference frame
    Spin rate
  Physical and cartographic constants
    Sets of radii for triaxial shape models.
    Additional items could be included, such as
      prime meridian offset from the principal axis
      magnetic dipole location
      gravity parameters: GM, J2, higher order gravity field terms
      ring model parameters
PCK data files are called “PCK kernels,” “PCKs” or “PCK files.”
The PCK subsystem supports text and binary PCK file formats.
  Text PCKs may contain orientation, shape, and other cartographic or physical data.
  Binary PCKs are used for high-accuracy orientation data.
    Binary PCKs are available only for the earth and the moon.

## Slide 4: Using PCKs
Load PCKs using FURNSH
  Orientation data from a binary PCK always supersedes orientation data (for the same object) obtained from a text PCK, no matter the order in which the kernels are loaded
PCK orientation data are usually accessed via Frame system or SPK calls
  Example: Get the IAU_SATURN body-fixed reference frame to J2000 position or state transformation matrix at ET:
    CALL PXFORM ( ‘IAU_SATURN’, ‘J2000’, ET, RMAT )
    CALL SXFORM ( ‘IAU_SATURN’, ‘J2000’, ET, XFORM )
  Example: Get state of Saturn relative to Cassini in the IAU_Saturn body-fixed reference frame:
    CALL SPKEZR ( ‘SATURN’, ET, ‘IAU_SATURN’, ‘LT+S’, CASSINI, STATE, LT )
  Example: Get state of Cassini relative to the DSN station DSS-13 in the J2000 inertial reference frame:
    CALL SPKEZR ( ‘CASSINI, ET, ‘J2000’, ‘LT+S’, ‘DSS-13’, STATE, LT )
      An Earth PCK must be loaded in order for this call to work.
        Even though the specified reference frame is inertial
        This call, in the course of its work, converts the position of the DSN station relative to the Earth’s center from an Earth-fixed, earth-centered frame to the J2000 frame.
Access to PCK shape and other data is discussed in the section titled “Interface Routines”

## Slide 5: Text PCK Files - 1
Text PCK files may contain orientation, shape and other data associated with natural solar system bodies.
NAIF creates and distributes “generic” text PCK files based on IAU/IAG reports, published in ICARUS.
  These PCKs contain orientation and shape data provided by the reports.
  SPICE PCK software is designed to use these data to compute orientation of body-fixed frames.
NAIF provides a “masses” PCK containing GM values for the Sun and planetary systems.
  Values from this file may be used with SPICE osculating element routines
Text PCKs are sometimes produced by NASA flight projects and others; not only by NAIF.

## Slide 6: Text PCK Files - 2
The SPICE text kernel mechanism is used to implement generic PCK files.
  Users may easily visually inspect data.
  Users may (carefully!) modify text PCKs with a text editor.
    Data or comments may be added, deleted, or changed.
    Comments should be added to explain changes.
  Kernel variables contain the mathematical terms appearing in rotation or shape models.
    BODY699_RADII = ( 60268 60268 54364 )
    BODY699_POLE_RA = ( 40.58 -0.036 0. )
  The user may include additional kernel variables to change the base frame or reference epoch.
  Kernel variable names are case-sensitive.
    NAIF uses only upper case for variable names; we suggest you do the same.

## Slide 7: IAU Rotation Models - 1
SPICE shape models use data from the IAU/IAG (formerly IAU/IAG/COSPAR) Working Group Report, as published in ICARUS.
  Latest full report used by NAIF was issued in 2000.
IAU rotation models are provided:
  for the sun and planets:
    IAU models use low-degree (typically linear) polynomials to represent RA and DEC of the pole (body-fixed +Z-axis) as a function of time.
    The prime meridian is also represented by a low-degree polynomial.
    Trigonometric polynomial terms are supported by SPICE
      but are rarely used in IAU models for planet orientation
  for natural satellites:
    Additional trigonometric polynomial terms are used to more accurately represent precession and nutation.
    A few satellites exhibit chaotic rotation and so are not modeled.
  for some major asteroids (e.g. Ida, Eros, Gaspra, Vesta)

## Slide 8: IAU Rotation Models - 2
IAU body-fixed frames are planetocentric.
  Z-axis is aligned with +/- spin axis. The positive Z-axis points toward the north side of the invariable plane of the solar system.
  The invariable plane is normal to the solar system’s angular momentum vector. It is
    approximately the same as Jupiter’s orbital plane.
    roughly parallel to the ecliptic plane.
  X-axis defines the prime meridian.
  Y-axis completes the right-handed frame.
The IAU base frame is the IERS-defined International Celestial Reference Frame (ICRF).
  SPICE treats the ICRF as equivalent to J2000 (EME2000).
The IAU reference epoch is J2000 (2000 Jan 1 12:00:00 TDB).

## Slide 9: IAU Shape Models
IAU shape models are nominally triaxial ellipsoids
  Triaxial ellipsoid shape models have the form:
  For many bodies, two of the axes (equatorial axes) have the same value (spheroidal)
  For some bodies, one or more radii have not been determined.
Although many bodies are in fact modeled by spheroids or oblate spheroids, SPICE deals with the general, triaxial case.
  Exception: SPICE supports geodetic coordinate transformations only for bodies modeled as spheroids or oblate spheroids.
    RECGEO and GEOREC are the modules performing these transformations.
  Exception: SPICE supports planetographic coordinate transformations only for bodies modeled as spheroids or oblate spheroids.
    PGRREC, RECPGR, DPGRDR and DRDPGR are the modules supporting these transformations.
x2
a2
z2
c2
y2
b2
+
+
= 1

## Slide 10: Binary PCK Files
The SPICE system stores high-accuracy orientation models in binary PCKs.
  Binary PCKs are implemented using the DAF file architecture (as are SPK files)
    Binary PCKs are not human-readable.
    SPICE API routines enable applications tocreate binary PCKs.
    SPICE Toolkit utilities enable reading and writing comments, summarizing, and porting binary PCKs.
  Like SPK files, binary PCKs support multiple data representations (“data types”).
    Type 2: Chebyshev polynomials for Euler angles, angular velocity obtained by differentiation, constant interval length.
    Type 3: Separate Chebyshev polynomials for Euler angles and their derivatives, variable interval length.
Binary PCKs are limited to storing orientation data.
  Applications that require shape data must also load a text PCK.
Binary PCKs are available for the Earth and Moon.
  The orientation data provided by these kernels are much more accurate than those provided by generic text PCKs based on the IAU/IAG reports.
  These kernels are the topic of the tutorial on high-accuracy orientation data and associated frames for the Earth and Moon.

## Slide 11: Interface Routines - 1
Call FURNSH to load PCKs.
  CALL UNLOAD or KCLEAR to unload them.
Call SXFORM to return a state transformation.
  Returns 6x6 matrix (attitude and angular velocity)
Call PXFORM to return a position transformation.
  Returns 3x3 matrix (attitude only)
The older routines TISBOD, TIPBOD, and BODMAT are still supported, but NAIF recommends users not call them directly.
CALL SXFORM ( FROM, TO, ET, XFORM )
sxform_c ( from, to, et, xform );
cspice_sxform, from, to, et, xform
xform = cspice_sxform ( from, to, et )
CALL PXFORM ( FROM, TO, ET, RMAT )
pxform_c ( from, to, et, rmat );
cspice_pxform, from, to, et, rmat
rmat = cspice_pxform ( from, to, et )

## Slide 12: Interface Routines - 2
Call BODVRD or BODVCD to retrieve constants associated with a body. For example:
  These calls retrieve values associated with the variable BODY699_RADII.
  The variable name is case-sensitive, so the string “RADII” above must be in upper case.
You can also use general kernel pool fetch routines to fetch data assigned to non-standard names:
  GCPOOL, GDPOOL, GIPOOL
CALL BODVRD ( 'SATURN', 'RADII', 3 N, RADII )
CALL BODVCD ( 699, 'RADII', 3 N, RADII )
bodvrd_c ( "SATURN", "RADII", 3 &n, radii );
bodvcd_c ( 699, "RADII", 3 &n, radii );
cspice_bodvrd, ‘SATURN’, item, 3, radii
cspice_bodvcd, 699, item, 3, radii
radii = cspice_bodvrd ( ‘SATURN’, item, 3 )
radii = cspice_bodvcd ( 699, item, 3 )
Notes: EDW 04-OCT-2001 (JPL)
Edits.

## Slide 13: PCK Reference Frames -1
Many PCK reference frame specifications are built-in to SPICE.
  “Just add orientation data” (load PCK files) to use these frames. Examples:
    IAU frames: IAU_SATURN, IAU_TITAN, IAU_EARTH, IAU_MOON, etc.
    IERS frames: ITRF93
Other PCK frames are not built in and must be specified at run time by loading frame kernels, for example:
  Body fixed frames for asteroids or “newer” natural satellites
    See the Frames Required Reading for information on creating frame kernels that specify PCK reference frames.
  Lunar body-fixed frames: MOON_ME, MOON_PA
    See the tutorial on “high-accuracy orientation data and associated frames for the Earth and Moon” for details.
SPICE makes default associations between bodies and built-in PCK frames
  For example, the default PCK frames for the planets are IAU_MERCURY, IAU_VENUS, IAU_EARTH, etc.
continued on next page

## Slide 14: PCK Reference Frames - 2
  (continued)
  You can look up the default PCK frame associated with a body by calling CNMFRM or CIDFRM.
    In Icy, only CNMFRM is currently available.
    Neither is yet available in beta version of Mice.
Some SPICE routines use the default PCK frames:
  SUBPT, SUBSOL, ILLUM, SRFXPT, ET2LST
  implicitly used in some dynamic frames
You can change the default PCK frame associated with a body by loading a frame kernel that assigns a new default frame to that body.
  For the Earth or Moon, you can load a “frame association kernel” provided by NAIF.
  For any body, you can load a frame kernel containing the assignment
  OBJECT_<body name>_FRAME = ‘<new default frame name>’
    Example: OBJECT_MOON_FRAME = ‘MOON_ME’
For high-accuracy work involving the Earth or Moon and any SPICE routines that use the default PCK frames, you normally would override the SPICE default frames by loading frame association kernels.
  See the tutorial on “high-accuracy orientation data and associated frames for the Earth and Moon” for details.