## Slide 1: Frames Kernel FK
October 2007

## Slide 2: Introduction
What does the FRAMES subsystem do?
It establishes relationships between reference frames used in geometry computations -- it "chains frames together."
It connects frames with sources of their orientation specifications.
Based on these relationships and orientation source information, it allows SPICE software to compute transformations between neighboring frames in the "chain," and to combine these transformations in the right order, thus providing an ability to compute orientation of any frame in the chain with respect to any other frame in the chain at any time. (*)
(*) If the complete set of underlying SPICE data need to compute the transformation is available.

## Slide 3: Sample Frame Tree and Chains

## Slide 4: Frame Classes
Frame class
Inertial
Body-fixed
CK-based
Fixed Offset
Dynamic
Examples
Earth Equator/Equinox of Epoch (J2000, …)
Planet Equator/Equinox of Epoch (MARSIAU, ...)
Ecliptic of Epoch (ECLIPJ2000, ...)
Solar system body IAU frames (IAU_SATURN, …)
High accuracy Earth frames (ITRF93, …)
High accuracy Moon frames (PA)
Spacecraft (CASSINI_SC_BUS, …)
Moving parts of an instrument (MPL_RA_JOINT1, ...)
Instrument mounting alignment (CASSINI_ISS_NAC, …)
Topocentric (DSS-14_TOPO, …)
Earth Mean Equator and Equinox of Date (EME_OF_DATE)
Geocentric Solar Ecliptic (GSE)
Nadir frame (SC_NADIR_POINTED)

## Slide 5: Frames Class Specifications
Frame class Frame Defined in Orientation provided in
Inertial Toolkit Toolkit
Bodyfixed Toolkit or FK PCK
CK based FK CK
Fixed offset FK FK
Dynamic FK Toolkit, or computed
using FK, SPK, CK, and/or
PCK

## Slide 6: FRAMES Subsystem Interfaces
SXFORM/PXFORM returns state or position transformation matrix
CALL SXFORM ( ‘FROM_FRAME_NAME’, ‘TO_FRAME_NAME’, ET, MAT6x6 )
CALL PXFORM ( ‘FROM_FRAME_NAME’, ‘TO_FRAME_NAME’, ET, MAT3X3 )
SPKEZR/SPKPOS returns state or position vector in specified frame
CALL SPKEZR ( BOD, ET, ‘FRAME_NAME’, CORR, OBS, STATE, LT )
CALL SPKPOS ( BOD, ET, ‘FRAME_NAME’, CORR, OBS, POSITN, LT )
The above are FORTRAN examples, using SPICELIB modules.
The same interfaces exist for C, using CSPICE modules, and for Icy and Mice.

## Slide 7: CK-Based Frames “Must Know”
The frames routines (SPKEZR/SPKEZ, SPKPOS, SXFORM, PXFORM) all read CK files using tolerance = 0
  For discrete CKs the orientation of a CK-based frame will be computed only if the time provided to a Frames routine exactly matches one of the times stored in the CK file; otherwise an error will be signaled.
  For continuous CKs the orientation of a CK-based frame will be computed only if the time provided to a Frames routine falls within one of the interpolation intervals defined by the CK file; otherwise an error will be signaled.
Using SPKEZR or SXFORM requires CKs with angular rates
  Since these routines return a state vector (6x1) or state transformation matrix (6x6), angular rates must be present in the CK in order to compute vectors and matrices; if rates are not present, an error will be signaled.
  SPKPOS and PXFORM, which return a position vector (3x1) and a position transformation matrix (3x3) respectively, can be used instead because they require only orientation data to be present in the CK.
Ephemeris time input to Frames routines is converted to SCLK to access CKs
  SCLK and LSK kernels must be loaded to support this conversion.
  SCLK ID is specified in one of the CK frame definition keywords; if not, it’s assumed to be the Frame ID divided by a 1000.
These are VERY IMPORTANT points you must understand!

## Slide 8: What are the Names of Frames?
Refer to FRAMES.REQ for the list of NAIF “built in” (hard coded) inertial and body-fixed frames
Refer to a project’s Frames Kernel (FK) file for a list of frames defined for the spacecraft, its subsystems and instruments
Refer to an earth stations FK for a list of frames defined for the DSN and other stations

## Slide 9: Frames Kernel File
Uses the SPICE text kernel file standards
Loaded using the FURNSH routine
Usually contains comprehensive information about the defined frames in the text section(s) of the file
Contains frame definition information consisting of a set of keywords in the data sections of the file. For example, the frame for the scanner assembly of the ASPERA instrument on the Mars Express spacecraft is defined as:
\begindata
FRAME_MEX_ASPERA_SAF = -41111
FRAME_-41111_NAME = 'MEX_ASPERA_SAF'
FRAME_-41111_CLASS = 3
FRAME_-41111_CLASS_ID = -41111
FRAME_-41111_CENTER = -41
CK_-41111_SCLK = -41
CK_-41111_SPK = -41
\begintext

## Slide 10: Frame Definition Details - 1
Frame ID is an integer number used by the SPICE system as a “handle” in buffering and retrieving various parameters associated with a frame. In an FK it “glues” together the keywords defining the frame.
FRAME…NAME assigns a name to the Frame ID code.
FRAME…CLASS specifies the method by which the frame is related to some other frame — inertial, PCK, CK, TK, dynamic.

## Slide 11: Frame Definition Details - 2
FRAME…CLASS_ID is the number that connects a frame with the orientation data for it.
  For body-fixed frames CLASS_ID is the ID of the natural body. It is used as input to PCK routines called by the Frame subsystem to compute orientation of the frame.
    Frame ID and CLASS_ID are not the same for the body-fixed frames defined in the Toolkit but they can be the same for frames defined in FK files.
  For CK-based frames CLASS_ID is the CK structure ID. It is used as input to CK routines called by the Frame subsystem to compute orientation of the frame.
    Normally CLASS_ID of a CK-based frame is the same as the frame ID.
  For fixed offset and dynamic frames CLASS_ID is the ID that is used to retrieve the frame definition keywords.
    CLASS_ID of a fixed offset or dynamic frame is the same as the frame ID
FRAME..CENTER specifies the ephemeris object at which the frame origin is located.
CK…SCLK identifies the spacecraft clock associated with the CK structure ID. Used by the frames subsystem to convert ET to SCLK used to look up CK data.
CK…SPK identifies the ephemeris object associated with the CK structure ID (not currently used; included for future use).

## Slide 12: Frame Tree Example: ASPERA Instrument on Mars Express
"J2000" <-inertial
|
+-----------------------------------------------------+
| | |
|<-pck | |<-pck
| | |
V | V
"IAU_MARS" | "IAU_EARTH"
MARS BODY-FIXED |<-ck EARTH BODY-FIXED
--------------- | ----------------
V
"MEX_SPACECRAFT"
+-----------------------------------------------------+
| |
|<-fixed |<-fixed
| |
V V
"MEX_ASPERA_URF" "MEX_ASPERA_IMA_URF"
----------------- --------------------
| |
|<-ck |<-fixed
| |
V V
"MEX_ASPERA_SAF” “MEX_ASPERA_IMA”
--------------------------------------------- ... ----------------
| | |
|<-fixed |<-fixed |<-fixed
| | |
V V V
"MEX_ASPERA_ELS" "MEX_ASPERA_NPI" "MEX_ASPERA_NPD1"
---------------- ---------------- ----------------
Blue text indicates frame class