## Slide 1: Instrument Kernel IK
October 2007

## Slide 2: Purpose
The Instrument kernel serves as a repository for instrument specific information that may be useful within the SPICE context.
  Specifications for an instrument’s field-of-view size, shape, and orientation.
  Internal instrument timing parameters and other data relating to SPICE computations might also be placed in an I-kernel.
Note: Instrument mounting alignment data are most often specified in a mission’s frames kernel (FK).
The IK is a SPICE text kernel.

## Slide 3: I-Kernel Structure
KPL/IK
Comments describing the keywords and values
to follow, as well as any other pertinent
information.
\begindata
Keyword = Value Assignments
\begintext
More descriptive comments.
\begindata
More Keyword = Value Assignments
\begintext
More comments, followed by more data, etc …
The format and structure of a typical I-Kernel is:

## Slide 4: I-Kernel Contents (1)
The requirements on keywords in an IK are the following:
  Keywords must begin with INS[#], where [#] is replaced with the NAIF instrument ID code (which is a negative number).
  The total length of the keyword must be less than 32 characters.
  Keywords are case-sensitive. (Keyword != KEYWORD)
Some examples of IK keywords:
  MGS MOC NA focal length: INS-94031_FOCAL_LENGTH
  MEX HRSC SRC pixel angular size: INS-41220_IFOV
  MEX ASPERA NPI number of sectors: INS-41130_NUMBER_OF_SECTORS
In general SPICE does not require any specific keywords to be present in an IK
  One exception is a set of keywords defining an instrument’s FOV if the NAIF Toolkit’s GETFOV routine is planned to be used to retrieve the FOV attributes
    Keywords required by GETFOV will be covered later in this tutorial

## Slide 5: I-Kernel Contents (2)
IKs usually contain extensive comments including
  Instrument overview
  Reference source(s) for the data included in the IK
  Names/IDs assigned to the instrument and its parts
  Explanation of each keyword included in the file
  Description of the FOV and detector layout
  Sometimes descriptions of the algorithms in which parameters provided in the IK are used, and even fragments of source code implementing these algorithms
    For example optical distortion models or timing algorithms
This documentation exists primarily to assist users in integrating I-Kernel data into their applications
  One needs to know the keyword name to get its value from the loaded IK data
  One needs to know what that value means in order to use it

## Slide 6: I-Kernel Interface Routines
As with any SPICE kernel, IK files are loaded using FURNSH
  CALL FURNSH ( ’ik_file_name.ti’ )
By knowing the name and type (DP, integer, or character) of a keyword of interest, the value(s) associated with that keyword can be retrieved using G*POOL routines
  CALL GDPOOL ( NAME, START, ROOM, N, VALUES, FOUND )
  CALL GIPOOL ( NAME, START, ROOM, N, VALUES, FOUND )
  CALL GCPOOL ( NAME, START, ROOM, N, VALUES, FOUND )
When an instrument’s FOV is defined in the IK using a special set of keywords discussed later in this tutorial, the FOV shape, reference frame, boresight vector, and boundary vectors can be retrieved by calling the GETFOV routine
  CALL GETFOV ( INSTID, ROOM, SHAPE, FRAME, BSIGHT, N, BOUNDS)

## Slide 7: FOV Definition Keywords (1)
The following keywords defining FOV attributes for the instrument with NAIF ID (#) must be present in the IK if the NAIF Toolkit’s GETFOV module will be used
  Keyword defining shape of the FOV
    INS#_FOV_SHAPE = 'CIRCLE' or 'ELLIPSE' or
    'RECTANGLE' or 'POLYGON'
  Keyword defining reference frame with respect to which the boresight vector and FOV boundary vectors are specified
    INS#_FOV_FRAME = 'frame name'
  Keyword defining the boresight vector
    INS#_FOV_BORESIGHT = ( X, Y, Z )

## Slide 8: FOV Definition Keywords (2)
  Keyword(s) defining FOV boundary vectors, in either of two ways
    By specifying boundary vectors explicitly
    INS#_FOV_CLASS_SPEC = 'CORNERS' (optional)
    INS#_FOV_BOUNDARY_CORNERS = ( X(1), Y(1), Z(1),
    … … …
    X(n), Y(n), Z(n) )
    where the FOV_BOUNDARY_CORNERS keyword provides an array of vectors that point to the "corners" of the instrument field of view.

## Slide 9: FOV Definition Keywords (3)
    By providing half angular extents of the FOV (possible only for circular, elliptical or rectangular FOVs)
INS#_FOV_CLASS_SPEC = 'ANGLES'
INS#_FOV_REF_VECTOR = ( X, Y, Z )
INS#_FOV_REF_ANGLE = halfangle1
INS#_FOV_CROSS_ANGLE = halfangle2
INS#_FOV_ANGLE_UNITS = 'DEGREES' or
'RADIANS’ or …
    where the FOV_REF_VECTOR keyword specifies a reference vector that together with the boresight vector defines the plane in which the half angle given in the FOV_REF_ANGLE keyword is measured. The other half angle given in the FOV_CROSS_ANGLE keyword is measured in the plane normal to this plane and containing the boresight vector.

## Slide 10: FOV Definition Keywords (4)
Neither boresight nor reference vectors have to be co-aligned with one of the FOV frame’s axes
  But for convenience they are frequently defined to be along one of the axes
Neither boresight nor corner nor reference vectors have to be unit vectors
  But they frequently are defined as unit vectors
When a FOV is specified using the half angular extents method, boresight and reference vectors have to be linearly independent but they don’t have to be perpendicular
  But for convenience the reference vector is usually picked to be normal to the boresight
Half angular extents for a rectangular FOV specify the angles between the boresight and the FOV sides, i.e. they are for the middle of the FOV

## Slide 11: Circular Field of View
Consider an instrument with a circular field of view.
Angular Size
Boundary Corner Vector
Boresight Vector
Instrument
X
Y
Z
(0,0,0)
(0,1,4)
Y
X
14.03 O
Subtended field of view angle
14.03 = arc tan (1/4)

## Slide 12: Circular FOV Definition
The following sets of keywords and values describe this circular field of view:
INS-11111_FOV_SHAPE = 'CIRCLE'
INS-11111_FOV_FRAME = 'FRAME_FOR_INS-11111'
INS-11111_FOV_BORESIGHT = ( 0.0 0.0 1.0 )
INS-11111_FOV_BOUNDARY_CORNERS = ( 0.0 1.0 4.0 )
INS-11111_FOV_SHAPE = 'CIRCLE'
INS-11111_FOV_FRAME = 'FRAME_FOR_INS-11111'
INS-11111_FOV_BORESIGHT = ( 0.0 0.0 1.0 )
INS-11111_FOV_CLASS_SPEC = 'ANGLES'
INS-11111_FOV_REF_VECTOR = ( 0.0 1.0 0.0 )
INS-11111_FOV_REF_ANGLE = 14.03624347
INS-11111_FOV_ANGLE_UNITS = 'DEGREES'
Specifying boundary vectors explicitly:
Specifying half angular extents of the FOV:

## Slide 13: Elliptical Field of View
Consider an instrument with an elliptical field of view.
Boundary Corner Vectors
Boresight Vector
Instrument
X
Y
Z
(0,0,0)
(0,1,4)
(2,0,4)
Y
X
14.03 O
26.57 O
Subtended field of view angle
14.03 = arc tan (1/4)
26.57 = arc tan (2/4)

## Slide 14: Elliptical FOV Definition
The following sets of keywords and values describe this elliptical field of view:
INS-22222_FOV_SHAPE = 'ELLIPSE'
INS-22222_FOV_FRAME = 'FRAME_FOR_INS-22222'
INS-22222_FOV_BORESIGHT = ( 0.0 0.0 1.0 )
INS-22222_FOV_BOUNDARY_CORNERS = ( 0.0 1.0 4.0
2.0 0.0 4.0 )
INS-22222_FOV_SHAPE = 'ELLIPSE'
INS-22222_FOV_FRAME = 'FRAME_FOR_INS-22222'
INS-22222_FOV_BORESIGHT = ( 0.0 0.0 1.0 )
INS-22222_FOV_CLASS_SPEC = 'ANGLES'
INS-22222_FOV_REF_VECTOR = ( 0.0 1.0 0.0 )
INS-22222_FOV_REF_ANGLE = 14.03624347
INS-22222_FOV_CROSS_ANGLE = 26.56505118
INS-22222_FOV_ANGLE_UNITS = 'DEGREES'
Specifying boundary vectors explicitly:
Specifying half angular extents of the FOV:

## Slide 15: Rectangular Field of View
Consider an instrument with a rectangular field of view.
Boundary Corner Vectors
Boresight Vector
Instrument
X
Y
Z
(0,0,0)
(2,1,4)
(-2,1,4)
(-2,-1,4)
(2,-1,4)
Y
X
14.03 O
26.57 O
Subtended field of view angle
14.03 = arc tan (1/4)
26.57 = arc tan (2/4)

## Slide 16: Rectangular FOV Definition
The following sets of keywords and values describe this rectangular field of view:
INS-33333_FOV_SHAPE = ’RECTANGLE'
INS-33333_FOV_FRAME = 'FRAME_FOR_INS-33333'
INS-33333_FOV_BORESIGHT = ( 0.0 0.0 1.0 )
INS-33333_FOV_BOUNDARY_CORNERS = ( 2.0 1.0 4.0
-2.0 1.0 4.0
-2.0 -1.0 4.0
2.0 -1.0 4.0 )
INS-33333_FOV_SHAPE = ’RECTANGLE'
INS-33333_FOV_FRAME = 'FRAME_FOR_INS-33333'
INS-33333_FOV_BORESIGHT = ( 0.0 0.0 1.0 )
INS-33333_FOV_CLASS_SPEC = 'ANGLES'
INS-33333_FOV_REF_VECTOR = ( 0.0 1.0 0.0 )
INS-33333_FOV_REF_ANGLE = 14.03624347
INS-33333_FOV_CROSS_ANGLE = 26.56505118
INS-33333_FOV_ANGLE_UNITS = 'DEGREES'
Specifying boundary vectors explicitly:
Specifying half angular extents of the FOV:

## Slide 17: Polygonal Fields of View
Consider an instrument with a trapezoidal field of view.
Boundary Corner Vectors
Boresight Vector
Instrument
X
Y
Z
(0,0,0)
(1,1,4)
(-1,1,4)
(-2,-1,4)
(2,-1,4)

## Slide 18: Polygonal FOV Definition
The following sets of keywords and values describe this polygonal field of view:
INS-44444_FOV_SHAPE = 'POLYGON'
INS-44444_FOV_FRAME = 'FRAME_FOR_INS-44444'
INS-44444_FOV_BORESIGHT = ( 0.0 0.0 1.0 )
INS-44444_FOV_BOUNDARY_CORNERS = ( 1.0 1.0 4.0
-1.0 1.0 4.0
-2.0 -1.0 4.0
2.0 -1.0 4.0 )
Specifying boundary vectors explicitly:
Polygonal FOV cannot be specified using half angular extents

## Slide 19: Backup
IK file example
Computing angular extents from corner vectors returned by GETFOV

## Slide 20
Low Energy Magnetospheric Measurements System 1 (LEMMS1)
Since the MIMI_LEMMS1 detector's FOV is circular and it's diameter is 15.0
degrees, looking down the X-axis in the CASSINI_MIMI_LEMMS1 frame, we have:
(Note we are arbitrarily choosing a vector that terminates in the Z=1
plane.)
^ Y
| ins
|
| /|
| / |
| / |
| / o |
|/ 7.50 |
x--------------->
X \ | Z
ins \ | ins
\ |
\ |
\|
|-- 1.0 --|
Sample IK Data
The following LEMMS1 FOV definition was taken from the Cassini MIMI IK (cas_mimi_v11.ti):
continues

## Slide 21
The Y component of one 'boundary corner' vector is:
Y Component = 1.0 * tan ( 7.50 degrees )
= 0.131652498
The boundary corner vector as displayed below is
normalized to unit length:
\begindata
INS-82762_FOV_FRAME = 'CASSINI_MIMI_LEMMS1'
INS-82762_FOV_SHAPE = 'CIRCLE'
INS-82762_BORESIGHT = (
0.0000000000000000 0.0000000000000000 +1.0000000000000000
)
INS-82762_FOV_BOUNDARY_CORNERS = (
0.0000000000000000 +0.1305261922200500 +0.9914448613738100
)
\begintext
FOV definition from the Cassini MIMI IK (continued):
Sample IK Data

## Slide 22: Circular FOV Angular Size
The angular separation between the boundary corner vector and the boresight is the angular size.
FORTRAN EXAMPLE
C Retrieve FOV parameters.
CALL GETFOV(-11111, 1, SHAPE, FRAME, BSGHT, N, BNDS)
C Compute the angular size. ANGSIZ = VSEP( BSGHT, BNDS(1,1) )
C EXAMPLE
/* Define the string length parameter. */
#define STRSIZ 80
/* Retrieve the field of view parameters. */
getfov_c(-11111, 1, STRSIZ, STRSIZ, shape, frame,
bsght, &n, bnds);
/* Compute the angular separation. */
angsiz = vsep_c( bsght, &(bnds[0][0]));

## Slide 23: Elliptical FOV Angular Size - 1
The angular sizes are the angular separations between the boresight and the boundary vectors.
FORTRAN EXAMPLE
C Retrieve the FOV parameters from the kernel pool. CALL GETFOV(-22222, 2, SHAPE, FRAME, BSGHT, N, BNDS)
C Compute the angular separations. ANG1 = VSEP( BSGHT, BNDS(1,1) )
ANG2 = VSEP( BSGHT, BNDS(1,2) )
C The angle along the semi-major axis is the larger
C of the two separations computed.
LRGANG = MAX( ANG1, ANG2)
SMLANG = MIN( ANG1, ANG2)

## Slide 24: Elliptical FOV Angular Size - 2
C EXAMPLE
/* Define the string length parameter. */
#define STRSIZ 80
/* Retrieve the FOV parameters from the kernel pool. */
getfov_c(-22222, 2, STRSIZ, STRSIZ, shape, frame,
bsght, &n, bnds);
/* Compute the angular separations. */
ang1 = vsep_c( bsght, &(bnds[0][0]));
ang2 = vsep_c( bsght, &(bnds[1][0]));
/* The angle along the semi-major axis is the larger of the
two separations computed. */
if ( ang1 > ang2 ) {
lrgang = ang1; smlang = ang2; }
else {
lrgang = ang2; smlang = ang1; }

## Slide 25: Rectangular FOV Angular Size - 1
The angular extents of the FOV are computed by calculating the angle between the bisector of adjacent unit boundary vectors and the boresight.
Instrument
(0,0,0)
Bisectors
sml_ang
lrg_ang
Subtended field of view
angles

## Slide 26: Rectangular FOV Angular Size - 2
FORTRAN EXAMPLE
C Retrieve FOV parameters from the kernel pool.
CALL GETFOV(-33333, 4, SHAPE, FRAME, BSGHT, N, BNDS)
C Normalize the 3 boundary vectors CALL UNORM(BNDS(1,1), UNTBND(1,1), MAG)
CALL UNORM(BNDS(1,2), UNTBND(1,2), MAG)
CALL UNORM(BNDS(1,3), UNTBND(1,3), MAG)
C Compute the averages.
CALL VADD(UNTBND(1,1), UNTBND(1,2), VEC1)
CALL VSCL(0.5, VEC1, VEC1)
CALL VADD(UNTBND(1,2), UNTBND(1,3), VEC2)
CALL VSCL(0.5, VEC2, VEC2)
C Compute the angular separations
ANG1 = VSEP( BSGHT, VEC1 )
ANG2 = VSEP( BSGHT, VEC2 )
C Separate the larger and smaller angles. LRGANG = MAX( ANG1, ANG2)
SMLANG = MIN( ANG1, ANG2)

## Slide 27: Rectangular FOV Angular Size - 3
C EXAMPLE
/* Define the string length parameter. */
#define STRSIZ 80
/* Retrieve the FOV parameters from the kernel pool. */
getfov_c(-33333, 4, STRSIZ, STRSIZ, shape, frame,
bsght, &n, bnds);
/* Normalize the 3 boundary vectors. */
unorm_c(&(bnds[0][0]), &(untbnd[0][0]), &mag);
unorm_c(&(bnds[1][0]), &(untbnd[1][0]), &mag);
unorm_c(&(bnds[2][0]), &(untbnd[2][0]), &mag);
/* Compute the averages */
vadd_c(&(untbnd[0][0]), &(untbnd[1][0]), vec1);
vscl_c(0.5, vec1, vec1);
vadd_c(&(untbnd[1][0]), &(untbnd[2][0]), vec2);
vscl_c(0.5, vec2, vec2);
/* Compute the angular separations. */
ang1 = vsep_c( bsght, vec1);
ang2 = vsep_c( bsght, vec2);
/* Separate the larger and smaller angles. */
if ( ang1 > ang2 ) {
lrgang = ang1; smlang = ang2; }
else {
lrgang = ang2; smlang = ang1; }