## Slide 1: Summary of Key Points
October 2007

## Slide 2: Which Pieces Do I Use?
There’s no single answer
  Depends on what task you wish to accomplish
  Depends on what mission you are working on
The next several charts highlight some key points
  We assume you have already looked at the major SPICE tutorials, or already have some familiarity with SPICE.
  We assume you have successfully downloaded and installed the SPICE Toolkit.
Consider printing this tutorial and keeping it near your workstation

## Slide 3: Reminder of Key Subsystems
SPK: Position (and velocity) of things
PCK: Size/shape/orientation of target bodies
IK: Instrument field-of-view geometry
CK: Orientation of spacecraft or spacecraft structures that move
FK: Definition/specification of non-core reference frames
LSK: UTC (SCET) ET time conversions
SCLK and LSK: SCLK ET time conversions

## Slide 4: Primary Kernel Interfaces - 1
SPK
PCK
IK
CK
FK
LSK
SCLK
EK/ESQ
SPKEZR, SPKPOS,
SPKCOV, SPKOBJ
SXFORM, PXFORM,
SPKEZR, SPKPOS,
BODVRD
G*POOL, GETFOV
SXFORM, PXFORM
SPKEZR, SPKPOS,
CKCOV, CKOBJ
(CKGPAV, CKGP)
STR2ET, TIMOUT
SCS2E, SCE2S
SXFORM, PXFORM,
SPKEZR, SPKPOS
EKFIND, EKG*
Notes: FURNSH is used to load (provide access to ) all SPICE kernels.
API names shown are for FORTRAN versions:
- use lower case and add an “_c” when using C
- use lower case and prepend “cspice_” when using Icy (IDL) and Mice (MATLAB)
Which SPICE interface modules are most commonly called to use the data from a given kernel type?
SXFORM, PXFORM,
SPKEZR, SPKPOS

## Slide 5: Primary Kernel Interfaces - 2
Module Name | SPK | PCK | IK | CK | FK | LSK | SCLK
SPKEZR, SPKPOS | Y | M |  | M | M | M | M
SXFORM, PXFORM | M | M |  | M | M | M | M
CKGP, CKGPAV |  | M |  | Y | M | M | M
GETFOV |  |  | Y |  |  |  | 
G*POOL |  |  | M |  |  |  | 
STR2ET, TIMOUT |  |  |  |  |  | Y | 
SCS2E, SCE2S |  |  |  |  |  | Y | Y
CHRONOS (time conversion app.) | M | M |  | M | M | Y | M
Yes = the indicated kernel type is needed
Maybe = the indicated kernel type may be needed
For a given module, which kind(s) of kernel(s) will or may be needed?
Kernel Type(s) Needed

## Slide 6: Kernel “Coverage” Cautions
Your set of kernels must:
  contain data for all “objects” of interest
    Sometimes you must include intermediary objects that provide a connection
  contain data covering the time span of interest to you
    Watch out for data gaps within that time span
    Watch out for the difference of ~65 seconds between ET and UTC
  contain all the kernel types needed by SPICE to answer your question
    As the previous charts allude, you may need one or more kernels that are not obvious
  be managed (loaded) properly if there are overlapping (competing) data within the set of files you are using

## Slide 7: How Can I Find Possibly Useful Toolkit Modules?
Review the previous charts
Look at the appropriate SPICE tutorial(s)
Look at the “Most Useful SPICELIB Subroutines” document …/doc/html/info/mostused.html
Search the permuted index:
  spicelib_idx for the FORTRAN toolkits …/doc/html/info/spicelib_idx.html
    (This document also correlates entry point names with source code files)
  cspice_idx for the C and Icy toolkits …/doc/html/info/cspice_idx.html
Read relevant portions of a SPICE “required reading” reference document (e.g. “spk.req)
  …/doc/html/req/spk.html for the hyperlinked html version (best)
  …/doc/spk.req for the plain text version

## Slide 8: How Can I Understand How To Use Those Modules?
The primary user-oriented documentation about each module is found in the “header” at the top of each source code file
  (More documentation is found at the additional entry points for those FORTRAN modules that have multiple entry points.)
Reference documentation for major subsystems is found in like-named “required reading” documents (e.g. spk.req, ck.req, etc.)
The SPICE tutorials contain much helpful information
See “SPICE Documentation Taxonomy” in the tutorials collection for additional reading suggestions

## Slide 9: Does NAIF Provide Any Examples?
Nearly all module headers contain one or more working examples
“Most Useful SPICELIB Subroutines” has code fragments …/doc/html/info/mostused.html
The “required reading” reference documents often contain examples …/doc/html/req/index.html
Three tutorials offer programming examples
Some simple “cookbook” programs are found in the Toolkit …/src/cookbook/…
Make use of the SPICE Programming Lessons available from the NAIF server
  ftp://naif.jpl.nasa.gov/pub/naif/toolkit_docs/Lessons/