## Slide 1: Shape Model Preview An overview of Current Status of and Further Development Plans for the SPICE Digital Shape Kernel Subsystem (DSK)
October 2007

## Slide 2: SPICE DSK Topics
Overview
Requirements
DSK Data Representations
DSK System Components
DSK Software Components
DSK API Examples
Using Shape with Orientation Data
DSK Development Status

## Slide 3: Overview
NAIF is developing a new SPICE kernel type: DSK (“digital shape kernel”)
  When completed, the DSK system will be incorporated into the SPICE Toolkit.
The SPICE DSK system deals with data sets describing topography of solar system objects, or more generally, shapes of 3-dimensional objects. Examples:
  Digital elevation models (DEM) for the surfaces of Mars or the Moon
  Tessellated plate model for the surface of a natural satellite, asteroid or comet nucleus
  Horizon masks for DSN stations
The DSK system facilitates high-accuracy, SPICE-based geometric computations using shape data
  Currently SPICE uses only triaxial ellipsoid shape models, which support low-accuracy computations
The DSK system comprises
  The DSK data file format
  Software (subroutines and programs)
  Documentation

## Slide 4: Requirements -1
All “requirements” listed here are of an informal nature; they are derived from customer interaction and NAIF team members’ experience using SPICE.
Overall requirement: facilitate high-accuracy geometry computations involving surfaces of extended bodies. Examples of computations that should be supported:
    Location of “sub-observer point” and height of observer above surface
    Ray-surface intercept point
    Occultation/transit state of a point target
    Limb and terminator location
    Illumination angles at a specified surface point
    Determine if a target is in an instrument’s field of view (FOV)

## Slide 5: Requirements -2
System should support popular shape representations
  For example: DEM, triangular plates
System should support efficient random access data search
  For example: for a given (LONGITUDE, LATITUDE) coordinate pair, return radius (distance from body center) of the corresponding surface point
System should support rapid, high volume data extraction (“bulk read”)
  Required for efficient use by graphics applications
System should be able to use data sets spread across multiple files
  Some current data sets exceed 2Gbytes in size
  Larger data sets should be expected in the future
  Impractical to store all needed data in one file
System should be able to work with models for different bodies simultaneously.
  For example: support simultaneous use of data sets for Mars and Phobos.

## Slide 6: Requirements -3
System should be able to work with multiple models for different parts of the surface of a specified body simultaneously.
  Support simultaneous use of multiple data sets having different resolutions, or event different mathematical representations, for different regions of the surface.
Data files should be portable
Data files should support inclusion of metadata
Tools should be provided for
  Summarizing contents of data files
  Accessing metadata in data files
  Merging or subsetting data files
  Ingesting data from other types of files
    For example: Bob Gaskell’s and Peter Thomas’ shape models

## Slide 7: DSK Data Representations -1
Digital elevation model (DEM)
  Maps longitude/latitude to “elevation”
    Elevation of a surface point can be defined as distance from the origin of a body-fixed reference frame
    Elevation can be defined as height above a reference ellipsoid
  Example: image created from MGS laser altimeter (MOLA) Mars DEM

## Slide 8: DSK Data Representations -2
Plate model
  Surface of object is represented as a collection of triangular plates
  More flexible than digital elevation model: arbitrary 3-D surface can be modeled
    Surface could be a complicated shape with multiple surface points having the same latitude and longitude
      Examples: “dumbbell”-shaped asteroid, caves, arches
  Less efficient than digital elevation model of similar resolution in terms of storage and computational speed
Example images created from DSK plate models (center and right images are based on Phobos data)

## Slide 9: DSK Data Representations -3
DSK shape representations are polymorphic:
  DSK shape representations are called “Data Types.”
  Each data type has its own mathematical representation of a surface
  Each data type has associated software that implements common functionality, such as the ability to return a radius (distance of surface point from body center) value for a specified latitude and longitude.
  Each data type may have additional, unique functionality.
    For example, type 2 has accessor routines that return plate and vertex data. These functions are not applicable to other data types.
DEM packed 16-bit integer radius data with scale factor and offset
Type 1
Type 2
TRIANGULAR PLATE MODEL
DSK Shape Data
Type 3
DOUBLE PRECISION RADIUS DATA
Type 4
DEM packed 16-bit integer radius data with scale factor and offset---stereographic projection
…

## Slide 10: DSK System Components
DSK Files
  Use the SPICE DAS file architecture
    Binary, direct access
    System-independent buffering built in
    Comment area built in
DSK Software
  SPICE software which enables users to create and use DSK kernels
    Writer routines
    Reader routines
    High-level API routines
      For example: routines dealing with observer-target geometry
    Supporting utility programs
DSK Documentation
  Tutorial
  Required Reading file
  Module headers

## Slide 11: DSK Software Components -1
Writers
  Routines that enable a SPICE-based application to create a DSK kernel
    Open new DSK kernel for write access
    Open existing DSK kernel for write access
    Start new DSK segment (“segments” are partial DSK data sets containing data for a given region on a specified object)
    Add data to DSK segment
Readers
  Routines that extract data from a DSK file
    Return elevation of surface at given longitude/latitude
    Return specified attributes, for example the surface normal vector, for a specified longitude and latitude
    Rapidly obtain data for large portion of surface (“bulk read”)
    Return DSK attributes such as number of plates, pixel size, min/max elevation, etc.
High-level functions (including, but not limited to, the following):
  Compute sub-observer point on surface and height of observer above surface
  Compute intercept of ray with surface
  Determine whether a portion of a target body’s surface is within the FOV of specified instrument at specified time.
  Determine occultation/transit state of a point target
  Compute limb and terminator location
  Compute Illumination angles at a specified surface point

## Slide 12: DSK Software Components -2
Utility programs that
  Create DSK files: import other surface shape data sets into SPICE DSK format
  Port DSK files
  Provide comment area access
  Summarize DSK file contents
  Subset or merge DSK files
  Downsample DSK files
  Convert one DSK data type to another
    Example: create type 2 DSK file from type 1

## Slide 13: DSK API Examples
Get radius at surface point (inputs are in red, outputs in blue):
  CALL DSKRAD ( TARGET, LON, LAT, RADIUS )
    Inputs: target body name, longitude and latitude of point of interest
    Output: radius (distance from target center) at surface point
Find sub-observer point on target:
  CALL SUBPT ( METHOD, TARGET, ET, ABCORR, OBSRVR, SPOINT, ALT )
    SUBPT is a generic, high-level API. SUBPT doesn’t assume the surface is modeled by a DSK.
    Input “METHOD” indicates surface model and sub-point definition
      For ellipsoids, METHOD may be set to ‘near point’ or ‘intercept’
      For DSKs, set METHOD to ‘DSK intercept’, indicating that the sub-point is defined as the closest intersection to the observer of the observer-target center ray with the surface, and DSK model is to be used.
      Note that SPICE should not assume DSK is to be used just because a DSK for the target body is loaded; may be too inefficient for some applications. Caller must say which model is to be used.
    Other inputs: target body name, epoch, aberration correction, observer name.
    Outputs: sub-observer point in Cartesian coordinates, expressed in the body-fixed frame associated with the target, and altitude of the observer above the sub-point.

## Slide 14: Using Shape with Orientation Data
MKPLAT
Program
(SPICE Toolkit)
Tessellated Plates
Shape Model
Lists of plate model vertices and associated plates, and optionally, albedo data for each plate
Planetary constants
kernel containing rotation data for the body, and possibly
tri-axial shape
Some source of rotation state information (pole RA/DEC and prime meridian location)
Text editor
(Usually done by NAIF)
Text editor
(Usually done by NAIF)
Program to
make a DSK
(SPICE Toolkit)
Digital Terrain
Shape Model
Triaxial Ellipsoid
Shape Model
Axes dimensions for tri-axial ellipsoid
LAT/LON and height
above ellipsoid or
distance from center
of frame
Digital
shape kernel
Your application program
for science data analysis
spicelib,
cspice,
Icy or
Mice
SPICE routines for obtaining rotation state and shape, and then computing derived quantities
DSK
PCK

## Slide 15: DSK Development Status
History
  Precursor “Plate Model” system was delivered to NEAR and Hayabusa and used successfully on those missions
  A prototype version of the DSK system was delivered to the DAWN project in November 2006. This software has been integrated into the SOA (Science Opportunity Analyzer) program.
    SOA uses DSK files to import shape model data for Vesta and Ceres.
    SOA also uses DSK software, along with custom, higher-level DSK-based software provided by NAIF, to perform geometric computations involving target body shape data.
Plans
  NAIF is currently developing the deliverable DSK system.
  NAIF plans to release an alpha-test version of the DSK system within six months.
  Release date of SPICE Toolkit including the DSK system is TBD.