## Slide 1: SPICE Event Finding Subsystem
October 2007

## Slide 2: Topics
Overview
Eclipse Events
Occultation Events
Field-of-View Events
Numeric Events
Window Math

## Slide 3: Overview
The NAIF team is working to add a new subsystem to the SPICE Toolkits. This subsystem is designed to identify the times or time intervals of particular geometric events.
  CSPICE, Icy, and Mice will include some or all event finding functionality.
The event subsystem algorithms detect four types of events:
  Eclipse
  Occultation
  Field-of-View
  Numerical
The first three types describe a specific set of geometric conditions identified with the corresponding type name. The fourth type describes a geometric quantity satisfying a numeric relationship.
NAIF has not determined a release date for the subsystem.

## Slide 4: Eclipse -1
The eclipse detection algorithm identifies twelve eclipse configurations (as observed from the eclipsed body).
Eclipse models assume a spherical shape for eclipser and eclipsed bodies. A sphere or point object can represent the illumination source.

## Slide 5: Eclipse - 2
1
2
3
4
6
5
Eclipsed body
Eclipser body
Spherical illumination source
1: Eclipsed body in full illumination
2: Eclipsed body partially illuminated, partially in the penumbra
3: Eclipsed body exclusively in the penumbra
4: Eclipsed body completely in the umbra (NAIF defines this state as also in the penumbra.)
5: Eclipsed body fully in penumbra with complete umbral shadow on body
6: Eclipsed body partially in penumbral and partially in umbral regions

## Slide 6: Eclipse - 3
9
8
7
7: Eclipsed body partially illuminated with the penumbral shadow completely on body, no umbral shadow
8: Eclipsed body in illuminated, penumbral, and umbral regions with full umbral shadow on body
9: Eclipsed body in illuminated, penumbral, and umbral regions without full umbral shadow on body
Eclipsed body
Eclipser body
Spherical illumination source

## Slide 7: Eclipse - 4
10
10: Eclipsed body partially illuminated with the penumbral and umbral shadows both fully on body
Eclipsed body
Eclipser body
Spherical illumination source

## Slide 8: Eclipse - 5
11
12
Eclipsed body
Eclipser body
Point illumination source
11: Eclipsed body partially illuminated with full umbral shadow on body, no penumbral shadow
12: Eclipsed body partially illuminated, partially in the umbra shadow, no penumbral shadow
Note, these configurations exist only for point illumination sources.
+
+

## Slide 9: Occultation
The occultation detection algorithm identifies configurations with a triaxial ellipsoid modeling the occulting body. A triaxial ellipsoid or point object models the occulted body.
Full
Point
Annular
Partial
A point target occulted by a spheroid.
A spheroid partially occulting a second spheroid.
A spheroid fully occulting a second spheroid.
A smaller spheroid passing between a second, larger spheroid and the observer.
Occulted body
Occulting body

## Slide 10: Field-of-View
The field-of-view detection algorithm identifies configurations where an instrument field-of-view intersects or contains a body of interest. The instrument’s field-of-view properties are defined in a SPICE instrument kernel.
  The field-of-view detection algorithms answer questions of the form:
    “Given a time interval [t1, t2] and a body, at what times within [t1, t2] does the body intersect the instrument field-of-view?” (Can I see it, if so, when?)
  In order to answer questions of the form:
    “Given a time interval [t1, t2] and a set of bodies, which bodies will intersect the instrument field-of-view across [t1, t2]?” (What can I see?)
    The user performs a field-of-view search over [t1, t2] for each body.

## Slide 11: Numeric - 1
The numerical event detection algorithms identify configurations where a particular scalar geometric quantity satisfies some relationship, as defined by an operator and a reference value, or a unary operator.
Geometric quantities:
  Angular separation: observed angular separation between limbs
  Angular speed: magnitude of angular velocity of apparent target about an observer
  Angular rate: the time derivative of the apparent angular separation
  Apparent angular diameter
  Range: ||r||
  Range rate: d(||r||)/dt
  Elongation angle: Sun-observer-target angle
  Phase angle: observer-target-Sun angle
  Coordinate: an element of the position vector in a particular coordinate system and reference frame. The position vector is defined as either “observer to target” or “sub observer point on target.”
    Coordinate systems and the corresponding coordinates:
      RECTANGULAR: X, Y, Z
      CYLINDRICAL: RANGE, LONGITUDE, Z
      GEODETIC: LONGITUDE, LATITUDE, ALTITUDE
      LATITUDINAL: RANGE, LONGITUDE, LATITUDE
      RA/DEC: RANGE, RIGHT_ASCENSION, DECLINATION
      SPHERICAL: RANGE, COLATITUDE, LONGITUDE
Continued on the next page

## Slide 12: Numeric - 2
Applicable operators:
  > (quantity > reference_value)
  = (quantity = reference_value)
  < (quantity < reference_value)
  ABSMAX ( quantity )
  ABSMIN ( quantity )
  LOCMAX ( quantity )
  LOCMIN ( quantity )
Examples of detectable events using a numeric event search:
  periapsis or closest approach
    minimum distance between a body and center or between two bodies
  apoapsis
    maximum distance between a body and center
  pointing constraints
    angular separation between the look direction and Sun direction
  boundary confinement
    a vehicle sub-point on a body lies within a latitude/longitude range
  node crossings
    Z coordinate of a body position in equator based frame equals zero

## Slide 13: Windows Math
The events subsystem uses the SPICE windows data type as an input, named the confinement window, to define the time intervals to search. A window is also used as an output, named the result window, during which the event of interest occurs.
  Windows are collections of zero or more ordered, disjoint intervals of double precision numbers. The event finder subsystem uses windows to define the initial search times and final result times.
  The Toolkit contains a family of routines for creating windows and performing “set arithmetic” on them (union, intersection, difference, etc.).
This windows based implementation allows a user to perform multiple searches where the window result of one search is used as the input (confinement) for the next, either to satisfy a restriction on multiple conditions or as a refinement process.
  Note, the physics of a multi-event geometry may be such that the search for one event will proceed faster than another and markedly reduce the measure of the search space for the next search.

## Slide 14: Example - 1
Time interval for which the subpoint of a vehicle passes through a latitude/longitude “box.”
Search first for time intervals with the restriction on the subpoint latitude, then use the result window as the confinement window for a restriction search on the subpoint longitude.

## Slide 15: Example - 2
Time intervals for which an orbiter passes in line-of-sight of a station, with a local elevation above 30 degrees, with a maximum distance of 30000 km.
Search first for time intervals where station-target distance is less-than 30000 km then use that result window as the confinement window for a search to determine when elevation is greater-than 30 degrees.