## Slide 1: Making an SPK File
October 2007

## Slide 2: Table of Contents
Purpose
Scope
Assumptions about user’s knowledge
SPK overview
Summary of SPK architecture
Discussion applicable to all production methods
  Recommended SPK types
Selecting the polynomial degree (for polynomial SPK types)
SPK production methods
  Using the “Make SPK” (MKSPK) program
  Using SPICELIB, CSPICE or IDL writer modules (subroutines)
Finishing up, applicable to all methods
  Adding comments
  Validation
  Merging
Special requirements for making SPKs to be used in DSN/NSS metric predicts or short-range scheduling
  Applies only to those entities not making JPL NAV-style “p-files”
Issues affecting performance (reading efficiency) and usability

## Slide 3: Purpose
This tutorial provides guidance for producing (writing) an SPK file using software provided by NAIF:
  the MKSPK application program
  or
  SPK writer modules from the SPICELIB (FORTRAN) or CSPICE (C-language) library, or from the Icy (IDL) system
    Only partial implementation in Icy
    No SPK writers implemented in Mice

## Slide 4: Scope
This tutorial addresses production of SPK files.
  For general purposes.
  For use with NASA’s Deep Space Network (the “NSS”).
    For antenna scheduling purposes.
    For operational metric predicts (tracking) using currently operational DSN software systems.
      It does not address the presumably less restricted case of metric predicts production once new DSN SPS software is in use.
        SPS is planned for full operational deployment around June 2006.
This tutorial does not address SPK production by JPL NAV teams using the NIOSPK application, which was specially built to process JPL’s NAVIO-format ephemeris/trajectory files.
  Those NAV teams may simply learn how to use the NIOSPK program and any useful SPK-related utilities.

## Slide 5: Background Assumptions
It is assumed the reader has some familiarity with the SPICE system, and with basic ideas of orbital mechanics.
  The SPICE Overview tutorial is available at:
  ftp://naif.jpl.nasa.gov/pub/naif/toolkit_docs/Tutorials/pdf/individual_docs/xx_SPICE_overview.pdf
It is assumed the reader has read the “SPK Tutorial” that characterizes much of the SPK subsystem, but with emphasis on reading SPK files.
  The SPK “reading” tutorial is available at:
  ftp://naif.jpl.nasa.gov/pub/naif/toolkit_docs/Tutorials/pdf/individual_docs/xx_spk.ppt
It is assumed the reader has available the SPK reference document entitled “SPK Required Reading,” supplied with each copy of the SPICE Toolkit (.../doc/spk.req)
  SPK Required Reading is also available at:
  http://naif.jpl.nasa.gov/naif/documentation.html

## Slide 6: SPK References
References for SPK production
  “Making an SPK” tutorial (this document)
  “SPK (Ephemeris System)” tutorial (focused on reading an SPK)
  “SPK Required Reading” (spk.req)
  “MKSPK Users Guide” (mkspk.ug)
  “SPKMERGE User’s Guide (spkmerge.ug)
  The source code “headers” provided as part of the SPK writer modules (subroutines)

## Slide 7
Brief Overview - 1
Understand the physics of your data and how that relates to SPK type.
  Type 5 implies an orbit well approximated by a sequence of one or more conic orbits.
  Types 9 and 13 fit data regardless of the expected physics.
    Caution: a good fit in the mathematical realm may not respect the physics of the trajectory. For example, fitting polynomials to an excessively sparse set of states for a planetary orbiter could result in an interpolated path that intersects the planet.

## Slide 8
Brief Overview - 2
Ordinarily, use the NAIF mkspk application to create SPKs from Cartesian state data or conic elements.
  Depending on your source data, SPK types 5, 9, 10, and 13 will satisfy the requirements for most users.
    Type 5, yields compact SPK files when the trajectory is well approximated by piecewise two-body motion. May be the best choice for planetary or solar orbiters when available state data are sparse.
    Type 9, a good, general choice
    Type 13, when you have very accurate velocity data
    Type 10 applies ONLY to Two Line Element Sets (TLEs).
Alternatively, use the Toolkit’s SPK writing subroutines in your own production program.
Caution: an SPK made for DSN metric predicts has special requirements, discussed later on.

## Slide 9: Summary of SPK Architecture

## Slide 10: SPK File Structure - Pictorial
This is a logical view of SPK file organization. A real SPK file is a binary, direct access file built upon a SPICE data structure known as the Double Precision Array File (DAF).
Using the DAF architecture and binary direct access method, including buffering, provides rapid look-up of the data needed to fulfill a read request, whether the data requests are sequential or random with respect to file organization.
Logical Organization
of an SPK File
[ ] = second or more
segments used as needed
Internal file name
Comment area
(Metadata)
Segment 1
.
.
.
[Segment N]

## Slide 11: SPK Detailed File Structure
File record: always present.
Comment area (variable number of records )
D27
The comment area may be empty.
An SPK file has at least one descriptor record and one segment ID ("name") record. These records contain up to 25 pairs of segment descriptors and segment IDs.
ND, NI: Number of d.p. and integer descriptor components
IFNAME: Internal file name
FWD, BWD: Forward and backward linked list pointers
FREE: First free DAF address
BFF: Binary file format ID
FTP: FTP corruption test string
DN: Descriptor for segment N
IN: Segment ID for segment N
N/P/C: Next, previous record pointers and descriptor count
U: Unused space
U*: Possibly unused space
Descriptor record
Segment ID ("Name") record
D1
D2
…
I2
…
Segment 1 (variable number of records )
Segment 2 (variable number of records )
N/P/C
I1
U
Descriptor record
Segment ID ("Name") record
…
…
Segment 26 (variable number of records )
Segment 27 (variable number of records )
N/P/C
U
I27
D26
I26
Records are fixed-length: 1024 bytes on all currently supported platforms.
U*
Segment 25 (variable number of records )
.
.
.
D25
I25
U*
U*
U*
…
Example: SPK file with 27 or more segments
U*
…
…
…
ID WORD
IFNAME
ND
NI
FWD
BWD
FREE
BFF
FTP
0 PAD
0 PAD
Diagram not to scale.
.
.
.

## Slide 12: SPK File Structure - Description
File record
  Contents
    Internal file name (set by file creator)
    Architecture and binary file format identifiers
    File structure parameters
    FTP transmission corruption detection string
  Used by SPK reader and writer subroutines
Comment Area
  A place where “metadata” (data about data) may be placed to help a user of the SPK file understand the circumstances of its production and any recommendations about for what uses it was intended
Descriptor record
  One of these is needed for every collection of 1-to-25 segments
Segment[s]
  Collection[s] of ephemeris data
    Minimum of one segment
    Maximum:
      The practical maximum is a few thousand segments
      Serious performance degradation occurs above 10000 segments for a single body
      Absolute limits are imposed by the range of the INTEGER data type for your computer
  Numerous SPK types may be used within an SPK file, but only one SPK type may appear within a given segment
  Segments of different types may be intermixed within a given SPK file

## Slide 13: What is an SPK Segment?
A segment is a collection of information:
    providing ephemeris (position and velocity) of a single object
    given relative to a single center of motion
    specified in a single reference frame (one known to SPICE)
    covering a specified, continuous period of time, and
    using a single SPK data type.
  Example: ephemeris for the Voyager 2 spacecraft, relative to the center of the Neptunian system (Neptune’s barycenter), given in the J2000 inertial reference frame, covering a specific period of time, and using the Hermite interpolation with variable length intervals SPK type (type 13)
An SPK segment must contain enough data to yield an object’s state at any epoch within the time bounds associated with the segment
  This has implications that depend on the SPK type being produced

## Slide 14: Discussion applicable to all SPK production methods

## Slide 15: The SPK Family

## Slide 16: Recommended SPK Data Types - 1
SPK type 2 (Chebyshev polynomials for position, velocity given by differentiation) Used at JPL for planetary ephemerides.
SPK type 3 (Separate Chebyshev polynomials for position and velocity) Used at JPL for satellite ephemerides.
SPK type 5 (Weighted two-body extrapolation) Often used for comets and asteroids, as well as for sparse data sets where a two-body approximation is acceptable.
SPK types 9 and 13 (Sliding-window Lagrange and Hermite interpolation of unequally-spaced states) Often used by non-JPL ephemeris producers and by users of NAIF’s “Make SPK” (MKSPK) application.
SPK type 10 (weighted Space Command two-line element extrapolation) Often used for earth orbiters.
SPK type 14 (Separate Chebyshev polynomials for position and velocity, with variable time steps) This is the most flexible Chebyshev data type.
SPK type 15 (Precessing conic elements) Provides a very compact ephemeris representation; limited to orbits where this type of approximation is valid.
SPK type 17 (Equinoctial elements) Most suited for representation of ephemerides of natural satellites in equatorial or near-equatorial orbits.

## Slide 17: Recommended SPK Data Types - 2
Each type has certain properties that may promote or limit its usefulness in a particular application. These properties include, but are not limited to the following.
    Ability to model the actual ephemeris to be represented with the accuracy required for your application.
    Consistency between velocity and derivative of position.
    Evaluation speed (performance).
    Compactness (file size).
    Availability of SPICE software needed to write files of that type.
Users are encouraged to consult with NAIF about the suitability of an SPK type for a particular purpose.

## Slide 18: Creating Multiple SPK Segments
Each SPK segment must have a single object, center of motion, reference frame and SPK data type.
Limiting segment size to 10,000 states or “packets of ephemeris data” can improve performance when searching within a segment.
  Absolute limits on segment size depend on the size of the INTEGER data type.
For good SPK reading performance, the total number of segments for any given body in a file should be kept under the dimension of the SPKBSR segment buffer, currently set to 30,000.
  More details about reading efficiency are provided at the end of this tutorial.
  When reading data from multiple SPK files, a more stringent limit applies: the total number of loaded segments for any body, possibly contributed by multiple files, should be less than the SPKBSR segment buffer size.
  For best efficiency, the total number of segments loaded should be less than this buffer size.
One may elect to initiate a new segment (or more) as the means for modeling a propulsive maneuver.
  This is because the SPK reader modules will NOT allow interpolation over a segment boundary.
When starting a new segment it is suggested, although not required, that you use a new segment identifier.

## Slide 19: Choosing Polynomial Degree
If you make a type 8 or 9 (Lagrange interpolation) or a type 12 or 13 (Hermite interpolation) SPK file you must specify the degree of the interpolating polynomial that the SPK reader subroutine will use.
  This choice needs some consideration about desired accuracy, file size and evaluation speed (performance).
  This choice is also affected by the “smoothness” of the orbit data you wish to represent with an SPK file.
  The allowed range of degree is 1-to-15. In addition, to ensure position and velocity continuity over the time span covered by the orbit data:
    for types 8 and 9, the polynomial degree must be odd.
    for types 12 and 13, the polynomial degree must be 3-mod-4, meaning degree 3, 7, 11 or 15.

## Slide 20: SPK Production Methods

## Slide 21: Choices for Making an SPK File
There are two methods available for making an SPK file.
  Take a data file produced by your own trajectory propagator program and input this into the conversion utility (MKSPK) provided by NAIF that outputs an SPK file.
  Incorporate the appropriate SPK writer modules (subroutines) into your own code.
    Add these routines to your trajectory estimator/ propagator.
    or...
    Write your own “post-processor” conversion utility, similar to MKSPK described above.
Both methods are described in the next few pages.

## Slide 22: Making Your Choice - 1
Using the MKSPK program provided in the Toolkit could be easiest for “simple” situations.
  Provides considerable flexibility for accepting a wide assortment of input data formats.
  Does allow one to make multi-segment SPK files when the target, center of motion, reference frame, or SPK type changes, but not as straight forward as it could/should be.
    Best done through multiple program executions (although one could be tricky and accomplish this in a single execution).
    A future version of MKSPK may better accommodate this.
    Note: production of multiple segments in type 5, 8, 9, 12 and 13 files when the amount of input data requires so, is automatically handled.

## Slide 23: Making Your Choice - 2
Using the SPK “writer” modules found in SPICELIB, CSPICE, and Icy offers the greatest flexibility and user control.
  Using these requires that you write your own program.
  You’ll likely need to use some additional SPICE modules as well.

## Slide 24: Using NAIF’s MKSPK Application Program

## Slide 25: Using the MKSPK Utility - 1
NAIF’s
MKSPK
Program
SPK File
Possible SPK
data types
produced are:
- Type 05
- Type 08
- Type 09
- Type 10
- Type 12
- Type 13
- Type 15
- Type 17
Suitable kinds of input
ephemeris data are:
- Table of Cartesian state vectors
- Table of conic elements
- One or more sets of equinoctial elements
- One or more sets of Space Command two-line elements
ASCII file of
ephemeris
data
Setup file
Optional comment
file

## Slide 26: Using the MKSPK Utility - 2
This table indicates which SPK types
can be made from the four kinds
of input data accepted by MKSPK
Y = Yes N = No

## Slide 27: Using the MKSPK Utility - 3
MKSPK will produce a file consisting of one or more segments as needed.
  It will write up to 10,000 data points in one segment.
  For multi-segment files based on types 5, 8, 9, 12 and 13 the program will repeat sufficient data points at both sides of each interior segment boundary to ensure the SPK file will provide a continuous ephemeris through the segment boundary epoch.
You can use MKSPK to add a new segment to an existing SPK file.
You can use SPKMERGE to merge two or more SPK files made from separate executions of MKSPK.
  It’s important to fully understand how SPKMERGE works if you do this.

## Slide 28: Using the MKSPK Utility - 4
MKSPK does not provide direct/specific means for including propulsive maneuvers within an SPK file.
  Instead, use either of these two methods.
    Append a new SPK segment to an existing SPK file, using MKSPK.
    Merge a collection of SPK files, using SPKMERGE.

## Slide 29: Using SPK “Writer” Modules

## Slide 30: Using SPK Writer Routines
The next several charts outline how to use the“SPK writer” modules available in the Toolkit libraries.
  SPICELIB (FORTRAN)
  CSPICE (C)
    All types supported except Type 1
  Icy (IDL)
    All types supported except Type 1, 15, 17, 18
These routines could be embedded in your existing trajectory propagator program, or they could be used to build a separate conversion program analogous to MKSPK.

## Slide 31: What Routines To Use - 1
SPKOPN Open a new SPK file. (Use
SPKOPA to append to existing file.)
SPKWxx Write a segment of SPK type xx
.
.
[SPKWxx] [ Write more segments ]
. [ Repeat as needed ]
.
SPKCLS Close the file
For all except SPK type 14
[ … ] indicates possible multiple occurrences
These routine names are for the FORTRAN (SPICELIB) Toolkit. For CSPICE
the names are the same but are in lower case and have an “_c” appended. For Icy, module names are case-insensitive and have "cspice_" prepended.

## Slide 32: What Routines To Use - 2
SPKOPN, SPKOPA Open file to add data
SPK14B Begin a new segment
SPK14A Add data to segment
[SPK14A] Add more data
SPK14E End the segment
SPK14B Begin a new segment
SPK14A Add data to segment
[SPK14A] Add more data
SPK14E End the segment
etc.
SPKCLS Close the file
For SPK type 14
[ … ] indicates possible multiple occurrences
Repeat
as needed

## Slide 33: Close the SPK File
Once you have completed the addition of all data to your SPK file, be sure to call the SPKCLS routine to close the file.
  Failure to properly close an SPK file will result in a problem file having been produced.
This point is emphasized here because it has been a frequent problem.

## Slide 34: Finishing Up

## Slide 35: Not Quite Done Yet
You’ve now used either MKSPK or the appropriate SPK writer routines to produce an SPK file. To complete the job you should consider the following.
  Add comments (metadata) to the comment area of the SPK file.
    This could have been done during execution of MKSPK.
    It can be done after the SPK has been created by using the Toolkit’s “commnt” utility program.
  Validate the file before sending it off to your customer.
  Consider if there is a need to merge this newly made SPK file with others.
See the next several charts for more information on these subjects.

## Slide 36: Add Comments (metadata)
It is recommended (but not a technical requirement ) that the producer of an SPK file add to the file, in the “comment area,” appropriate descriptive information.
  When, how and by whom the file was created.
  Intended use for the file.
  Cautions or restrictions on how the file is to be used.
The comments might also include some of these topics.
  Time coverage.
  Ephemeris objects included.
  Type(s) of data used (in the sense of reconstructed versus predicted).
  Any available estimates of accuracy.
  Sources of the data used to produce this SPK file.
  Name(s) of previously generated SPK file(s) being replaced by this file.
  Any knowledge of plans for future updates to (replacements for) this file.
  Name and version number of your SPK production program.
  Type of platform (hardware/OS/compiler) on which the SPK file was generated.

## Slide 37: How to Add Comments to an SPK
Several means are available for adding comments (metadata) to an SPK file.
  An option in the MKSPK program allows comments supplied in a separate text file to be added to the comment area during MKSPK execution.
  Use the “commnt” utility program from the SPICE Toolkit.
    This may be run as an interactive program or in command line mode within a script.
  In FORTRAN and C use APIs.
    Not currently supported in Icy and Mice.

## Slide 38: Validate the SPK File
Validation of SPK files is recommended
  Caution is needed more for one-of-a-kind files than for those generated in a previously tested, unchanging process.
  Some SPICE utility programs might help with this validation.
    The following are under development at NAIF and will become available in the future.
      “CHECKER” - examines the structure and some contents of an SPK file and reports any errors found.
      “CMPSPK2” - reads data from two supposedly similar SPK files and provides statistics on the differences in both position and velocity, mapped into down-track, cross-track and out-of-plane components.
      “DUMP13” - does an ASCII “dump” of a type 9 or type 13 SPK file.
  Consider writing your own validation program.
  Caution: successfully running an SPK summary program (e.g. BRIEF or SPACIT) or successfully running the format conversion program (TOXFR or SPACIT) is a positive sign, but is not a fully sufficient test.

## Slide 39: Validate the Process
When you first start producing SPK files, or when changing the SPK “type” used or the kind of mission (trajectory) to be represented, validation (or revalidation) of the overall process is advised.
  Validation of not only SPKs, but of end products derived from SPKs, is advised.
Consider writing a program that compares states from your source data with states extracted from your new SPK file.
  Do this using interpolated states from your source data–not only the states placed in the SPK file.
  Verify a uniformly good fit on the whole time interval covered by the file.

## Slide 40: Make a Merged SPK File ?
Sometimes it is helpful to customers if portions of two or more SPK files are merged into just one.
  (Sometimes the opposite is true, so be careful!)
If making a merged product is appropriate, use the SPICE utility SPKMERGE.
  Read the SPKMERGE User’s Guide.
    Be especially aware of how SPKMERGE directives affect the precedence order of the data being merged. (This is different from the precedence order that applies when one reads an SPK file or files.)
  Carefully examine your results (probably using either BRIEF or SPACIT) to help verify you got what you expected.

## Slide 41: Get Help
Ask JPL’s NAIF team for assistance with:
  picking the SPK type to be used
  picking the method for producing SPK files
  designing tests to validate the process
Ask NAIF for samples of SPK files from other missions that could help you check your process.

## Slide 42: What SPK Type to Use for Interfaces with the DSN?

## Slide 43: DSN Interface Overview
The version of the DSN “operating system” current as of March 2006 is known as the Network Support System (NSS). This has been in use for many years.
  SPK files intended for use in generating DSN/NSS operational metric predicts and/or short-range scheduling must meet some strict limitations, delineated in the next few pages.
  When the future DSN “operating system” known as the Service Preparation Subsystem (SPS) can be used, many fewer--if any--restrictions on SPK files are expected.
    SPS is expected to become operational around December 2006.
    Consult with DSN staff to determine specific requirements.

## Slide 44: What SPK Type to Use for Interfaces with the DSN/NSS?
For short-term scheduling of DSN antennas, and for producing “metric predicts” that control DSN antennas during tracking operations, limitations in the current end-to-end DSN software system (the “NSS”) restrict the SPK choice to only type 13*.
  See next pages for additional restrictions and recommendations.
Long range SPICE-based scheduling software not associated with the NSS is not restricted to these two SPK types.
  *JPL navigation teams can and always do provide type 1 files. This type is unique to JPL software.

## Slide 45: Restrictions for DSN/NSS Use of Type 13 SPKs
These apply only when the DSN’s “NSS” software will be used
  The SPK must contain data for a single spacecraft
    If the SPK also contains data for natural bodies, it’s ok; these will be ignored
  The maximum size of an acceptable SPK file is limited and must be determined by consulting with the DSN.
    This limitation appears to stem from:
      Disk space limitations on the NSS VAX computer
      Slow CPU of the NSS VAX as compared to modern computers
  The minimum spacing between states must be at least one second.
    This limitation is inherent in the implementation of the NSS metric predicts software and cannot be changed.
  The degree specified for the type 13 polynomials must be 3-mod-4, which means degree 3, 7, 11 or 15.

## Slide 46: Issues Affecting SPK Reading Efficiency
The way you write an SPK file could substantially affect
how quickly your customers will be able to read the file.

## Slide 47: SPK Reading: Efficiency Issues - 1
SPK file creators should design files to support efficient read access.
  This requires knowledge of how SPK file attributes impact efficiency.
When you store "large" amounts (>10^5 states or data packets) of ephemeris data in one or more SPK files, SPK reading efficiency may be affected by:
  SPK segment size
  Number of segments for a body in one SPK file
  Number of segments for a body contributed by multiple SPK files
  The number of loaded segments for all bodies
  The number of loaded files

## Slide 48: SPK Reading: Efficiency Issues - 2
Segment size
  When a segment contains more than 10,000 states or data packets, the SPK readers will generally take longer to search the segment for requested data.
    When the segment is larger than this size, more records are read to look up segment directory information. If these records are not buffered, more physical records are read from the SPK file.
  There is a trade-off between segment size and numbers of segments and files.
    It can be preferable to have large segments rather than have "too many" segments or files. (Read on)

## Slide 49: SPK Reading: Efficiency Issues - 3
Number of segments for a body in one SPK file
  An SPK file MUST not contain more segments for one body than can be "buffered" at one time.
    The SPK reading system buffers coverage descriptions ("segment descriptors") for segments it has examined to satisfy previous requests for state data.
      Don't confuse descriptor buffering with data buffering.
        The SPK reading system also buffers segment DATA, as opposed to segment descriptors, but this is not relevant to this discussion.
    One fixed-size buffer is used for all SPK segments.
      The size of this buffer is given by the parameter "STSIZE," declared in the SPKBSR suite of routines.
      STSIZE is currently set by NAIF to 30,000.
        NAIF recommends that users NOT change this parameter, since maintenance problems may result.
    Unsurprisingly, the system works best when all needed segment descriptors are buffered simultaneously.
continues

## Slide 50: SPK Reading: Efficiency Issues - 4
Number of segments for a body in one SPK file, continued:
    The buffering scheme is "lazy": no descriptors are buffered for segments that haven't been examined.
      But when an SPK file is searched for data for a specified body, descriptor data for ALL segments in the file for that body are buffered.
    The buffering algorithm can "make room" in the buffer by discarding unneeded, buffered descriptor data.
      A "least cost" algorithm decides which buffered data to discard.
    When more buffer room is needed than can be found:
      The SPK reading system reads data directly from SPK files without buffering descriptor information.
      This is NOT an error case: the SPK system will continue to provide correct answers.
      BUT: the system will run VERY SLOWLY.
        This situation is analogous to "thrashing" in a virtual-memory operating system.
        If buffer overflow occurs frequently, the SPK reading system may be too slow to be of practical use.

## Slide 51: SPK Reading: Efficiency Issues - 5
Number of segments for a body contributed by multiple SPK files:
  Buffer overflow can occur if too many segments for one body are contributed by multiple loaded SPK files.
    Overflow can take longer to occur than in the single-SPK case, due to lazy buffering: files that haven't been searched don't consume buffer space.
      Thus an impending overflow problem may not be detected early in a program run.
  User applications can avoid buffer overflow if data are appropriately spread across multiple SPK files.
    Applications can avoid buffer overflow by:
      loading only those files of immediate interest
      unloading files once they're no longer needed

## Slide 52: SPK Reading: Efficiency Issues - 6
Number of segments for all bodies, contributed by all loaded SPK files:
  Buffer overflow does not result from loading SPK files contributing more than STSIZE segments for different bodies.
  However, if the total number of loaded segments for bodies of interest exceeds STSIZE, thrashing can occur as descriptor data are repeatedly discarded from the buffer and then re-read.
    Loaded segments for bodies for which data are not requested do not contribute to the problem.
  For best efficiency, load only files contributing fewer than a total of STSIZE segments for all bodies of interest.
    When more than STSIZE segments are needed, applications should process data in batches: unload files containing unneeded data in order to make room for new files.

## Slide 53: SPK Reading: Efficiency Issues - 7
Number of loaded SPK files:
  Up to 1000 SPK files may be loaded at one time by an application.
    The "1000" limit applies to DAF-based files, so loaded C-kernels and binary PCK kernels count against this limit.
  But loading large numbers of SPK files hurts efficiency:
    Since operating systems usually allow a process to open much fewer than 1000 files, the SPK system must open and close files via the host system's file I/O API in order to provide a "virtual" view of 1000 open files.
      The more such file I/O, the slower an application runs.
    Loading a large number of SPK files could result in a buffering problem if too many segments are loaded for bodies of interest.

## Slide 54: SPK Reading: Efficiency Issues - 8
Recommendations
  Limit segment counts to avoid buffer overflow and thrashing
    Never have more than STSIZE segments for one body in an SPK file and never have more than STSIZE segments for one body loaded simultaneously.
    Don't require users to have more than STSIZE segments loaded at one time.
    If necessary, use larger segments to enable smaller segment counts.
  Consider distributing SPK data across multiple files:
    so as to make selective SPK loading convenient
      facilitate processing data in batches
    so that loading very large numbers of SPK files at once is unnecessary

## Slide 55: SPK Reading: Further Usability Issues
We've discussed reading efficiency in terms of application execution speed; other usability concerns include:
  ease with which files can be transferred between systems
  simplicity of file management required of user applications
  ease with which files of interest can be identified by users, both for current use and in an archival setting