## Slide 1: Making a CK file
October 2007

## Slide 2: Summary
SPICE provides means to create CK files either by packaging orientation computed elsewhere or by first computing orientation and then packaging it in a CK file
Packaging of already existing orientation data can be done in two ways:
  Use SPICE CK writer routines by calling them from within a SPICE-based application
  Convert a text file containing attitude data to a CK using the msopck program
Computing as well as packaging orientation can be done in two ways:
  Use SPICE geometry routines and CK writer routines by calling them from within a SPICE-based application
    Constructing attitude using SPICE routines is not discussed here
  Convert orientation rules and schedules to a CK using the prediCkt program

## Slide 3: CK Writer Routines
The SPICE toolkit provides the following CK writer routines:
  For Type 1 CK
    CKW01 / ckw01_c / cspice_ckw01
  For Type 2 CK
    CKW02 / ckw02_c / cspice_ckw02
  For Type 3 CK
    CKW03 / ckw03_c / cspice_ckw03
  For Type 4 CK
    CKW04B, CKW04A, CKW04E (no CSPICE, Icy, or Mice wrappers)
  For Type 5 CK
    CKW05 / ckw05_c (no Icy or Mice wrapper)
Only the Type 3 writer is discussed in this tutorial
  Writers for Types 1 and 2 have very similar interfaces
  Types 4 and 5 are are not commonly used

## Slide 4: Type 3 Writer - Example
The following code fragment illustrates the creation of a Type 3 C-kernel having a single segment.
ckopn_c ( filename, “my-ckernel”, 0, &handle );
/*
Insert code that properly constructs the
sclkdp, quats, avvs, and starts arrays.
*/
ckw03_c ( handle, begtim, endtim, inst,
“reference_frame”, avflag, “segment_id”,
nrec, sclkdp, quats, avvs, nints, starts );
ckcls_c ( handle );

## Slide 5: Type 3 Writer - ckw03_c (1)
handle - file handle for the newly created C-kernel.
begtim, endtim - start and stop times in SCLK ticks for the segment.
inst - instrument ID code for the C-kernel.
ref - name of the reference or base frame that is known to SPICE.
avflag - a SpiceBoolean indicating whether or not to include angular velocity in the segment.
segid - a string identifying the segment. It should be less than 40 characters in length.

## Slide 6: Type 3 Writer - ckw03_c (2)
nrec - number of records in sclkdp, quats, and avvs.
sclkdp - monotonically increasing list of times, given in SCLK ticks, that identify when quats and avvs were sampled.
quats - a list of SPICE quaternions that rotate vectors from the frame specified by ref argument to the inst frame.
  m2q_c ( C_matrix, quaterion );
avvs - angular rate vectors given in the frame specified by the ref argument.
starts - a list of SCLK ticks indicating the start of interpolation intervals. They must correspond to entries in sclkdp.
nints - number of entries in starts.

## Slide 7: Type 3 writer - Making Up Rates
One of the easiest ways to accomplish this is to assume a constant rotation rate between subsequent quaternions:
for(k=0; k<(nrec-1); k++ ) {
q2m_c ( quats[k][0], init_rot );
q2m_c ( quats[k+1][0], final_rot );
mtxm_c ( final_rot, init_rot, rotmat );
raxisa_c ( rotmat, axis, &angle );
sct2e_c ( scid, sclkdp[k], &init_et );
sct2e_c ( scid, sclkdp[k+1], &final_et );
vscl_c ( angle/(final_et-init_et), axis,
&avvs[k][0] ); }
Then copy the (nrec-1) value of avvs into the last element of avvs.
continues on next page

## Slide 8: Type 3 Writer - Making Up Rates (2)
Constructing angular rates in this fashion assumes that no more than a 180-degree rotation has occurred between adjacent quaternions. In short, raxisa_c chooses the smallest angle that performs the rotation encapsulated in the input matrix.
Other techniques exist, including differentiating quaternions. Care must be exercised when taking that particular approach, however.

## Slide 9: MSOPCK
msopck is a program for making CK files from orientation provided as a time tagged, space-delimited table in a text file
msopck can process quaternions (SPICE and non-SPICE flavors), Euler angles, or matrixes, tagged with UTC, SCLK, or ET
msopck requires all setups to be provided in a setup file that follows the SPICE text kernel syntax
msopck has a simple command line interface with the following usage
  msopck setup_file input_data_file output_ck_file
If output CK already exists, new segment(s) are appended to it

## Slide 10: MSOPCK - Setup File Keywords
LSK_FILE_NAME = 'LSK file'
SCLK_FILE_NAME = 'SCLK file’ (or MAKE_FAKE_SCLK=‘new SCLK file’)
FRAMES_FILE_NAME = 'FRAMES file'
COMMENTS_FILE_NAME = 'file containing comments'
PRODUCER_ID = 'producer group/person name'
INTERNAL_FILE_NAME = 'internal file name string'
CK_SEGMENT_ID = 'segment ID string'
CK_TYPE = 1, 2, or 3
INSTRUMENT_ID = CK ID
REFERENCE_FRAME_NAME = 'reference frame name'
MAXIMUM_VALID_INTERVAL = interval length, seconds
INPUT_TIME_TYPE = 'SCLK', 'UTC', 'TICKS’, ‘DPSCLK’, or ‘ET’
TIME_CORRECTION = bias to be applied to input times, seconds
INPUT_DATA_TYPE = 'MSOP QUATERNIONS', 'SPICE QUATERNIONS',
'EULER ANGLES', or 'MATRICES'
QUATERNION_NORM_ERROR = maximum normalization error
EULER_ANGLE_UNITS = 'DEGREES' or 'RADIANS'
EULER_ROTATIONS_ORDER = ( ’axis3’, ’axis2’, ’axis1' )
EULER_ROTATIONS_TYPE = 'BODY' or 'SPACE'
ANGULAR_RATE_PRESENT = 'YES', 'NO', 'MAKE UP', 'MAKE UP/NO AVERAGING'
ANGULAR_RATE_FRAME = 'REFERENCE' or 'INSTRUMENT'
ANGULAR_RATE_THRESHOLD = ( max X rate, max Y rate, max Z rate )
OFFSET_ROTATION_ANGLES = ( angle3, angle2, angle1 )
OFFSET_ROTATION_AXES = ( ’axis3’, ’axis2’, ’axis1' )
OFFSET_ROTATION_UNITS = 'DEGREES' or 'RADIANS'
Supporing
Kernels/Files
Output CK
Specs
Input data
Specs
Optional keywords are shown in green

## Slide 11: MSOPCK - Input Details (1)
INPUT_DATA_TYPE = 'SPICE QUATERNIONS'
Input file: TIME1 [TIME2] QCOS QSIN1 QSIN2 QSIN3 [ARX ARY ARZ ]
..... ....... .... ..... ..... ..... ... ... ...
TIME1 [TIME2] QCOS QSIN1 QSIN2 QSIN3 [ARX ARY ARZ ]
INPUT_DATA_TYPE = 'MSOP QUATERNIONS'
Input file: TIME1 [TIME2] -QSIN1 -QSIN2 -QSIN3 QCOS [ARX ARY ARZ ]
..... ....... ..... ..... ..... .... ... ... ...
TIME1 [TIME2] -QSIN1 -QSIN2 -QSIN3 QCOS [ARX ARY ARZ ]
INPUT_DATA_TYPE = 'EULER ANGLES'
Input file: TIME1 [TIME2] ANG3 ANG2 ANG1 [ARX ARY ARZ ]
..... ...... .... .... .... ... ... ...
TIME1 [TIME2] ANG3 ANG2 ANG1 [ARX ARY ARZ ]
INPUT_DATA_TYPE = 'MATRICES'
Input file: TIME1 [TIME2] M11 M12 M13 M21 ... M33 [ARX ARY ARZ ]
..... ...... ... ... ... ... ... ... ... ... ...
TIME1 [TIME2] M11 M12 M13 M21 ... M33 [ARX ARY ARZ ]
Four Examples

## Slide 12: MSOPCK - Input Details (2)
Quaternions
  INPUT_DATA_TYPE=‘SPICE QUATERNIONS’ indicates the quaternions being used follow the SPICE formation rules(*)
  INPUT_DATA_TYPE=‘MSOP QUATERNIONS’ indicates the quaternions being used follow the traditional AACS formation rules(*)
    Normally quaternions that come in telemetry are of this type
  QUATERNION_NORM_ERROR keyword may be used to identify and filter out input records with quaternions that are not unit vectors
    It is set a tolerance for comparing the norm of the input quaternion with 1
Euler angles
  All three angles must be provided
  For the angles provided on the input as
    TIME1 [TIME2] ANG3 ANG2 ANG1 [ ARX ARY ARZ ]
  and rotation axes specified in the setup as
EULER_ROTATIONS_ORDER = ( ’axis3’, ’axis2’, ’axis1' )
  the matrix rotating vectors from base to the structure frame is computed as
Vinst = [ANG3]axis3 * [ANG2]axis2 * [ANG1]axis1 * Vref
  Angles can be provided in degrees or radians
(*) NAIF prepared and provides on request a “white paper” explaining differences between various quaternion styles.

## Slide 13: MSOPCK - Input Details (3)
Angular rates are an optional input. Their presence or absence must be indicated using the ANGULAR_RATE_PRESENT keyword
  If angular rates are provided (ANGULAR_RATE_PRESENT=‘YES’), they must be in a form of 3d vector expressed either in the base frame (less common) or structure frame (more common)
    The ANGULAR_RATE_FRAME keyword must be set to indicate which of the two is used
  If angular rates are not provided, the program can either make a CK without rates (ANGULAR_RATE_PRESENT=‘NO’), or try to compute rates from the orientation data by using uniform rotation algorithm implemented in Type 3 CK, either with averaging (ANGULAR_RATE_PRESENT=‘MAKE UP’) or without averaging (ANGULAR_RATE_PRESENT=‘MAKE UP/NO AVERAGING’) of the rates computed for adjacent orientation data points
  ANGULAR_RATE_THRESHOLD may be used to identify and filter out input records with angular rate components that are too large to be real
Input data can be tagged with UTC, SCLK, or SCLK ticks, specified using the INPUT_TIME_TYPE keyword
  Time tags must not have embedded spaces

## Slide 14: MSOPCK - Output Details (1)
msopck can generate Type 1, 2, or 3 CKs
  Type 1 is rarely used - only in cases when the input contains very few data points that are far apart so that interpolation between them make no sense
  Type 2 is also rarely used, primarily to package orientation for spinners
    Normally the input for making Type 2 CKs should contain two times and the angular rate in each record
  Type 3 is the most commonly used output type because it provides interpolation between the orientation data points stored in the CK
Interpolation intervals are determined based on the threshold value specified in the MAXIMUM_VALID_INTERVAL keyword
  The threshold interval is given in seconds
  The output Type 3 CK will allow interpolation between all input points that are less than or equal to the threshold
An additional transformation to be combined with the input attitude may be specified using OFFSET_ROTATION_* keywords
  Convention for specification of the offset rotation angles is the same as for the input Euler angles
  A vector defined in the base frame is first multiplied by the offset rotation
Vinst = [ROTinput] * [ROToffset] * Vref

## Slide 15: MSOPCK - Output Details (2)
Input times may be adjusted by a constant value specified in seconds using TIME_CORRECTION keyword
The output CK file contains one or more CK segments
  Multiple segments are generated if the input data volume is large and does not fit into the program’s internal buffer (100,000 pointing records)
  When the output file has many segments, each segment’s start time is equal to the stop time of the previous segment, i.e. there are no gaps at the segment boundaries
The Comment area of the output CK contains the following information:
  Contents of the comment file, if it was specified using the COMMENT_FILE_NAME keyword
  Contents of the setup file
  Summary of coverage for each segment written to the file, including a table listing interpolation intervals for segments of Type 2 or 3

## Slide 16: MSOPCK - Example (1)
Terminal Window
$ more msopck_setup.example
MSOPCK setup for predict M'01 CK generation.
==============================================================================
\begindata
PRODUCER_ID = ’NAIF/JPL'
LSK_FILE_NAME = 'naif0007.tls'
SCLK_FILE_NAME = 'ORB1_SCLKSCET.00001.tsc'
COMMENTS_FILE_NAME = 'msopck_comments.example'
INTERNAL_FILE_NAME = 'sample M01 SC Orientation CK File'
CK_SEGMENT_ID = 'SAMPLE M01 SC BUS ATTITUDE'
INSTRUMENT_ID = -53000
REFERENCE_FRAME_NAME = 'MARSIAU'
CK_TYPE = 3
MAXIMUM_VALID_INTERVAL = 60
INPUT_TIME_TYPE = ’SCLK'
INPUT_DATA_TYPE = 'MSOP QUATERNIONS'
QUATERNION_NORM_ERROR = 1.0E-3
ANGULAR_RATE_PRESENT = 'MAKE UP'
\begintext
$

## Slide 17: MSOPCK - Example (2)
Terminal Window
$ more msopck_comments.example
Sample Mars Surveyor '01 Orbiter Spacecraft Orientation CK File
===========================================================================
Orientation Data in the File
--------------------------------------------------------
This file contains sample orientation for the Mars Surveyor ‘01
Orbiter (M01) spacecraft frame, 'M01_SPACECRAFT', relative
to the Mars Mean Equator and IAU vector of J2000, 'MARSIAU', inertial
frame. The NAIF ID code for the 'M01_SPACECRAFT' frame is -53000.
Status
--------------------------------------------------------
This file is a special sample C-Kernel file created by NAIF to illustrate
MSOPCK program. This file should not be used for any other purposes.
...

## Slide 18: MSOPCK - Example (3)
Terminal Window
$ more msopck_input.example
0767491368.064 -0.24376335 0.68291384 0.28475901 0.62699316
0767491372.114 -0.24249471 0.68338563 0.28591829 0.62644323
0767491373.242 -0.24204185 0.68355329 0.28633291 0.62624605
0767491374.064 -0.24194814 0.68358228 0.28641744 0.62621196
0767491380.064 -0.24012676 0.68424169 0.28807922 0.62543010
0767491386.064 -0.23830473 0.68489895 0.28973563 0.62464193
0767491392.064 -0.23648008 0.68555126 0.29139303 0.62384833
0767491398.064 -0.23465389 0.68620253 0.29304524 0.62304745
0767491404.064 -0.23282999 0.68684150 0.29470173 0.62224580
0767491404.114 -0.23277293 0.68686688 0.29475362 0.62221455
0767491405.242 -0.23231585 0.68702790 0.29516507 0.62201253
0767491410.064 -0.23100059 0.68748174 0.29634561 0.62143935
0767491416.064 -0.22917353 0.68811325 0.29799308 0.62062853
0767491422.064 -0.22734161 0.68874177 0.29963482 0.61981412
0767491428.064 -0.22551078 0.68936246 0.30128030 0.61899473
0767491434.064 -0.22367453 0.68998299 0.30291779 0.61816987
0767491436.114 -0.22300583 0.69021050 0.30351804 0.61786298
0767491438.011 -0.22251770 0.69037871 0.30395477 0.61763631
...

## Slide 19: MSOPCK - Example (4)
Terminal Window
$ msopck msopck_setup.example msopck_input.example msopck_example_ck.bc
MSOPCK Utility Program, Version 3.0.0, 2003-05-05; SPICE Toolkit Ver. N0057
...
<comment file contents>
...
<setup file contents>
...
********************************************************************************
RUN-TIME OBTAINED META INFORMATION:
********************************************************************************
PRODUCT_CREATION_TIME = 2004-04-29T12:17:55
START_TIME = 2004-04-27T00:00:05.516
STOP_TIME = 2004-04-27T23:59:56.275
********************************************************************************
INTERPOLATION INTERVALS IN THE FILE SEGMENTS:
********************************************************************************
SEG.SUMMARY: ID -53000, COVERG: 2004-04-27T00:00:05.516 2004-04-27T23:59:56.275
--------------------------------------------------------------------------------
2004-04-27T00:00:05.516 2004-04-27T20:05:26.282
2004-04-27T20:11:20.278 2004-04-27T23:59:56.273

## Slide 20: PREDICKT
prediCkt is a program for making CK files from a set of orientation specification rules, and schedules defining when these rules are to be followed
prediCkt has a simple command line interface
prediCkt requires orientation and schedule specification to be provided in a setup file that follows the SPICE text kernel syntax
prediCkt requires all supporting kernels -- SPK, PCK, etc -- to be provided in a meta-kernel

## Slide 21: PREDICKT - Usage
prediCkt has the following command line arguments
prediCkt -furnish support_data
-spec ck_specs
-ck outfile
-tol fit_tolerance [units]
-<sclk|newsclk> sclk_kernel
‘-furnish’, ‘-spec’ and ‘-ck’ are used to specify the input meta-kernel, input attitude specification file and output CK file
‘-tol’ is used to specify the tolerance to which the orientation stored in the CK should match the specified attitude profile
‘-sclk’ and ‘-newsclk’ specify the name of an existing SCLK or the new “fake” SCLK to be created for use with the output CK

## Slide 22: PREDICKT - Furnsh and Spec Files
A “FURNSH” kernel lists SPICE kernels that are to be used by prediCkt to determine geometry needed to compute orientations
A prediCkt attitude specification (spec) file follows the text kernel syntax and provides three types of information:
  Specification of dynamic directions
  Specification of orientations based on these directions
  Specification of the schedules defining when those orientations should be followed
The contents of the FURNSH kernel and the spec file are included in the comment area of the output CK file

## Slide 23: PREDICKT - Directions
Dynamic directions can be of the following types:
  Based on ephemeris (position vectors, velocity vectors)
  Fixed with respect to a frame (expressed as Cartesian vector or specified by RA and DEC)
  Towards sub-observer point
  Based on the surface normal and lines of constant latitude or longitude
  Based on other, already defined directions (rotated from them, computed as cross products using them, etc)
Example: these two sets of spec file keyword assignments specify nadir and spacecraft velocity directions for M01
    DIRECTION_SPECS += ( 'ToMars = POSITION OF MARS -' )
    DIRECTION_SPECS += ( 'FROM M01 -' )
    DIRECTION_SPECS += ( 'CORRECTION NONE' )
    DIRECTION_SPECS += ( 'scVelocity = VELOCITY OF M01 -' )
    DIRECTION_SPECS += ( 'FROM MARS -' )
    DIRECTION_SPECS += ( 'CORRECTION NONE' )

## Slide 24: PREDICKT - Orientations
An orientation is specified by:
  defining that one of the frames axes (+X,+Y,+Z,-X,-Y,-Z) points exactly along one of the defined directions
  defining that another frame axis points as closely as possible to another defined direction
    The third axis is the cross product of the first two
  specifying the base frame with respect to which the orientation of this “constructed” frame is to be computed
Example: these spec file keyword assignments specify the nominal nadir orientation for THEMIS, flown on M01
    ORIENTATION_NAME += 'CameratoMars'
    PRIMARY += '+Z = ToMars'
    SECONDARY += '+Y = scVelocity'
    BASE_FRAME += 'J2000'

## Slide 25: PREDICKT - Schedules (1)
A schedule is defined by specifying a series of time intervals during which a given orientation is to be followed
  For each interval for a given CK ID the spec file defines the orientation name, start time, and stop time (as Ephemeris Times)
Example: these spec file keyword assignments specify a schedule with a single window during which M01 will yield nadir-pointed orientation for THEMIS
    CK-SCLK = 53
    CK-SPK = -53
    CK-FRAMES += -53000
    CK-53000ORIENTATION += 'SOLUTION TO M01_THEMIS_IR = CameratoMars'
    CK-53000START += @2004-FEB-10-00:00
    CK-53000STOP += @2004-FEB-15-00:00

## Slide 26: PREDICKT - Schedules (2)
In the example on the previous slide:
  CK-FRAMES keyword specifies the CK ID to be used in the output CK
    This ID is incorporated into the keywords defining the schedule intervals
  CK-SCLK keyword specifies the ID of the SCLK to be used in creating the CK
  CK-SPK keyword specifies the ID of the object, the position of which is used in applying light time correction when orientation is computed
  “SOLUTION TO” construct specifies that although the orientation is sought for the M01 spacecraft frame (ID -53000), it is computed for the camera frame (M01_THEMIS_IR) and then transformed to be for the spacecraft frame

## Slide 27: PREDICKT - Example (1)
Terminal Window
$ cat m01_map_nadir.prediCkt
\begindata
DIRECTION_SPECS += ( 'ToMars = POSITION OF MARS -' )
DIRECTION_SPECS += ( 'FROM M01 -' )
DIRECTION_SPECS += ( 'CORRECTION NONE' )
DIRECTION_SPECS += ( 'scVelocity = VELOCITY OF M01 -' )
DIRECTION_SPECS += ( 'FROM MARS -' )
DIRECTION_SPECS += ( 'CORRECTION NONE' )
ORIENTATION_NAME += 'CameratoMars'
PRIMARY += '+Z = ToMars'
SECONDARY += '+Y = scVelocity'
BASE_FRAME += 'J2000'
CK-SCLK = 53
CK-SPK = -53
CK-FRAMES += -53000
CK-53000ORIENTATION += 'SOLUTION TO M01_THEMIS_IR = CameratoMars'
CK-53000START += @2004-FEB-10-00:00
CK-53000STOP += @2004-FEB-15-00:00
\begintext

## Slide 28: PREDICKT - Example (2)
Terminal Window
$ cat m01_map_nadir.furnsh
\begindata
KERNELS_TO_LOAD = ( 'naif0007.tls'
'm01_v26.tf'
'mar033-5.bsp'
'm01_map_rec.bsp'
'm01.tsc' )
\begintext
$ prediCkt -furnish m01_map_nadir.furnsh -spec m01_map_nadir.prediCkt -ck m01_map_nadir.bc -tol 0.01 degrees -sclk m01.tsc
Begin Segment: 1 --- SOLUTION TO M01_THEMIS_IR = CameratoMars
Constructing Segment
From: 2004 FEB 10 00:00:00.000
To : 2004 FEB 15 00:00:00.000
Percentage finished: 0.0%
Percentage finished: 5.0 % (50 quaternions)
...
Percentage finished: 95.0 % (925 quaternions)
$