## Slide 1: NAIF IDs and Names for Physical Objects and Reference Frames
October 2007

## Slide 2: Overview
Summary of naming/numbering schemes used in SPICE
Naming/numbering of physical objects
Naming/numbering of reference frames
Connection between the schemes
Caution: users sometimes confuse the ID assigned to an object and the ID(s) assigned to a reference frame or frames associated with that object. Read on for details.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Overview
SPICE uses IDs and names to identify:
  physical objects
  reference frames
A name is a text string; an ID is an integer number
The naming/numbering schemes for physical objects and for frames are independent
  This means that in general SPICE does not make any assumptions about frame names/IDs based on the physical objects’ names/IDs and vice versa
    There are some exceptions though; they will be mentioned later
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Names and IDs associated with Objects

## Slide 5: Object IDs/Names
Names and IDs are assigned to the following types of physical objects:
  Natural bodies -- planets, satellites, comets, asteroids
  Artificial bodies -- spacecraft, spacecraft structures, science instruments, individual detectors within science instruments, DSN stations
  Any other point, the location of which can be known within the SPICE context
    Barycenters of solar system and planetary systems, landing sites, corners of solar arrays, focal points of antennas, etc.
A single ID is assigned to each physical object, but multiple names can be associated with (map to) that ID
  On input, the names are treated as synonyms
  On output, the name that was last associated with the ID is used
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Object IDs -- How Used
Physical object IDs are used:
  in the following kernels as data identifiers:
    SPKs -- to identify object and center of motion
    text PCKs -- in keywords associated with a body
    IKs -- in keywords associated with instrument/detector
    FKs -- to specify the center for computing LT correction, and to identify the body in PCK-based frames
    SCLKs -- normally the SCLK ID used in keywords is the negative of the spacecraft’s ID (thus a positive integer)
  in the following APIs as input and/or output arguments:
    Older SPK routines -- SPKEZ, SPKEZP, SPKGEO, …
    Older derived geometry routines -- ET2LST, …
    Older PCK routines -- BODVAR, BODMAT, …
    IK routines -- GETFOV, indirectly in G*POOL, …
    SCLK routines -- SCE2C, SCT2E, …
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Object Names -- How Used
Physical object names are used in the following APIs as input and/or output arguments:
    Newer SPK routines -- SPKEZR, SPKPOS
    Newer derived geometry routines -- SRFXPT, ILLUM, SUBSOL, …
    Newer PCK routines -- BODVRD, …
Physical object names are NOT used as data identifiers within kernels.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Object IDs/Names -- How Defined
Name/ID mappings used by SPICE may be defined in two places
  Inside the Toolkit: hard-coded in the source code
    See NAIF_IDS.REQ for a complete listing of built-in (default) assignments
  In text kernels
    You may define additional mappings using KEYWORD = VALUE assignments. For example, for a spacecraft:
      NAIF_BODY_NAME += ( ’spacecraft_name’ )*
      NAIF_BODY_CODE += ( spacecraft_ID_number )*
    These assignments exist most often in FKs (e.g. DI, GNS, M01, MER, SIRTF), sometimes in IKs (e.g. CASSINI, MGS), but can be placed in any text kernel
    Normally text kernels are used to define name/ID mappings for instruments, their subsystems/detectors and other spacecraft structures
      See comments and the actual data sections in a text kernel for the complete listing of the names/IDs defined in that kernel
    Mappings defined in text kernels take precedence over those defined in Toolkit source code.
* See Kernels Required Reading for information about the “+=“ operator
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Object IDs/Names Spacecraft and Ground Stations
Spacecraft (negative numbers)
  Within NASA, this number is generally the negative of the numeric ID assigned by the NASA control authority at GSFC
      -6 ‘PIONEER-6’, ‘P6’
      -7 ‘PIONEER-7, ‘P7’,
      -82 ‘CASSINI’, ‘CAS’
      -94 ‘MARS GLOBAL SURVYOR’, ‘MGS’
      …
  Unfortunately sometimes NASA re-uses a number
    This will happen with increasing frequency in the future
    Probably a new scheme is needed
DSN ground stations (399000 + station number)
      399005 ‘DSS-05’
      …
      399066 ‘DSS-66’
Non-DSN stations (398000 + some integer 0 to 999)
      398990 ‘NEW_NORCIA’
      …
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Object IDs/Names -- Planets
Sun and Solar System Barycenter (10 and 0)
      0 ‘SOLAR SYSTEM BARYCENTER’, ‘SSB’
      10 ‘SUN’
Planetary barycenters (numbers from 1 to 9)
      1 ‘MERCURY BARYCENTER’
      2 ‘VENUS BARYCENTER’
      3 ‘EARTH MOON BARYCENTER’, ‘EMB’, …
      4 ‘MARS BARYCENTER’
      …
      9 ‘PLUTO BARYCENTER’
Planet centers (planet barycenter ID * 100 + 99)
      199 ‘MERCURY’
      299 ‘VENUS’
      399 ‘EARTH’
      499 ‘MARS’
      …
      999 ‘PLUTO’
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: Object IDs/Names -- Satellites (1)
Satellites (planet barycenter ID*100 + number <1… 98>)
      301 ‘MOON’
      401 ‘PHOBOS’
      402 ‘DEIMOS’
      501 ‘IO’
      …
      901 ‘CHARON’, ‘1978P1’
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Object IDs/Names -- Satellites (2)
The scheme described on the previous page can accommodate only 98 natural satellites. How do we handle more than 98?
  For IAU provisional assignments, use “psbbb” also, where:
    p = planet barycenter ID
    s = separator, set equal to “5”
    bbb = satellite number
      Start with the next available unused IAU two-digit number with a “0” pre-pended, when we elect to put this scheme into effect
      Increment by one thereafter
  For IAU permanent assignments, use “psbbb” where:
    p = planet barycenter ID
    s = separator, set equal to “0”
    bbb = satellite number
      Use “099” for the first new permanent assignment after “p98” from the current range is used
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Object IDs/Names -- Satellites (3)
The satellite extended numbering scheme described on the previous two pages attempts to, but may not be able to, maintain consistency in the last three digits as the boundary between 98 and 99 is crossed.
  This is because the IAU sometimes changes the numbering order of new satellites when migrating from provisional to permanent status.
It has been suggested that some JPL entity maintain a public web page showing the history of all assignments.
  (Not done so far…)
It is recommended that any SPK file made using provisional IDs be trashed (or hidden away) when a new file using permanent IDs is obtained.
  If no new file is expected, the bspidmod program can be used to replace provisional ID(s) with official ID(s) in the old file
Notes: <number>
<footer>
<header>
<date/time>

## Slide 14: Object IDs/Names Comets & Asteroids
Periodic Comets (1000000 + number)
      1000001 ‘AREND’
      1000002 ‘AREND-REGAUX’
      …
      1000032 ‘HALE-BOPP’
Numbered Asteroids (2000000 + asteroid number)
      2000001 ‘CERES’
      2000004 ‘VESTA’
      …
      2009969 ‘BRAILLE’, ‘1992KD’
      There are a few exceptions; see NAIF_IDS.REQ
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Object IDs/Names -- Instruments
Science Instruments (s/c ID*1000 - inst. number)
  A number should be picked for EVERY instrument, instrument subsystem or detector, or spacecraft structure, the parameters for which are to be stored in IKs, or the location of which is to be stored in SPKs
  Instrument numbers are picked from the range 0…999. The only requirement is that they must be unique
      …
      -82760 ‘CASSINI_MIMI_CHEMS’
      -82761 ‘CASSINI_MIMI_INCA’
      -82762 ‘CASSINI_MIMI_LEMMS1’
      -82763 ‘CASSINI_MIMI_LEMMS2’
      …
      -82001 ‘CASSINI_SRU-A’
      -82002 ‘CASSINI_SRU-B’
      -82008 ‘CASSINI_SRU-A_RAD’
      -82009 ‘CASSINI_SRU-B_RAD’
      …
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Object IDs/Names -- Mapping APIs
SPICE provides two routines to map physical object IDs to names, and vice versa
  To get the ID for a given physical object name:
    CALL BODN2C ( NAME, ID, FOUND )
    CALL BODS2C ( NAME, ID, FOUND )
  To get the name for a given physical object ID:
    CALL BODC2N( ID, NAME, FOUND )
  If the “FOUND” flag returned by either of these routines comes back FALSE, then the input ID or name cannot be mapped
(This is a more general version as compared to BODN2C. Use this one.)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: Names and IDs associated with Reference Frames

## Slide 18: Frame IDs/Names
Names and IDs are assigned to the following kinds of reference frames
  Inertial frames
  Body-fixed frames
  Spacecraft and instrument frames
  Topocentric frames
  Any other reference frame for which the orientation may be needed to compute observation geometry
Unlike for objects, only a single ID and a single name are assigned to each reference frame
  “Aliases” for a frame name can only be set up by defining new zero-offset frames with their own unique names and IDs
Notes: <number>
<footer>
<header>
<date/time>

## Slide 19: Frame IDs/Names -- How Used
Reference frame IDs are used
  in the following kernels as data identifiers:
    FKs -- to “glue” frame definition keywords together
    SPKs -- to identify base reference frames
    PCKs -- to identify base reference frames
  in the following APIs as input and/or output arguments:
    Almost nowhere -- users rarely or never need to deal with or be aware of reference frame IDs
Reference frame names are used
  as arguments in all high level APIs that require a reference frame to be specified on the input
    Derived geometry routines -- SRFXPT, …
    Frame transformation routines -- PXFORM, SXFORM
    SPK routines -- SPKEZR, SPKPOS, …
  Frame names are NOT used as data identifiers within kernels
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: Frame IDs/Names -- How Defined
The reference frame name/ID mappings used by the SPICE system are defined in two places
  Inside the Toolkit: hard-coded into the source code
    For inertial frames
    For body-fixed frames for planets and satellites
    See FRAMES REQUIRED READING for a complete listing
  In text kernels: provided by KEYWORD=VALUE sets
    Almost always in FKs (DI, GNS, M01, MER, SIRTF, …), very rarely in other kernels, but can be in any text kernel
      (For historic reasons, MGS frames are defined in IKs and SCLK)
    Text kernels define spacecraft frames, instrument frames, spacecraft subsystem frames, DSN station frames, etc.
      See comments/data sections in a text kernel for the complete listing of the frames defined in that kernel
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: Frame IDs/Names -- Inertial and Body-fixed
  The samples of frame IDs shown below are shown for completeness. Users would rarely if ever need to know or use them.
Inertial frames (positive integers starting at 1)
      1 ‘J2000’
      …
      16 ‘MARSIAU’
      17 ‘ECLIPJ2000’
      …
      21 ‘DE-143’
Body-fixed frames (positive integers starting at 10001)
      10001 ‘IAU_MERCURY_BARYCENTER’
      …
      10011 ‘IAU_MERCURY’
      …
      10020 ‘IAU_MOON’
      …
      10081 ‘EARTH_FIXED’
      …
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Frame IDs/Names -- Spacecraft and Instrument
  The samples of frame IDs shown below are shown for completeness. Users would rarely if ever need to know or use them.
IDs for frames associated with spacecraft, spacecraft structures, and instruments are usually:
  s/c ID times 1000 minus an arbitrary number
As example, for Cassini:
  Spacecraft frame
        -82000 ‘CASSINI_SC_COORD’
  Spacecraft structure frame
        -82001 ‘CASSINI_SRU-A’
  Instrument frames
        -82760 ‘CASSINI_MIMI_CHEMS’
        -82761 ‘CASSINI_MIMI_LEMMS_INCA’
        -82762 ‘CASSINI_MIMI_LEMMS1’
        -82763 ‘CASSINI_MIMI_LEMMS2’
        -82764 ‘CASSINI_MIMI_LEMMS_BASE’
        -83765 ‘CASSINI_MIMI_LEMMS_ART’
        …
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Frame IDs/Names -- Mapping APIs
SPICE provides two routines to convert (map) reference frame IDs to names, and vice versa
  To get the ID for a given reference frame name:
    CALL NAMFRM( NAME, ID )
  To get the name for a given reference frame ID:
    CALL FRMNAM( ID, NAME )
  If the ID or name cannot be mapped, these routines return zero and an empty/blank string respectively.
Users will rarely if ever need to call these routines
Notes: <number>
<footer>
<header>
<date/time>

## Slide 24: Name/ID Schemes Connections
Although physical object and reference frame naming/numbering schemes are independent, in practice there is a lot of overlap in the way objects and frames are named and numbered
This overlap is due to the following reasons
  Conventions adopted over the course of SPICE implementation
    Example: PCK-based body-fixed frames for planets and satellites are named ‘IAU_<body name>’
      However, the IDs of these frames have nothing in common with the IDs of the objects (bodies) for which these frames are defined
  The need for the object and frame IDs to be unique
    For this reason both the instrument (object) IDs and the instrument frame IDs are derived from the ID of the spacecraft on which the instrument is flown
  The need for the object and frame names to be meaningful
    For this reason the instrument frame names normally contain both the name of the spacecraft and the name of the instrument
Notes: <number>
<footer>
<header>
<date/time>

## Slide 25: “Odd Ball” Cases
CK IDs
  Historically IDs used in CKs are called structure IDs but in reality they are much more closely related to frames than to physical objects
  To find which frame is associated with a particular CK ID, look through FK for a frame whose _CLASS_ID keyword is set to the CK ID
    In practice, for CK-based frames both the frame ID and frame _CLASS_ID are set to the CK ID
SCLK IDs
  Because most spacecraft have only one on-board clock, the SCLK ID of that clock is the same as the spacecraft ID
  Should a spacecraft carry more than one independent clock, unique SCLK IDs for these other clocks would be needed
    Normally the ID of an additional clock will be set to the ID of the instrument, of which that clock is a part
  SCLK IDs are used in SCLK APIs (must be provided by the user) and by the frames subsystem when it reads CKs to determine orientation of CK-based frames (gets SCLK ID from CK_*_SCLK keyword provided in the frame definition or computes it by dividing CK ID by 1000)
Notes: <number>
<footer>
<header>
<date/time>

## Slide 26: Name/IDs Example -- CASSINI (1)
10 | ‘SUN’ | 1 | ‘J2000’
399 | ‘EARTH’ | 10013 | ‘IAU_EARTH’
699 | ‘SATURN’ | 10016 | ‘IAU_SATURN’
601 | ‘MIMAS’ | 10039 | ‘IAU_MIMAS’
602 | ‘ENCELADUS’ | 10040 | ‘IAU_ENCELADUS’
-82 | ‘CASSINI’ | -82000 | ‘CASSINI_SC_COORD’
-82001 | ‘CASSINI_SRU-A’ | -82001 | ‘CASSINI_SRU-A’
-82790 | ‘CASSINI_CDA’ | -82790 | ‘CASSINI_CDA’
 |  | -82791 | ‘CASSINI_CDA_ART’
 |  | -82792 | ‘CASSINI_CDA_BASE’
-82820 | ‘CASSINI_CAPS_IMS’ | -82820 | ‘CASSINI_CAPS’
-82821 | ‘CASSINI_CAPS_ELS’ | -82821 | ‘CASSINI_CAPS_ART’
-82822 | ‘CASSINI_CAPS_IBS_DT1’ | -82822 | ‘CASSINI_CAPS_BASE’
-82823 | ‘CASSINI_CAPS_IBS_DT2’ |  | 
-82824 | ‘CASSINI_CAPS_IBS_DT3’ |  | 
Objects IDs/Names Frames IDs/Names
Ephemeris objects
Spacecraft and its structures
CDA instrument
CAPS instrument
Notes: <number>
<footer>
<header>
<date/time>

## Slide 27: Name/IDs Example -- CASSINI (2)
The lists provided on the previous page are by no means complete
  There are many more Saturnian satellites and other natural bodies of interest to the Cassini mission, each having an associated frame
  There are many more instruments on the Cassini spacecraft, with multiple frames associated with each of them
To find names and IDs associated with these objects and frames users should refer as follows
  For names/IDs of natural objects: NAIF_IDS.REQ
  For names/IDs of Cassini instruments and their subsystems: IK files
    For other missions this information is in the mission’s FK file
  For names of inertial frames and body-fixed frames associated with natural bodies: FRAMES.REQ
  For names of the reference frames associated with the Cassini spacecraft, its subsystems and instruments: FK file
Notes: <number>
<footer>
<header>
<date/time>