## Slide 1: MATLAB Interface to CSPICE “Mice”
How to Access the CSPICE library Using
MATLAB©
October 2007
© The MathWorks Inc.

## Slide 2: Topics
Mice Benefits
How does it work?
Distribution
Mice Operation
Vectorization
Simple Use of Mice Functionality

## Slide 3: Mice Benefits
Mice operates as an extension to the MATLAB language regime.
All Mice calls are functions regardless of the call format of the underlying CSPICE routine, returning MATLAB native data types.
Mice has some capability not available in CSPICE such as vectorization.
CSPICE error messages return to MATLAB in the form usable by the try...catch construct.
Notes: Added OS X mention.

## Slide 4: How Does It Work? (1)
The MATLAB environment includes an intrinsic capability to use external routines.
  Mice functions as a MATLAB Executable, MEX, consisting of the Mice MEX shared object library and a set of .m wrapper files.
    The Mice library contains the MATLAB callable C interface routines that wrap a subset of CSPICE wrapper calls.
    The wrapper files, named cspice_*.m and mice_*.m, provide the MATLAB calls to the interface functions.
      A function prefixed with ‘cspice_’ retains essentially the same argument list as the CSPICE counterpart.
      An interface prefixed with ‘mice_’ returns a structure, with the fields of the structure corresponding to the output arguments of the CSPICE counterpart.
    The wrappers include a header section describing the function call, displayable by the MATLAB help command.

## Slide 5: How Does It Work? (2)
When a user invokes a call to a Mice function:
1. MATLAB calls…
2. the function's wrapper, which calls…
3. the Mice MEX shared object library, which
    performs its function then returns the result…
4. to the wrapper, which…
      5. returns the result to the user
… transparent from the user’s perspective.

## Slide 6
Mice Distribution
NAIF distributes Mice as a complete, standalone package.
The package includes:
  The CSPICE source files.
  The Mice interface source code.
  Platform specific build scripts for Mice and CSPICE.
  MATLAB versions of the SPICE cookbook programs, states, tictoc, subpt, and simple.
  An HTML based help system for both Mice and CSPICE, with the Mice help cross-linked to CSPICE.
  The Mice MEX shared library and the M wrapper files. The system is ready for use after installation of the the library and wrapper files.
Notes: Updated test information. Edited furnsh warning. CSPICE no longer throws an error for multiply loaded binary files.

## Slide 7
Mice Operation (1)
A possible irritant exists in loading kernels using the cspice_furnsh function.
  Kernels load into your MATLAB session, not into your MATLAB scripts. This means:
    loaded binary kernels remain accessible (“active”) throughout your MATLAB session
    data from loaded text kernels remain in the kernel pool (in the memory space used by CSPICE) throughout your MATLAB session
  Consequence: some kernel data may be available to one of your scripts even though not intended to be so.
    You could get incorrect results!
    (If you run only one script during your MATLAB session, there’s no problem.)
continued on next page

## Slide 8
Mice Operation (2)
Mitigation: two approaches
  Load all needed SPICE kernels for your MATLAB session at the beginning of the session, paying careful attention to the files loaded and the loading order (loading order affects precedence)
    Convince yourself that this approach will provide ALL of the scripts you will run during this MATLAB session with the appropriate SPICE data
  At or near the end of every MATLAB script:
    include a call to cspice_unload for each kernel loaded using cspice_furnsh
    or include a call to cspice_kclear to remove ALL kernel data from the kernel pool loaded using cspice_furnsh

## Slide 9
Most Mice functions include use of vectorized arguments, a capability not available in C or FORTRAN toolkits.
Example: use Mice to retrieve state vectors and light-time values for 1000 ephemeris times.
  Create the array of 1000 ephemeris times in steps of 10 hours, keyed on July 1, 2005:
  start = cspice_str2et('July 1 2005');
  et = (0:999)*36000 + start;
  Retrieve the state vectors and corresponding light times from Mars to earth at each et in the J2000 frame with LT+S aberration correction:
  [state, ltime] = cspice_spkezr( 'Earth', et, 'J2000', 'LT+S', 'MARS');
Mice Vectorization (1)
continued on next page

## Slide 10
  Access the ith state 6-vector (6x1 array) corresponding to the ith ephemeris time with the expression
  state_i = state(:,i)
Convert the ephemeris time vector et from the previous example to UTC calendar strings with three decimal places of precision in the seconds field.
  format = 'C';
  prec = 3;
  utcstr = cspice_et2utc( et, format, prec );
  The call returns utcstr, an array of 1000 strings (dimensioned 1000x24), where each ith string is the calendar date corresponding to et(i). Access the ith string of utcstr corresponding to the ith ephemeris time with the expression
  utcstr_i = utcstr(i,:)
Mice Vectorization (2)

## Slide 11
Convert the position components (the first three components in a state vector) of the N state vectors returned in state to latitudinal coordinates.
[radius, latitude, longitude] = cspice_reclat( state(1:3,:) );
  The call returns three double precision 1x1000 arrays (vectorized scalars): radius, latitude, and longitude.
Mice Vectorization (3)

## Slide 12
Simple Use of Mice Functionality
As an example of Mice use, calculate and plot the trajectory in the J2000 inertial frame of the Cassini spacecraft from June 20, 2004 to December 1, 2005.
% Define the number of divisions of the time interval and the time interval.
STEP = 1000;
utc = strvcat( 'Jun 20, 2004', 'Dec 1, 2005' )
% Load the needed kernels. Use a meta kernel "standard.ker" to load the kernels
% "naif0008.tls," "de405_2000-2050.bsp," "pck00008.tpc."
cspice_furnsh( 'standard.ker')
cspice_furnsh( '/kernels/cassini/spk/T18-5TDJ5.bsp')
et = cspice_str2et( utc );
times = (0:STEP-1) * ( et(2) - et(1) )/STEP + et(1);
[pos,ltime ]=cspice_spkpos( 'Cassini', times, 'J2000', 'NONE', 'SATURN BARYCENTER' );
% Plot the resulting trajectory.
x = pos(1,:);
y = pos(2,:);
z = pos(3,:);
plot3(x,y,z)
cspice_kclear

## Slide 13
Graphic Output using MATLAB
Trajectory of the Cassini vehicle in the J2000 frame, for June 20, 2005 to Dec 1, 2005