## Slide 1: Writing an Mice (MATLAB) Based Program
October 2007

## Slide 2: Viewing This Tutorial
This coding example is an “animated” presentation that is best viewed using PowerPoint set to “Slide Show” mode.
Undefined variables are displayed in red; results are displayed in blue.

## Slide 3: Introduction
First, let's go over the important steps in the process of writing a Mice-based program and putting it to work:
Understand the geometry problem.
Identify the set of SPICE kernels that contain the data needed to perform the computation.
Formulate an algorithm to compute the quantities of interest using SPICE.
Write and compile the program.
Get actual kernel files and verify that they contain the data needed to support the computation for the time(s) of interest.
Run the program.
To illustrate these steps, let's write a program that computes the apparent intersection of the boresight ray of a given CASSINI science instrument with the surface of a given Saturnian satellite. The program will compute:
Planetocentric and planetodetic (geodetic) latitudes and longitudes of the intercept point.
Range from spacecraft to intercept point and from spacecraft to target center.
Illumination angles (phase, solar incidence, and emission) at the intercept point.

## Slide 4: Observation geometry
Using what model?
We want the boresight
intercept on the surface, range
from s/c to intercept and target
center, and illumination angles at
the intercept point.
When?
On what object?
For which instrument?
For what spacecraft?
TIME (UTC, TDB or TT)
SATNM
INSTNM
SCNM
SETUPF
Phase angle
solar incidence angle
surface normal
emission angle

## Slide 5: Needed Data
Time transformation kernels
Orientation models
Instrument descriptions
Shapes of satellites, planets
Ephemerides for spacecraft,
Saturn barycenter and satellites.
surface normal
solar incidence angle
emission angle
Phase angle

## Slide 6: Which kinds of kernels are needed?
Data required to compute vectors, rotations and other parameters shown in the picture are stored in the SPICE kernels listed below.
  Note: these kernels have been selected to support this presentation; they should not be assumed to be appropriate for user applications.
Parameter Kernel Type File name
----------------------- -------------- ------------
time conversions generic LSK naif0008.tls
CASSINI SCLK cassini.tsc
satellite orientation generic PCK pck00008.tpc
satellite shape generic PCK pck00008.tpc
satellite position planet/sat
ephemeris SPK 020514_SE_SAT105.bsp
planet barycenter position planet SPK 981005_PLTEPH-DE405S.bsp
spacecraft position spacecraft SPK tour9201.bsp
spacecraft orientation spacecraft CK cas_050215.bc
instrument alignment CASSINI FK cas_v37.tf
instrument boresight Instrument IK cas_iss_v09.ti

## Slide 7
The easiest and most flexible way to make these kernels available to the program is via cspice_furnsh. For this example we make a setup file (also called a “metakernel” or “furnsh kernel”) containing a list of kernels to be loaded:
\begindata
KERNELS_TO_LOAD = ( 'naif0008.tls', 'cassini.tsc',
'pck00008.tpc', '020514_SE_SAT105.bsp',
'981005_PLTEPH-DE405S.bsp', 'tour9201.bsp',
'cas_050215.bc', 'cas_v37.tf',
'cas_iss_v09.ti' )
\begintext
and we make the program prompt for the name of this setup file:
setupf = input('Enter setup file name > ', 's');
cspice_furnsh( setupf )
Load kernels
  Note: these kernels have been selected to support this presentation; they should not be assumed to be appropriate for user applications.

## Slide 8: Programming Solution
Prompt for setup file (“metakernel”) name; load kernels specified via setup file. (Done on previous chart.)
Prompt for user inputs required to completely specify problem. Obtain further inputs required by geometry routines via Mice calls.
Compute the intersection of the boresight direction ray with the surface of the satellite, presented as a triaxial ellipsoid.
If there is an intersection:
  Convert Cartesian coordinates of the intersection point to planetocentric latitudinal and planetodetic coordinates
  Compute spacecraft-to-intercept point range and spacecraft-to-target center range
  Find the illumination angles (phase, solar incidence, and emission) at the intercept point
Display the results.
We discuss the geometric portion of the problem first.

## Slide 9: Compute surface intercept
Compute the intercept point (point) of the instrument boresight vector (insite)
with the satellite’s (satnm) surface at the TDB time of interest (et). This call
also returns the distance between the spacecraft and intercept point (dist),
the light-time corrected epoch at the intercept point (trgepc), the target
center-to-spacecraft vector (obspos), and a boolean flag indicating whether
the intercept was found (found).
Note: undefined variables are in red; results are in blue.
[point, dist, trgepc, obspos, found] = cspice_srfxpt( 'Ellipsoid', ...
satnm, et, ‘CN+S’, scnm, iframe, insite );
The ranges we want are obtained from the outputs of cspice_srfxpt. These outputs are defined only if a surface intercept is found. If found is true, the spacecraft-to-surface intercept range is the output argument dist, and the
spacecraft-to-target center range is the norm of the output argument obspos.
Units are km. We use the MATLAB function norm to obtain the norm:
  norm( obspos )
We'll write out the range data along with the other program results.

## Slide 10: Compute Lat/Lon and Illumination Angles
Compute the planetocentric latitude (pclat) and longitude (pclon), as well as the planetodetic latitude (pdlat) and longitude (pdlon) of the intersection point; ‘found’ the return boolean from cspice_srfxpt.
if ( found )
[r, pclon, pclat] = cspice_reclat( point );
% Let re, rp, and f be the satellite's longer equatorial
% radius, polar radius, and flattening factor.
re = radii(1);
rp = radii(3);
f = ( re - rp ) / re;
[pdlat, pdlat, alt] = cspice_recgeo( point, re, f );
The illumination angles we want are the outputs of cspice_illum. Units are radians.
  [phase, solar, emissn] = cspice_illum( satnm, et, ‘CN+S’, scnm, point);

## Slide 11: Geometry Calculations: Summary
% Compute the boresight ray intersection with the surface of the
% target body. `dist’ and norm(obspos) yield desired ranges.
[point, dist, trgepc, obspos, found] = cspice_srfxpt( 'Ellipsoid', ...
satnm, et, ‘CN+S’, scnm, iframe, insite);
% If an intercept is found, compute planetocentric and planetodetic
% latitude and longitude of the point.
if ( found )
[r, pclon, pclat] = cspice_reclat( point );
% Let re, rp, and f be the satellite's longer equatorial
% radius, polar radius, and flattening factor.
re = radii(1);
rp = radii(3);
f = ( re - rp ) / re;
[pdlon, pdlat, alt] = cspice_recgeo( point, re, f );
% Compute illumination angles at the surface point.
[phase, solar, emissn] = cspice_illum( satnm, et, ’CN+S', scnm, point );
...
else
...

## Slide 12: Get inputs - 1
The code above used quite a few inputs that we don't have yet:
TDB epoch of interest ( et );
satellite and s/c names (satnm, scnm);
satellite ellipsoid radii (radii);
instrument fixed frame name (iframe);
instrument boresight vector in the instrument frame (insite);
Some of these values are user inputs; others can be obtained via CSPICE calls
once the required kernels have been loaded.
Let's prompt for the satellite name (satnm), spacecraft name (scnm), instrument
name (instnm) and time of interest (time):
satnm = input( 'Enter satellite name > ', 's');
scnm = input( 'Enter spacecraft name > ', 's');
instnm = input( 'Enter instrument name > ', 's');
time = input( 'Enter time > ', 's');

## Slide 13: Get Inputs - 2
Then we can get the rest of the inputs from Mice calls:
To get the TDB epoch (et) from the user-supplied time string (which may
refer to the UTC, TDB or TT time systems):
et = cspice_str2et( time );
To get the satellite’s ellipsoid radii (radii):
radii = cspice_bodvrd( satnm, 'RADII', 3 );
To get the instrument boresight direction (insite) and the name of the
instrument frame (iframe) in which it is defined:
[instid, found] = cspice_bodn2c( instnm );
if ( ~found )
txt = sprintf( 'Unable to determine ID for instrument: %d', instnm );
error(txt)
end
[shape, iframe, insite, bundry] = cspice_getfov( instid, ROOM );

## Slide 14: Getting inputs: summary
% Prompt for the user-supplied inputs for our program.
setupf = input( 'Enter setup file name > ', 's');
cspice_furnsh( setupf )
satnm = input( 'Enter satellite name > ', 's');
scnm = input( 'Enter spacecraft name > ', 's');
instnm = input( 'Enter instrument name > ', 's');
time = input( 'Enter time > ', 's');
% Get the epoch corresponding to the input time:
et = cspice_str2et( time );
% Get the radii of the satellite.
radii = cspice_bodvrd( satnm, 'RADII', 3 );
% Get the instrument boresight and frame name.
[instid, found] = cspice_bodn2c( instnm );
if ( ~found )
txt = sprintf( 'Unable to determine ID for instrument: %d', instnm );
error(txt)
end
[shape, iframe, insite, bundry] = cspice_getfov( instid, ROOM );

## Slide 15: Display results
...
% Display results. Convert angles from radians to degrees
% for output.
fprintf( 'Intercept planetocentric longitude (deg): %11.6f\n', ...
R2D*pclon )
fprintf( 'Intercept planetocentric latitude (deg): %11.6f\n', ...
R2D*pclat )
fprintf( 'Intercept planetodetic longitude (deg): %11.6f\n', ...
R2D*pdlon )
fprintf( 'Intercept planetodetic latitude (deg): %11.6f\n', ... R2D*pdlat )
fprintf( 'Range from spacecraft to intercept point (km): %11.6f\n', ...
dist )
fprintf( 'Range from spacecraft to target center (km): %11.6f\n', ...
norm(obspos) )
fprintf( 'Intercept phase angle (deg): %11.6f\n', ...
R2D*phase )
fprintf( 'Intercept solar incidence angle (deg): %11.6f\n', ...
R2D*solar )
fprintf( 'Intercept emission angle (deg): %11.6f\n', ...
R2D*emissn )
else
disp( ['No intercept point found at ' time ] )
end

## Slide 16: Complete the program
To finish up the program we need to declare the variables we've used.
We'll highlight techniques used by NAIF programmers
Add remaining MATLAB code required to make a syntactically valid program
PRO PROG_GEOMETRY
ABCORR = 'CN+S';
ROOM = 10;
R2D = cspice_dpr;
% Prompt for the user-supplied inputs for our program.
setupf = input( 'Enter setup file name > ', 's');
cspice_furnsh( setupf )
satnm = input( 'Enter satellite name > ', 's');
scnm = input( 'Enter spacecraft name > ', 's');
instnm = input( 'Enter instrument name > ', 's');
time = input( 'Enter time > ', 's');

## Slide 17: Complete source code - 1
% Get the epoch corresponding to the input time:
et = cspice_str2et( time );
% Get the radii of the satellite.
radii = cspice_bodvrd( satnm, 'RADII', 3 );
% Get the instrument boresight and frame name.
[instid, found] = cspice_bodn2c( instnm );
if ( ~found )
txt = sprintf( 'Unable to determine ID for instrument: %d', instnm );
error(txt)
end
[shape, iframe, insite, bundry] = cspice_getfov( instid, ROOM );

## Slide 18: Complete source code - 2
% Compute the boresight ray intersection with the surface of the
% target body. `dist’ and norm(obspos) yield desired ranges.
[ point, dist, trgepc, obspos, found ] = cspice_srfxpt( 'Ellipsoid', ...
satnm, et, ABCORR, scnm, iframe, insite );
% If an intercept is found, compute planetocentric and planetodetic
% latitude and longitude of the point.
if ( found )
[r, pclon, pclat] = cspice_reclat( point );
% Let re, rp, and f be the satellite's longer equatorial
% radius, polar radius, and flattening factor.
re = radii(1);
rp = radii(3);
f = ( re - rp ) / re;
[pdlon, pdlat, alt] = cspice_recgeo( point, re, f );
% Compute illumination angles at the surface point.
[phase, solar, emissn] = cspice_illum( satnm, et, ABCORR, scnm, point );

## Slide 19: Complete source code - 3
% Display results. Convert angles from radians to degrees
% for output.
fprintf( 'Intercept planetocentric longitude (deg): %11.6f\n',...
R2D*pclon )
fprintf( 'Intercept planetocentric latitude (deg): %11.6f\n',...
R2D*pclat )
fprintf( 'Intercept planetodetic longitude (deg): %11.6f\n',...
R2D*pdlon )
fprintf( 'Intercept planetodetic latitude (deg): %11.6f\n',... R2D*pdlat )
fprintf( 'Range from spacecraft to intercept point (km): %11.6f\n',...
dist )
fprintf( 'Range from spacecraft to target center (km): %11.6f\n',...
norm(obspos) )
fprintf( 'Intercept phase angle (deg): %11.6f\n',...
R2D*phase )
fprintf( 'Intercept solar incidence angle (deg): %11.6f\n',...
R2D*solar )
fprintf( 'Intercept emission angle (deg): %11.6f\n’,...
R2D*emissn )
else
disp( ['No intercept point found at ' time ]
end
% Unload the kernels and clear the kernel pool
cspice_kclear

## Slide 20: Running the program
It looks like we have everything taken care of:
We have all necessary kernels
We made a setup file (metakernel) pointing to them
We wrote the program
Let's run it.

## Slide 21: Running the program
Terminal Window
>>
Enter setup file name > setup.ker
Enter satellite name > titan
Enter spacecraft name > cassini
Enter instrument name > cassini_iss_nac
Enter time > 2005 feb 15 8:15 UTC
Intercept planetocentric longitude (deg): -156.443003
Intercept planetocentric latitude (deg): 18.788539
Intercept planetodetic longitude (deg): -156.443003
Intercept planetodetic latitude (deg): 18.788539
Range from spacecraft to intercept point (km): 4810.941881
Range from spacecraft to target center (km): 7384.326555
Intercept phase angle (deg): 43.274588
Intercept solar incidence angle (deg): 41.038424
Intercept emission angle (deg): 2.514613
prog_geometry

## Slide 22: Backup
Latitude definitions:
  Planetocentric latitude of a point P: angle between segment from origin to point and x-y plane (red arc in diagram).
  Planetodetic latitude of a point P: angle between x-y plane and extension of ellipsoid normal vector N that connects x-y plane and P (blue arc in diagram).
P
O
Reference ellipsoid
x-y plane
z-axis
N
Planetocentric latitude
Planetodetic latitude