## Slide 1: Fundamental Concepts
October 2007

## Slide 2: Topics
Preface
Time
Reference Frames
Coordinate Systems
Positions and States
Aberration Corrections
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Preface
This tutorial introduces terminology and concepts used in the later SPICE tutorials.
Some of this material is more difficult than what follows in later presentations.
  A complete understanding of this material is not essential in order to use SPICE.
Still, we think this information may be helpful, so… on we go!

## Slide 4: Time
An epoch is an instant in time specified by some singular event
  Passage of a star across your zenith meridian
  Eclipse of a spacecraft signal as it passes behind a solid body
Clocks
  More mundane specifications are given as a count: “regular” oscillations of a pendulum, quartz crystal, or electromagnetic radiation from a specified source, measured from an agreed upon reference epoch.
  Careful specification of epochs using clocks requires reference to the particular clock and the location of that clock.
Time Systems
  Agreed upon standards for “naming” epochs, measuring time, and synchronizing clocks

## Slide 5: Atomic Time and UTC
International Atomic Time (TAI)
  Statistical time scale
    Based on data from ~200 atomic clocks in over 50 national laboratories
  Maintained by Bureau International des Poids et Mesures (BIPM)
  Unit is the SI (System International) second
    duration of 9192631770 periods of the radiation corresponding to the transition between two hyperfine levels of the ground state of the cesium 133 atom
  Count of atomic seconds past the astronomically determined instant of midnight 1 Jan 1958 00:00:00
Coordinated Universal Time (UTC)
  Civil Time at Greenwich England (~GMT)
  Usual Calendar Formats plus Hour:Minute:Second.fraction
  UTC + 10 seconds + number of leap seconds = TAI
    Valid only after Jan 01, 1972

## Slide 6: Astronomical Time
Astronomical Time (UT1) is an hour representation of the angle between the Greenwich zenith meridian and the location of the “computed mean sun.”
Used prior to atomic time for civil time keeping
UT1

## Slide 7: Tying UTC to Earth’s Rotation
Ideally, UTC noon and astronomical noon at Greenwich (UT1) should occur simultaneously. However, the earth’s rotation is not uniform. Eventually, UTC noon and astronomical noon at Greenwich get out of sync.
When the mismatch becomes greater than 0.9 atomic seconds, a “leap second” is added to (or removed from) the end of a designated UTC day—normally either June 30 or December 31.
The variations in the earth’s rotation that cause leap seconds to be needed are not predictable.
UT1
UTC

## Slide 8: Leapseconds (+ and -)
“Normal” sequence of UTC time tags
  1998 Dec 31 23:59:58.0
  1998 Dec 31 23:59:59.0
  1999 Jan 01 00:00:00.0
  1999 Jan 01 00:00:01.0
Sequence with a Positive Leapsecond
  1998 Dec 31 23:59:58.0
  1998 Dec 31 23:59:59.0
  1998 Dec 31 23:59:60.0
  1999 Jan 01 00:00:00.0
  1999 Jan 01 00:00:01.0
Sequence with a Negative Leapsecond
  1998 Dec 31 23:59:57.0
  1998 Dec 31 23:59:58.0
  1999 Jan 01 00:00:00.0
  1999 Jan 01 00:00:01.0
Leap seconds complicate the task of
finding the duration between two
UTC epochs:
You need to know when past leap seconds occurred to compute durations defined by pairs of past UTC epochs.
Durations defined by pairs of future UTC epochs are indeterminate if leap seconds could occur in the interim.

## Slide 9: Barycentric Dynamical Time
Barycentric Dynamical Time (TDB) and Ephemeris Time (ET) are synonyms in SPICE documentation.
TDB is
  Mathematical Ideal used in the equations of motion.
  Used as the independent time variable for many SPICE subroutine interfaces.
  Related to ideal Time at the Solar System Barycenter (TCB) by a scale factor, so that TDB advances on average at the same rate as TAI.

## Slide 10: Terrestrial Dynamical Time
Terrestrial Dynamical Time (TDT)
  IAU has adopted the name “Terrestrial Time” (TT)
    But called TDT throughout SPICE documentation
  Ideal Time (proper time) on Earth at sea level
  TDT = TAI + 32.184 seconds
TDB and TDT have same reference epoch (approximately 1 Jan 2000, 12:00:00 at Greenwich England)
TDB and TDT advance at different rates.
  Variations are small ~ 1.6 milliseconds
  Variations are periodic with a period of 1 sidereal year (to first order)
  Variations are due to relativistic effects
    TDB = TDT + 0.001657 sin( E + 0.01671sin(E) )
Use of TDT in the SPICE system is quite limited.
  SCLK kernels
  Duration computations involving UTC

## Slide 11: Spacecraft Clocks
Spacecraft have onboard clocks to control scheduling of observations, maneuvers, attitude adjustments, etc.
Used to time stamp data
Fundamental unit of time is the “tick”
  Smallest increment possible for spacecraft clock
Spacecraft clock time is a count of ticks since some reference tick.
The duration of the tick drifts with respect to other time systems.

## Slide 12: More about Spacecraft Clocks
SCLK string formats vary from one spacecraft clock to the next.
  Cassini: Maximum reading for partition 1 = 1/4294967295.255
    Partition number: 1
    Seconds: 4294967295
    Ticks (for Cassini, unit = 1/256 second): 255
  Galileo: Maximum reading for partition 1 = 1/16777215:90:09:07
    Partition number: 1
    "RIM" count (unit = 60 2/3 seconds): 16777215
    "Mod 91" count (unit = 2/3 second): 90
    "RTI" count (unit = 1/15 second): 9
    "Mod 8" count (unit = 1/120 second): 7
Format of spacecraft clock and relationship between tick count and other time systems (usually UTC) is captured in a SPICE SCLK kernel
  Pronounced “ess-clock”
    sometimes the more vulgar “sclock” pronunciation is used

## Slide 13: Reference Frames: Definition
A reference frame is an ordered set of three mutually orthogonal (possibly time dependent) unit-length direction vectors, coupled with a location called the frame’s “center” or “origin.”
  SPICE documentation frequently uses the shorthand “frame.”
  A reference frame is also called a “basis,” but SPICE documentation very rarely uses this term.

## Slide 14: Reference Frame Center
A frame’s center is an ephemeris object whose location is coincident with the origin (0, 0, 0) of a reference frame.
  The center of the IAU_<body> frame is <body>.
  The center of any inertial frame is (in SPICE) the solar system barycenter.
    Even for frames naturally associated with accelerated bodies, such as MARSIAU.
A frame’s center plays little role in specification of states
  Origin cancels out when doing vector arithmetic
    Whether positions of objects A and B are specified relative to centers C1 or C2 makes no difference:
    (A – C1) – ( B – C1 ) = ( A – C2 ) – ( B – C2 ) = A – B
  But the center *is* used in computing light time to centers of non-inertial frames
    When the aberration-corrected state of Titan as seen from the Cassini orbiter is computed in the body-fixed IAU_Titan frame, light time is computed from Titan’s center to the Cassini orbiter, and this light time is used to correct both the state and orientation of Titan.

## Slide 15: Types of Reference Frames
Inertial
  Non-rotating
    With respect to fixed stars
  Non-accelerating origin
    Velocity is typically non-zero; acceleration is negligible
  Examples:
    J2000, B1950
Non-Inertial
  Examples
    Body-fixed
      Centered at body center
      Topocentric
    Instrument
    Dynamic frames
      For example, frames defined by time-dependent vectors

## Slide 16: Frames Defined by Dynamics
Mean Equator
  Model gives mean direction of north pole of earth accounting for precession
  Defines z-axis of frame
  Defines a mean plane of equator
Mean Ecliptic
  Model gives mean direction of the “pole” of the earth's orbit
  Defines a mean plane of the ecliptic
Intersection of planes at a particular epoch determines x-axis
Ecliptic Plane

## Slide 17: J2000 Frame

## Slide 18: Rotating Frames
Rotating frames rotate with respect to Inertial Frames. Directions of axes are not constant w.r.t. inertial frames
Centers may accelerate
Examples:
  Body-fixed frames are tied to the surface of a body and rotate with it.
  Spacecraft-fixed frames are defined by the time-varying orientation of a spacecraft

## Slide 19: IAU Bodyfixed Frames
Defined with simple models for position of spin axis and motion of prime meridian
Z-axis points to the “north” side of the invariable plane of the solar system
Invariable plane is perpendicular to the angular momentum vector of the solar system
IAU = International Astronomical Union

## Slide 20: Topocentric Frames
Topocentric frames are attached to a surface
Z-axis is parallel to the gravity gradient or orthogonal to reference spheroid
x points North
z points “up”
y points West
Azimuth (increases
in clockwise direction, measured
from +x axis)
Elevation (angle between
vector and x-y plane)
One example of a topocentric frame. There are other types of topocentric frames: for example, the z-axis could point down, the x-axis North, and the y-axis East.
Position Vector
Orthogonal projection of vector onto x-y plane

## Slide 21: Spacecraft and Instrument Frames
Defined relative to structures
  Spacecraft
  Scan platform
  Instrument
    For example you might have:
      z-axis lies along instrument boresight
      x and y axes defined by instrument characteristics

## Slide 22: State Vectors
The state of an object is its position and velocity relative to a second object
  In SPICE, these objects are often referred to as “target” and “observer” or “center”
  E.g. Saturn relative to Saturn barycenter; Titan relative to Huygens probe
In the SPK subsystem a state is a six dimensional vector
  First three components are Cartesian position: x, y, z
  Second three components are Cartesian velocity: dx/dt, dy/dt, dz/dt
  Units are km, km/sec
A state is specified relative to a reference frame

## Slide 23: Transforming States
To perform algebraic operations on states they must be in the same frame.
Position-only frame transformations require only a rotation* matrix given as a function of time.
    PB (t) = RA to B(t) PA(t)
Position and velocity frame transformations require that we differentiate the above equation
    dPB (t) /dt = dRA to B(t)/dt PA(t) + RA to B(t) d PA(t)/dt
We can use a 6x6 matrix to combine these two transformations into a single equation
* Assuming both frames are right-handed

## Slide 24: Transforming States
SB(t) = TA to B(t)SA(t)
where
Si(t) =
and
TA to B(t) =
Pi(t)
dPi(t)/dt i = A or B
(
RA to B(t)
dRA to B(t)/dt
RA to B(t)
0
(
)
)
The SPICELIB routines SXFORM and PXFORM return state transformation and position transformation matrices respectively.

## Slide 25: Coordinate Systems
Planetocentric
  Latitude: measured from X-Y plane
  Longitude: increases counterclockwise w.r.t. the +Z axis
    +Z points to the north side of the invariable plane
  Radius: measured from center of object
Planetographic, Geodetic, Planetodetic
  Tied to a reference surface
  Latitude: for a point on a reference ellipsoid, angle measured from X-Y plane to the isurface normal at the point of interest. For other points, equals latitude at the nearest point on the reference ellipsoid.
  Longitude
    -odetic: same as for planetocentric
    -ographic: longitude of sub-observer point, for a distant, fixed observer in the J2000 frame, increases with time
  Height above reference surface

## Slide 26: Aberration Corrections: Introduction
Within the SPICE system, “aberration corrections” are adjustments made to state vectors and time-dependent reference frames to accurately reflect the apparent–as opposed to the actual–state and attitude of a target object as seen from a specified observer at a specified time.
  Actual, uncorrected states from an ephemeris are called “geometric” states.
  When computing state vectors, SPICE users may request geometric or aberration-corrected states.
Aberration corrections are needed to accurately answer questions such as:
  In which direction must a remote sensing instrument be pointed to observe a target of interest?
  For a given pointing direction and observation time, what target body surface location would be observed by a remote sensing instrument?
  In which direction must an antenna be pointed to transmit a signal to a specified target?

## Slide 27: Example: Predicted vs Actual Photo
We compare the predicted appearance of a photograph from an optical camera against the actual photograph. We show three predictions derived using different aberration corrections: NONE, LT ("light time only"), and LT+S ("light time plus stellar aberration").
For each prediction, we use red overlays to indicate the expected location in the photo of the images of an extended target body (for example, a natural satellite), of features on the surface of the target body, and of a star.
NONE
Predicted images using uncorrected target position and orientation and uncorrected star direction vector
LT
Predicted images using light time-corrected target position and orientation and uncorrected star direction vector
LT+S
Predicted images using light time and stellar aberration-corrected target position, light time-corrected target orientation, and stellar aberration-corrected star direction vector

## Slide 28: Prediction Without Corrections
Predicted target body, surface feature, and star image locations (in red)
Actual image
Using geometric target positions, target images in photos or other remote-sensing observations don’t appear at their predicted locations.
Actual image

## Slide 29: Light Time Corrections
Observer’s position at time ET
Target’s (geometric) position and orientation at time ET
Target’s position and orientation at time ET-LT (light time corrected position and orientation)
Light travels this path in LT seconds
At time ET, the observer’s camera records photons emitted from the target at time ET-LT, where LT is the one-way light time. The camera "sees" the target's position and orientation at ET-LT.
Note: The angular separation of the geometric and light time corrected positions as seen by the observer has been exaggerated for readability.
Target’s angular velocity vector
Target’s velocity vector

## Slide 30: Prediction Using Light Time Corrections
Using the light time corrected target position and orientation, the predicted locations in the photo of the target image and surface features have changed, but the accuracy of the prediction may still be poor.
Predicted target body, surface feature, and star image locations (in red)
Actual image
Actual image

## Slide 31: Stellar Aberration Correction
Observer’s position at time ET
To the observer, light appears to travel this path
At time ET, the observer’s camera records photons emitted from the target at time ET-LT, where LT is the one-way light time.
The vector from the observer at ET to the location of the target at ET-LT is displaced by a physical phenomenon called stellar aberration. The displaced vector yields the apparent position of the target.
Target’s apparent position and orientation
Observer’s velocity relative to SSB
Note: The angular separation of the geometric, light time corrected, and apparent positions as seen by the observer has been exaggerated for readability.
Target’s (geometric) position and orientation at time ET
Target’s position and orientation at time ET-LT (light time corrected position and orientation)

## Slide 32: Prediction Using "LT+S" Corrections
Predicted target body, surface feature, and star image locations (in red)
Using the light time and stellar aberration-corrected target position, light time-corrected target orientation, and stellar aberration-corrected star direction, we obtain a significantly improved image location predictions.
Remaining prediction errors may be due to, among other causes, pointing error, spacecraft and target ephemeris errors, and timing errors.
Actual image
Actual image

## Slide 33: Effect of Aberration Corrections - 1
Angular offsets between corrected and uncorrected position vectors over the time span 2004 Jan 1--2005 Jan1
  Mars as seen from MEX:
    LT+S vs NONE: .0002 to .0008 degrees
    LT vs NONE: .0006 to .0047 degrees
  Earth as seen from MEX:
    LT+S vs NONE: .0035 to .0106 degrees
    LT vs NONE: .0000 to .0057 degrees
  MEX as seen from Earth:
    LT+S vs NONE: .0035 to .0104 degrees
    LT vs NONE: .0033 to .0048 degrees
  Sun as seen from Mars:
    LT+S vs NONE: .0042 to .0047 degrees
    LT vs NONE: .0000 to .0000 degrees

## Slide 34: Effect of Aberration Corrections - 2
Angular offsets between corrected and uncorrected position vectors over the time span 2004 Jan 1--2008 Jan1
  Saturn as seen from CASSINI:
    LT+S vs NONE: .0000 to .0058 degrees
    LT vs NONE: .0001 to .0019 degrees
  Titan as seen from CASSINI:
    LT+S vs NONE: .0000 to .0057 degrees
    LT vs NONE: .0000 to .0030 degrees
  Earth as seen from CASSINI:
    LT+S vs NONE: .0000 to .0107 degrees
    LT vs NONE: .0000 to .0058 degrees
  CASSINI as seen from Earth:
    LT+S vs NONE: .0000 to .0107 degrees
    LT vs NONE: .0000 to .0059 degrees
  Sun as seen from CASSINI:
    LT+S vs NONE: .0000 to .0059 degrees
    LT vs NONE: .0000 to .0000 degrees