## Slide 1: Instrument Kernel IK
April 2012

## Slide 2: What is an IK?
An Instrument Kernel (IK) is a text file that includes information about a spacecraft’s instruments.
Always includes
  Field-of-view (FOV) information
    Shape
    Orientation
    Size
Sometimes includes
  Timing parameters
  Calibration data
Boresight
Instrument
focal point
X
Y
Z

## Slide 3: Field of View - Visibility
Cassini’s narrow angle camera took this picture.
Which of Saturn’s moons are in the picture?
  Use GFTFOV (or FOVTRG) to find which targets are in the camera’s field of view.
  Only works because the camera’s FOV is defined in an instrument kernel.
  Result: There are 7 moons in this picture!
    Enceladus, Janus, Epimetheus, Atlas, Pan, Daphnis, and Anthe
Notes: Figure from PDS Image Node.

## Slide 4: IK Structure
KPL/IK
ISS Instrument Kernel
=========================
This instrument kernel (I-kernel) contains references
to the mounting alignment, internal and FOV geometry
for the Cassini Imaging Science Subsystem (ISS) instruments.
. . .
Narrow Angle Camera (NAC):
\begindata
INS-82360_FOV_FRAME = 'CASSINI_ISS_NAC'
INS-82360_FOV_SHAPE = 'RECTANGLE'
INS-82360_BORESIGHT = (
0.0000000000000000 0.0000000000000000 +1.0000000000000000
)
INS-82360_FOV_CLASS_SPEC = 'ANGLES'
INS-82360_FOV_REF_VECTOR = (
+1.0000000000000000 0.0000000000000000 0.0000000000000000
)
INS-82360_FOV_REF_ANGLE = ( 0.175 )
INS-82360_FOV_CROSS_ANGLE = ( 0.175 )
INS-82360_FOV_ANGLE_UNITS = 'DEGREES'
\begintext
. . .
Tells SPICE this text file is an IK
Tells SPICE where the data are
Write A LOT of comments!
Include instrument data
  Keyword = value
  Format
    INS#_KEYWORD

## Slide 5: Circular Field of View
Boundary Corner Vector
Boresight
Instrument
focal point
X
Y
Z
(0,0,0)
Ref
Basic Definition
  Shape
  Frame
  Boresight
Option 1: Vectors
  Boundary corner vector
    One vector for a circular FOV
Option 2: Angles
  Angle
    Ref angle value
      One angle for a circular FOV
    Units
  Reference vector

## Slide 6: Elliptical Field of View
Basic Definition
  Shape
  Frame
  Boresight
Option 1: Vectors
  Boundary corner vectors
    Two vectors for an elliptical FOV
Option 2: Angles
  Angle
    Reference Angle
    Cross Angle
    Units
  Reference vector
Boundary Corner Vectors
Boresight
Instrument
focal point
X
Y
Z
(0,0,0)
Ref
Cross

## Slide 7: Rectangular Field of View
Basic Definition
  Shape
  Frame
  Boresight
Option 1: Vectors
  Boundary corner vectors
    Four vectors for a rectangular FOV
Option 2: Angles
  Angle
    Reference Angle
    Cross Angle
    Units
  Reference vector
Boresight
Instrument
focal point
X
Y
Z
Boundary Corner Vectors
X
Z
Boresight
Cross
Top View
Side View
Y
Z
Boresight
Ref

## Slide 8: Polygonal Field of View
FOV Definition
  Shape
  Frame
  Boresight
  Boundary corner vectors
Boundary Corner Vectors
Boresight
Instrument
focal point
X
Y
Z

## Slide 9: Field of View Utility
Optiks shows information about each instrument’s field of view from instrument and frames kernels (IKs and FKs)
  Shape
    Rectangular
    Elliptical
    Circular
    Polygonal
  Boresight
Download Optiks
  NAIF Website
Notes: FOV image from: http://codinghorror.typepad.com/.a/6a0120a85dcdae970b0120a86d9495970b-pi

## Slide 10: IK Examples – NAIF Website
Visit the NAIF website for examples of real mission IKs:
http://naif.jpl.nasa.gov/naif/data.html

## Slide 11: More IK Resources
Documentation of GETFOV routine
  http://naif.jpl.nasa.gov/pub/naif/toolkit_docs/FORTRAN/spicelib/getfov.html
Optiks User’s Guide
  ftp://naif.jpl.nasa.gov/pub/naif/utilities/MacIntel_OSX_64bit/optiks.ug
NAIF IDs Required Reading
  http://naif.jpl.nasa.gov/pub/naif/toolkit_docs/FORTRAN/req/naif_ids.html#Instruments
Kernel Required Reading
  http://naif.jpl.nasa.gov/pub/naif/toolkit_docs/FORTRAN/req/kernel.html
NAIF IDs Tutorial
  ftp://naif.jpl.nasa.gov/pub/naif/toolkit_docs/Tutorials/pdf/individual_docs/07_naif_ids.pdf
Frames Required Reading
  http://naif.jpl.nasa.gov/pub/naif/toolkit_docs/FORTRAN/req/frames.html

## Slide 12: Backup

## Slide 13: Using an IK
Ways to Use an IK | SPICE Function
Use IK information in a program | FURNSH
Get field-of-view information | GETFOV
Find whether a target or direction vector is within the field-of-view of an instrument | GFTFOV GFRFOV FOVTRG FOVRAY
Get data from the IK (double precision, integer, or character) | GDPOOL GIPOOL GCPOOL