## Slide 1: Non-Toolkit Applications
April 2012

## Slide 2: Location of Utilities and Documentation
Download utilities and documentation from the NAIF Website

## Slide 3: Make Slow-Moving SPKs and FKs
PinPoint creates files for objects with fixed or slowly changing positions with respect to another object.
Creates:
  SPK (position and velocity ephemeris)
  Topocentric FK frames kernels
Applications:
  Ground stations
  Landing sites
  Sites along a rover’s path
Coming soon:
  Constant velocity routines in SPICE
Notes: DSN picture from: http://deepspace.jpl.nasa.gov/dsn/gallery/images/goldstone3.jpg

## Slide 4: View SPKs
Spy is used to validate, inspect, and analyze SPK (position, velocity ephemeris) files.
  View contents of an SPK file
    Data
    Summary
    Comments
  Sample data
    Position, distance, velocity, speed, acceleration, etc.
  Check SPK files
    Validate the structure of an SPK
    Locate invalid double precision numbers
    Check for boundary violations
  Find geometric events
    Observer  target distance
    Target elevation
Notes: Trajectory picture: http://www.cbsnews.com/network/news/space/pictures/juno/juno_orbit.jpg and http://www.nasa.gov/images/content/575571main_Juno20110727-3-43_946-710.jpg

## Slide 5: Make Simple CKs
prediCkt makes CK (orientation, attitude) files for objects with orientations that can be described with simple geometry.
  Point at the Sun
  Point at the Earth
  30 degrees away from the Sun in a certain direction
  Nadir direction
More information: Making a CK file tutorial
Notes: Picture from: http://ars.sciencedirect.com/content/image/1-s2.0-S0273117712001068-gr1.jpg

## Slide 6: CK Slicer
CkSlicer reduces a CK file to a shorter interval of time.
Applications:
  If a small time interval of the CK file is needed and the CK file is very large.
  If you need to merge CKs from different sources that have too much overlap.
Time
Original CK Coverage
CK Coverage after CkSlicer
Notes: CkSlicer graphic made by Sam Krening.

## Slide 7: Fill in Gaps Between CK Segments
CKsMrg fills in gaps between multiple CK segments
  Used for CKs from the same data stream
    Daily CKs created from downlinked telemetry
  Don’t use on CKs from multiple data streams
    Reconstructed and predicted
Can make a CK smaller by down sampling
Original CK: 3 segments
CK after CKsMrg:
1 segment
Time
S1
S2
S3
Notes: CKsMrg graphic made by Sam Krening.

## Slide 8: Fill in CK Segment Gaps
CkSpanIt fills in gaps within segments in a Type 3 CK file
  Changes the interpolation intervals that used a small tolerance in the original CK file
  Account for telemetry dropouts
CkSpanIt converts CKs to different SPICE formats
  From Type 1 to Type 3
  From Type 1 to Type 2
  From Type 3 to Type 2
Time
Original CK Segment with Gaps
Modified CK Segment after CkSpanIt
Notes: CkSpanIt graphic made by Sam Krening

## Slide 9: Orbit Number
OrbNum calculates the:
  Orbit number
    Apoapse, periapse, descending or ascending node
  Start and Stop times of the orbit
Can calculate more information at the start of each orbit
  Latitude and longitude of surface point closest to the spacecraft
  Sub-solar latitude and longitude
  Altitude of spacecraft
  Distance to Sun
  Keplerian orbital elements
Notes: Orbit picture from: http://sci.esa.int/science-e-media/img/10/orbtis410.jpg

## Slide 10: Field of View
Optiks shows information about each instrument’s field of view from instrument and frames kernels (IKs and FKs)
  Shape
    Rectangular
    Elliptical
    Circular
    Polygonal
  Boresight
Notes: FOV image from: http://codinghorror.typepad.com/.a/6a0120a85dcdae970b0120a86d9495970b-pi

## Slide 11: Join Binary DAF Files
DafCat concatenates (joins) binary DAF files
  SPKs, CKs, binary PCKs
  We recommend using SpkMerge for merging SPKs
New DAF file after DafCat
DAF 1
DAF 2

## Slide 12: Replace IDs
DafMod alters IDs in binary SPK, CK, or PCK files.
  Can modify:
    Target, center, or reference frame ID in an SPK
    Object or reference frame ID in a CK or PCK
  Applications
    Create simulation spacecraft
    Compare two trajectories for the same object in one program
BSpIdMod modifies the object IDs in a binary SPK file
  Less powerful version of DafMod.
DAF File before DafMod
Information
Object: -41
More information…
DAF File after DafMod
Information
Object: -123456
More information…

## Slide 13: Make SCLK Kernel
MakClk makes a spacecraft clock (SCLK) kernel from a SCLKSCET file.
  A SCLKSCET file is a time correlation file used by most JPL missions
    Contains information needed to make an SCLK kernel

## Slide 14: More Utilities – File Formats
BFF - Binary File Format
  BFF displays the binary file format of a SPICE kernel
    BIG-IEEE
    LTL-IEEE
Bingo – Converts files between formats
  IEEE big endian  IEEE little endian
  DOS  UNIX
ArchType - file architecture and type of a SPICE kernel
  Architectures
    DAF, DAS, KPL
  Types
    SPK, PCK, IK, CK, LSK, FK
  Useful for scripts that need to identify SPICE kernels
Notes: UNIX picture from: http://www.unix.org/
DOS picture from:

## Slide 15: backup

## Slide 16: PinPoint Example
Terminal Window
$ more mer1_meridiani.def
Sample PINPOINT input for MER-1 landing site coordinates.
\begindata
SITES = ( 'LS' )
LS_CENTER = 499
LS_FRAME = 'IAU_MARS'
LS_IDCODE = -253900
LS_XYZ = ( +3.3764222E+03 -3.2664876E+02 -1.1539218E+02 )
LS_BOUNDS = ( @2001-01-01-00:00:00.000, @2100-01-01-00:00:00.000 )
\begintext
$ pinpoint -def mer1_meridiani.def -spk mer1_meridiani.bsp
$ brief mer1_meridiani.bsp
Brief. Version: 2.2.0 (SPICE Toolkit N0057)
Summary for: mer1_meridiani.bsp
Body: -253900* w.r.t. MARS (499)
Start of Interval (ET) End of Interval (ET)
-------------------------------- --------------------------------
2001 JAN 01 00:00:00.000 2100 JAN 01 00:00:00.000